LAKES OIL N.L.

A.C.N. (004 247 214)

Patrobus No.1		PEP 155 (east)

DAILY GEOLOGICAL REPORT No. 14	Date: 06 Oct 05

Depth: 252m		Progress: 20m		Days from Spud: 30

Rig:			Drilltec		GL(ASL):		31.55m

Drilling Rep:	Tim O’Brien	RT (AGL):		0.80m

Geologist:		Ingrid Campbell	Last Casing:         115mm at 232m

Comments: Core out cement track and cut 20m of continuous conventional core.

| Interval (mRT) | Hydrocarbon Show Summary | Gas |
| --- | --- | --- |
| 232-252 | No oil flourescence | Nil |

| Formation Tops: | Prognosed (mGL) | Actual٭ (mGL) | Actual٭ (mSS) | Difference٭ (High/Low) |
| --- | --- | --- | --- | --- |
| Pleistocene dune deposit | Absent | Surface | +31.55 | - |
| Haunted Hills Gravel | Surface | 34.45 | -2.9 | 34.45 Low |
| Jemmy’s Point Formation | 15 | 45 | -13.45 | 30 Low |
| Gippsland Limestone | 50 | 120 | -88.45 | 70 Low |
| Lakes Entrance Formation | 190 | 226 | -194.45 | 36 Low |
| Colquhuon Gravels | 360 |  |  |  |
| Granite Basement | 400 |  |  |  |
| Total Depth | 600 |  |  |  |

٭Provisional, based on mudlog

LAKES OIL N.L.

A.C.N. (004 247 214)

Patrobus No.1		PEP 155 (east)

DAILY GEOLOGICAL REPORT No. 14

Lithological and Fluorescence Description

| Interval (m) | Description |
| --- | --- |
| 232-243.05m | LAKES ENTRANCE FORMATION Fine Sandy Marlstone (80%) interbedded with Sandy Limestone (20%) FINE SANDY MARLSTONE: medium grey-medium greenish grey, moderately sorted, subangular-subrounded, fine-very fine, abundant subangular-subrounded fine-very fine translucent-opaque quartz, common well rounded dark green glauconite nodules, trace-common calcareous fossils, medium blue-grey claystone matrix, matrix supported, weakly to strongly calcareous, weak limonite cement, moderately consolidated, soft, poor to fair visual porosity, no oil fluorescence. SANDY LIMESTONE: very light grey-pale yellow grey, fine-medium, moderately sorted subrounded-rounded, abundant subrounded-rounded fine-medium, translucent-opaque quartz grains with common iron-oxide cement, common fine, rounded-well rounded dark green glauconite, common calcareous fossils, occasional extremely thin calcite bands, brown silty matrix, strong calcareous cement, hard, good vuggy porosity, no oil fluorescence. |
| 243.05-246.42m | LAKES ENTRANCE FORMATION Fine Sandy Marlstone (100%) FINE SANDY MARLSTONE: medium greenish grey-medium green, fine-very fine rounded-well rounded, dominantly well sorted, well rounded, fine, translucent-opaque quartz with common iron oxide staining, rare very fine, subrounded-well rounded glauconitic nodules, trace calcareous fossils, brown marly matrix, moderately consolidated, weakly calcareous, soft, poor-fair visual porosity, no oil flourescence. |
| 246.42-252m | LAKES ENTRANCE FORMATION Fine Sandy Marlstone (70%) interbedded with Sandy Limestone (30%) FINE SANDY MARLSTONE: medium greenish grey-medium green, fine-very fine rounded-well rounded, dominantly well sorted, well rounded, fine, translucent-opaque quartz with common iron oxide staining, rare very fine, subrounded-well rounded glauconitic nodules, trace calcareous fossils, brown marly matrix, moderately consolidated, weakly calcareous, soft, poor-fair visual porosity, no oil flourescence. SANDY LIMESTONE: very light grey-light greenish grey, fine-very fine, moderately sorted, subangular-subrounded, common calcareous fossils, large shell fossils, common rounded-well rounded, dominantly well sorted, well rounded, fine, translucent-opaque quartz with common iron oxide staining, strong calcite cement, hard, good visual vuggy porosity, no oil fluorescence. |

LAKES OIL N.L.					CORE REPORT No. 1

WELL NAME: 	Patrobus No.1		DATE: 06 OCT 05

| INTERVAL CORED | 232-234m |  |
| --- | --- | --- |
| CUT: 2m | RECOVERED: 1.3m | RECOVERY: 65% |
| GEOLOGIST: | Ingrid Campbell |  |

GENERALIZED LITHOLOGY OF INTERVAL:

Fine Sandy Marlstone (80%) With Sandy Limestone beds (20%)

Sedimentary bedding at 0 degrees. Limestone bands at 233.45m-233.55m and 234.8m-235m. Generally sedimentary structurally amorphous, apart from limestone beds.

| POROSITY | Poor |
| --- | --- |
| FLOURESCENCE | No oil fluorescence. Rare dull yellow mineral flourescence |
| CUT | Nil |
| STAIN | Nil |

DESCRIPTION:

232.0-232.7m No Recovery 232.7-234.8m except 233.45-233.55m Fine Sandy Marlstone (100%). FINE SANDY MARLSTONE: medium grey-medium greenish grey, moderately sorted, subangular-subrounded, fine-very fine, abundant subangular-subrounded fine-very fine translucent-opaque quartz, common well rounded dark green glauconite nodules, common calcareous fossils, medium blue-grey claystone matrix, matrix supported, calcareous, weak limonite cement, poor visual porosity, no oil fluorescence. 233.45-233.55m and 234.8-235m Sandy Limestone (100%) SANDY LIMESTONE: very light grey-light greenish grey, moderately sorted, subangular-subrounded, fine-medium, abundant calcareous fossils, shells, gastropods, bryozoan, common subangular-subrounded fine-medium translucent-opaque quartz, medium blue-grey claystone matrix, matrix supported, strong calcareous cement, poor visual porosity, no oil fluorescence.

REMARKS:

The fine sandy marlstone and sandstone appear to contain a similar composition, however the sandstone contains a higher proportion of calcareous fossils and consequently contains a stronger calcite cement.

LAKES OIL N.L.				CORE REPORT No. 2

WELL NAME: 	Patrobus No.1		DATE: 06 OCT 05

| INTERVAL CORED | 234-237m |  |
| --- | --- | --- |
| CUT: 3m | RECOVERED: 1.6m | RECOVERY: 53% |
| GEOLOGIST: | Ingrid Campbell |  |

GENERALIZED LITHOLOGY OF INTERVAL:

Sandy Limestone (80%) with beds of Fine Sandy Marlstone (20%)

Sedimentary bedding at 0 degrees. Minor calcite fractures at 10 to 20 degrees within the sandy limestone beds. Generally sedimentary structurally amorphous apart from sandy limestone/fine sandy marlstone contacts.

| POROSITY | Poor |
| --- | --- |
| FLOURESCENCE | No oil fluorescence. Rare dull yellow mineral flourescence |
| CUT | Nil |
| STAIN | Nil |

DESCRIPTION:

234.0-234.8m Sandy Limestone (100%) SANDY LIMESTONE: very light grey-pale yellow grey, fine-medium, moderately sorted subrounded-rounded, abundant subrounded-rounded fine-medium, translucent-opaque quartz grains with common iron-oxide cement, common fine, rounded-well rounded dark green glauconite, common calcareous fossils, occasional extremely thin calcite bands, brown silty matrix, strong calcareous cement, hard, good vuggy porosity, no oil fluorescence. 234.8-235.15m Fine Sandy Marlstone (100%) FINE SANDY MARLSTONE: medium grey-medium greenish grey, moderately sorted, subangular-subrounded, fine-very fine, abundant subangular-subrounded fine-very fine translucent-opaque quartz, common well rounded dark green glauconite nodules, common calcareous fossils, medium blue-grey claystone matrix, matrix supported, calcareous, weak limonite cement, poor visual porosity, no oil fluorescence. 235.15-235.4m Sandy Limestone (100%) SANDY LIMESTONE: very light grey-pale yellow grey, fine-medium, moderately sorted subrounded-rounded, abundant subrounded-rounded fine-medium, translucent-opaque quartz grains with common iron-oxide cement, common fine, rounded-well rounded dark green glauconite, common calcareous fossils, occasional extremely thin calcite bands, brown silty matrix, strong calcareous cement, hard, good vuggy porosity, no oil fluorescence. 235.4-237m No Recovery.

REMARKS:

LAKES OIL N.L.					CORE REPORT No. 3

WELL NAME: 	Patrobus No.1		DATE: 06 OCT 05

| INTERVAL CORED | 237-240m |  |
| --- | --- | --- |
| CUT: 3m | RECOVERED: 1.4m | RECOVERY: 46% |
| GEOLOGIST: | Ingrid Campbell |  |

GENERALIZED LITHOLOGY OF INTERVAL:

Fine Sandy Marlstone (100%)

No definable sedimentary bedding. Generally sedimentary structurally amorphous.

| POROSITY | Poor |
| --- | --- |
| FLOURESCENCE | No oil fluorescence. Rare dull yellow mineral flourescence |
| CUT | Nil |
| STAIN | Nil |

DESCRIPTION:

237-238.6m No Recovery. 238.6-240.0m Fine Sandy Marlstone (100%) FINE SANDY MARLSTONE: uniform medium grey-medium greenish grey, moderately sorted, subangular-subrounded, fine-very fine, abundant subangular-subrounded fine-very fine translucent-opaque quartz, abundant well rounded dark green glauconite nodules, rare calcareous fossils, medium blue-grey claystone matrix, matrix supported, calcareous, poor visual porosity, no oil fluorescence.

REMARKS:

Due to poor recovery in interval No.2, core 3 was run with no splits. Initially there was no recovery, and the splits were replaced for core No.4. Subsequently when core No.4 was cut 1.4m of Core No. 3 was recovered.

LAKES OIL N.L.					CORE REPORT No. 4

WELL NAME: 	Patrobus No.1		DATE: 06 OCT 05

| INTERVAL CORED | 240-241.7m |  |
| --- | --- | --- |
| CUT: 1.7m | RECOVERED: 1.7m | RECOVERY: 100% |
| GEOLOGIST: | Ingrid Campbell |  |

GENERALIZED LITHOLOGY OF INTERVAL:

Fine Sandy Marlstone (100%)

Sedimentary bedding at 0 degrees. Generally sedimentary structurally amorphous. Minor shelly band with coaly material

| POROSITY | Poor |
| --- | --- |
| FLOURESCENCE | No oil fluorescence. Rare dull yellow mineral flourescence |
| CUT | Nil |
| STAIN | Nil |

DESCRIPTION:

240-241.7m Fine Sandy Marlstone (100%) with minor shelly band at 240.33-240.34m FINE SANDY MARLSTONE: dark greenish grey, fine-very fine subangular-subrounded, abundant, fine-very fine subangular-subrounded, translucent-opaque quartz, common very fine, subrounded-well rounded glauconitic nodules, trace calcareous fossils, trace carbonaceous material, dark blue-grey claystone matrix, matrix supported, calcareous, poor visual porosity, no show. SHELLY BAND: light grey-medium grey, fossiliferous, strong calcareous cement, minor carbonaceous material.

REMARKS:

Recovered 1.4m of Core No3.

LAKES OIL N.L.					CORE REPORT No. 5

WELL NAME: 	Patrobus No.1		DATE: 06 OCT 05

| INTERVAL CORED | 241.7-243m |  |
| --- | --- | --- |
| CUT: 1.3m | RECOVERED: 1.3m | RECOVERY: 100% |
| GEOLOGIST: | Ingrid Campbell |  |

GENERALIZED LITHOLOGY OF INTERVAL:

Fine Sandy Marlstone (100%)

Sedimentary bedding at 0 degrees. Generally sedimentary structurally amorphous.

| POROSITY | Poor |
| --- | --- |
| FLOURESCENCE | No oil fluorescence. Rare dull yellow mineral flourescence |
| CUT | Nil |
| STAIN | Nil |

DESCRIPTION:

241.7-243.0m Fine Sandy Marlstone (100%) FINE SANDY MARLSTONE: medium greenish grey-medium green, fine-very fine subangular-subrounded, abundant, fine-very fine subangular-subrounded, translucent-opaque quartz, common very fine, subrounded-well rounded glauconitic nodules, trace calcareous fossils, trace pebbly lithics, dark blue-grey claystone matrix, matrix supported, moderately consolidated, calcareous, non-fissile, poor visual porosity, no oil flourescence.

REMARKS:

LAKES OIL N.L.					CORE REPORT No. 6

WELL NAME: 	Patrobus No.1		DATE: 06 OCT 05

| INTERVAL CORED | 243-246m |  |
| --- | --- | --- |
| CUT: 3m | RECOVERED: 3m | RECOVERY: 100% |
| GEOLOGIST: | Ingrid Campbell |  |

GENERALIZED LITHOLOGY OF INTERVAL:

Fine Sandy Marlstone (98%) with minor Sandy Limestone bed (2%)

Sedimentary bedding at 0 degrees. Generally sedimentary structurally amorphous.

| POROSITY | Poor to fair, good vuggy porosity in the Limestone |
| --- | --- |
| FLOURESCENCE | No oil fluorescence. Rare dull yellow mineral flourescence |
| CUT | Nil |
| STAIN | Nil |

DESCRIPTION:

243.0-243.05m Sandy Limestone (100%) SANDY LIMESTONE: light grey-medium greenish grey, well sorted, subrounded-rounded, fine-medium, abundant fine-medium, subrounded-rounded, translucent-opaque quartz, abundant calcareous fossils, strong calcite cement, hard, good visual vuggy porosity, no oil fluorescence. 243.05-246.0m Fine Sandy Marlstone (100%) FINE SANDY MARLSTONE: medium greenish grey-medium green, fine-very fine rounded-well rounded, dominantly well sorted, well rounded, fine, translucent-opaque quartz with common iron oxide staining, rare very fine, subrounded-well rounded glauconitic nodules, trace calcareous fossils, brown marly matrix, moderately consolidated, weakly calcareous, soft, poor-fair visual porosity, no oil flourescence.

REMARKS:

The quartz grains appear to be well rounded and sorted, the marly matrix appears to be only loosely attached to the sand grains.

LAKES OIL N.L.					CORE REPORT No. 7

WELL NAME: 	Patrobus No.1		DATE: 06 OCT 05

| INTERVAL CORED | 246-249m |  |
| --- | --- | --- |
| CUT: 3m | RECOVERED: 3m | RECOVERY: 100% |
| GEOLOGIST: | Ingrid Campbell |  |

GENERALIZED LITHOLOGY OF INTERVAL:

Fine Sandy Marlstone (95%) interbedded with Sandy Limestone (5%)

Sedimentary bedding at 0 degrees. Major Limestone beds at 246.42-246.46m and 247.97-248.2m. Generally sedimentary structurally amorphous apart from Sandy Limestone beds.

| POROSITY | Poor to fair, good vuggy porosity in the Limestone |
| --- | --- |
| FLOURESCENCE | No oil fluorescence. Rare dull yellow mineral flourescence |
| CUT | Nil |
| STAIN | Nil |

DESCRIPTION:

246.0-246.42m Fine Sandy Marlstone (100%) FINE SANDY MARLSTONE: medium greenish grey-medium green, fine-very fine rounded-well rounded, dominantly well sorted, well rounded, fine, translucent-opaque quartz with common iron oxide staining, rare very fine, subrounded-well rounded glauconitic nodules, trace calcareous fossils, brown marly matrix, moderately consolidated, weakly calcareous, soft, poor-fair visual porosity, no oil flourescence. 246.42-246.46m Sandy Limestone (100%) SANDY LIMESTONE: very light grey-light greenish grey, fine-very fine, moderately sorted, subangular-subrounded, common calcareous fossils, large shell fossils, common rounded-well rounded, dominantly well sorted, well rounded, fine, translucent-opaque quartz with common iron oxide staining, strong calcite cement, good visual vuggy porosity, no oil fluorescence. 246.46-247.97m Fine Sandy Marlstone (100%) FINE SANDY MARLSTONE: medium greenish grey-medium green, fine-very fine rounded-well rounded, dominantly well sorted, well rounded, fine, translucent-opaque quartz with common iron oxide staining, rare very fine, subrounded-well rounded glauconitic nodules, trace calcareous fossils, brown marly matrix, moderately consolidated, weakly calcareous, soft, poor-fair visual porosity, no oil flourescence. 247.97-248.2m Sandy Limestone (100%) SANDY LIMESTONE: very light grey-light greenish grey, fine-very fine, moderately sorted, subangular-subrounded, common calcareous fossils, large shell fossils, common rounded-well rounded, dominantly well sorted, well rounded, fine, translucent-opaque quartz with common iron oxide staining, strong calcite cement, good visual vuggy porosity, no oil fluorescence. 248.2-249.0m Fine Sandy Marlstone (100%) FINE SANDY MARLSTONE: medium greenish grey-medium green, fine-very fine rounded-well rounded, dominantly well sorted, well rounded, fine, translucent-opaque quartz with common iron oxide staining, rare very fine, subrounded-well rounded glauconitic nodules, trace calcareous fossils, brown marly matrix, moderately consolidated, weakly calcareous, soft, poor-fair visual porosity, no oil flourescence.

LAKES OIL N.L.					CORE REPORT No. 8

WELL NAME: 	Patrobus No.1		DATE: 06 OCT 05

| INTERVAL CORED | 249-252m |  |
| --- | --- | --- |
| CUT: 3m | RECOVERED: 2.96m | RECOVERY: 99% |
| GEOLOGIST: | Ingrid Campbell |  |

GENERALIZED LITHOLOGY OF INTERVAL:

Fine Sandy Marlstone (75%) interbedded with Sandy Limestone (25%)

Sedimentary bedding at 0 degrees. Major Limestone bed at 249.47-249.63m Generally sedimentary structurally amorphous apart from Sandy Limestone beds.

| POROSITY | Poor, good vuggy porosity in the Limestone |
| --- | --- |
| FLOURESCENCE | No oil fluorescence. Rare dull yellow mineral flourescence |
| CUT | Nil |
| STAIN | Nil |

DESCRIPTION:

249.0-252.0m except 249.47-249.63m Fine Sandy Marlstone (100%) FINE SANDY MARLSTONE: medium greenish grey-dark greenish grey, fine-very fine, subangular-subrounded, moderately sorted, abundant fine-very fine, subangular-subrounded quartz, trace-common large shelly fossils, light grey-blue grey claystone matrix, matrix supported, calcareous, soft, poor visual porosity, no fluorescence. 249.47-249.63m Fossiliferous Sandy Limestone (100%) FOSSILIFEROUS SANDY LIMESTONE: very light grey-light brown grey, common subangular-subrounded fine-medium quartz, common calcareous fossils, strong calcite cement, hard, good visual vuggy porosity.

REMARKS: