LAKES OIL N.L.

A.C.N. (004 247 214)

Patrobus No.1		PEP 155 (east)

DAILY GEOLOGICAL REPORT No. 15	Date: 07 Oct 05

Depth: 267m		Progress: 15m		Days from Spud: 31

Rig:			Drilltec		GL(ASL):		31.55m

Drilling Rep:	Tim O’Brien	RT (AGL):		0.80m

Geologist:		Ingrid Campbell	Last Casing:         115mm at 232m

Comments: Cut 15m of Continuous Core.

| Interval (mRT) | Hydrocarbon Show Summary | Gas |
| --- | --- | --- |
| 252-267 | No oil flourescence | Nil |

| Formation Tops: | Prognosed (mGL) | Actual٭ (mGL) | Actual٭ (mSS) | Difference٭ (High/Low) |
| --- | --- | --- | --- | --- |
| Pleistocene dune deposit | Absent | Surface | +31.55 | - |
| Haunted Hills Gravel | Surface | 34.45 | -2.9 | 34.45 Low |
| Jemmy’s Point Formation | 15 | 45 | -13.45 | 30 Low |
| Gippsland Limestone | 50 | 120 | -88.45 | 70 Low |
| Lakes Entrance Formation | 190 | 226 | -194.45 | 36 Low |
| Colquhuon Gravels | 360 |  |  |  |
| Granite Basement | 400 |  |  |  |
| Total Depth | 600 |  |  |  |

٭Provisional, based on mudlog

LAKES OIL N.L.

A.C.N. (004 247 214)

Patrobus No.1		PEP 155 (east)

DAILY GEOLOGICAL REPORT No. 15

Lithological and Fluorescence Description

| Interval (m) | Description |
| --- | --- |
| 252-262.9m | LAKES ENTRANCE FORMATION Fine Sandy Marlstone with occasional coaly bands grading to Fine Marly Sandstone (70%) with bands of Sandy Limestone grading to Calcareous Sandstone (25%) and occasional Unconsolidated Sand (5%) FINE SANDY MARLSTONE: medium greenish grey-dark greenish grey, poorly sorted, subangular-rounded, fine-very fine, abundant subangular-rounded fine-very fine translucent-opaque quartz with common iron oxide staining, common fine black coaly material, white-very light grey claystone matrix, moderately firm, clast supported, weakly calcareous, fair-good visual porosity, no oil fluorescence. COALY BANDS: minor smeared disseminated brown coaly bands, soft, light grey-blue claystone matrix, weakly calcareous, rare calcareous fossils. FINE MARLY SANDSTONE: medium grey-medium greenish grey, moderately sorted, subangular-subrounded, fine-very fine, abundant subangular-rounded fine-very fine translucent-opaque quartz with common iron oxide staining, trace basaltic lithics, rare calcareous fossils, trace carbonaceous material, common greenish grey-light greenish grey silty matrix, moderately consolidated, moderately calcareous, soft, poor-fair visual porosity, no oil fluorescence. SANDY LIMESTONE: very light bluish grey- bluish grey, moderately sorted, subangular-subrounded, fine-very fine, common subangular-rounded fine-very fine translucent-opaque quartz with common iron oxide staining, rare fine black coaly material, no visible matrix, strong calcite cement, hard, moderate visual porosity, no oil fluorescence. CALCAREOUS SANDSTONE: white-very light greenish grey, moderately sorted, fine-very fine, common subangular-rounded fine-very fine translucent-opaque quartz with common iron oxide staining, rare fine black coaly material, trace calcareous fossils, white-pale blue claystone matrix, strong calcareous cement, hard, poor-fair visual porosity, no oil fluorescence. UNCONSOLIDATED SAND: light greenish grey-medium bluish grey, moderately sorted, fine-medium, subangular-rounded, dominant subangular-rounded fine-very fine translucent-opaque quartz with common iron oxide staining, common round-well rounded granitic lithics, trace carbonaceous material, trace brown silty matrix, moderately calcareous, no visible cement, unconsolidated, good-excellent visual porosity, no oil fluorescence. |
| 262.9-267m | LAKES ENTRANCE FORMATION Greensand (90%) with interval of Glauconitic Conglomerate (10%) GREENSAND: medium green, moderately consolidated-consolidated, abundant dark green-brown subrounded-rounded medium-coarse glauconitic nodules, fine-moderately fine clear-opaque quartz, common medium-coarse shell fragments, trace pyrite, calcareous cement, hard, occasional fracture material, poor-moderate visual porosity, no oil fluorescence. GLAUCONTIC CONGLOMERATE: medium green-grey green, coarse-very coarse shelly fragments, mud clasts, lithic fragments, poorly sorted, moderately consolidated. |

LAKES OIL N.L.					CORE REPORT No. 9

WELL NAME: 	Patrobus No.1		DATE: 07 OCT 05

| INTERVAL CORED | 255-258m |  |
| --- | --- | --- |
| CUT: 3m | RECOVERED: 2.53m | RECOVERY: 84% |
| GEOLOGIST: | Ingrid Campbell |  |

GENERALIZED LITHOLOGY OF INTERVAL:

Fine Sandy Marlstone (70%) interbedded with Sandy Limestone (25%) grading to Sandstone (5%).

Sedimentary bedding at 0 degrees. Major Limestone bed grading to sandstone at 252.8-253.0m Major Limestone bed at 253.7-253.83m. Generally sedimentary structurally amorphous apart from Sandy Limestone and Sandstone beds.

| POROSITY | Poor-good visual porosity |
| --- | --- |
| FLOURESCENCE | No oil fluorescence, dull yellow mineral flourescence |
| CUT | Nil. |
| STAIN | Nil. |

DESCRIPTION:

252.0-252.8m Fine Sandy Marlstone (100%) FINE SANDY MARLSTONE: medium greenish grey-dark greenish grey, poorly sorted, subangular-rounded, fine-very fine, abundant subangular-rounded fine-very fine translucent-opaque quartz with common iron oxide staining, common fine black coaly material, white-very light grey claystone matrix, moderately firm, clast supported, weakly calcareous, fair-good visual porosity, no oil fluorescence. 252.8-253.0m Sandy Limestone (100%) grading to Sandstone at base (100%) SANDY LIMESTONE: very light bluish grey- bluish grey, moderately sorted, subangular-subrounded, fine-very fine, common subangular-rounded fine-very fine translucent-opaque quartz with common iron oxide staining, rare fine black coaly material, no visible matrix, strong calcite cement, hard, moderate visual porosity, no oil fluorescence. SANDSTONE: very light bluish grey- bluish grey, moderately sorted, subangular-subrounded, fine-very fine, dominant subangular-rounded fine-very fine translucent-opaque quartz with common iron oxide staining, rare fine black coaly material, very light grey silty matrix, moderately consolidated, moderately calcareous, good visual porosity, no oil fluorescence. 253.0-253.7m Fine Sandy Marlstone (100%) FINE SANDY MARLSTONE: medium greenish grey-dark greenish grey, poorly sorted, subangular-rounded, fine-very fine, abundant subangular-rounded fine-very fine translucent-opaque quartz with common iron oxide staining, common fine black coaly material, white-very light grey claystone matrix, moderately firm, clast supported, weakly calcareous, fair-good visual porosity, no oil fluorescence. 253.7-253.83m Sandy Limestone (100%) SANDY LIMESTONE: very light bluish grey- bluish grey, moderately sorted, subangular-subrounded, fine-very fine, common subangular-rounded fine-very fine translucent-opaque quartz with common iron oxide staining, rare fine black coaly material, no visible matrix, strong calcite cement, hard, moderate visual porosity, no oil fluorescence. 253.83-254.53m Fine Sandy Marlstone (100%) FINE SANDY MARLSTONE: medium greenish grey-dark greenish grey, moderately-well rounded, subangular-rounded, fine-very fine, abundant subangular-rounded fine-very fine translucent-opaque quartz with common iron oxide staining, common fine black coaly material, white-very light grey claystone matrix, moderately firm, clast supported, moderately calcareous, fair-good visual porosity, soft, no oil fluorescence. 254.53-255m No Recovery

REMARKS:

LAKES OIL N.L.				CORE REPORT No. 10

WELL NAME: 	Patrobus No.1		DATE: 07 OCT 05

| INTERVAL CORED | 255-258m |  |
| --- | --- | --- |
| CUT: 3m | RECOVERED: 3.1m | RECOVERY: 103% |
| GEOLOGIST: | Ingrid Campbell |  |

GENERALIZED LITHOLOGY OF INTERVAL:

Fine Sandy Marlstone (80%) with occasional coaly bands interbedded with Sandstone (15%) and Calcareous Sandstone (5%)

Sedimentary bedding at 0 degrees. Sandy granite wash from 257.6-257.9m Generally sedimentary structurally amorphous apart from occasional coaly bands.

| POROSITY | Poor-good visual porosity |
| --- | --- |
| FLOURESCENCE | No oil fluorescence, dull yellow mineral fluorescence |
| CUT | Nil. |
| STAIN | Nil. |

DESCRIPTION:

254.9-257.6m Fine Sandy Marlstone (100%) with minor coaly bands. FINE SANDY MARLSTONE: medium greenish grey-dark greenish grey, moderately-well rounded, subangular-rounded, fine-very fine, abundant subangular-rounded fine-very fine translucent-opaque quartz with common iron oxide staining, common fine black coaly material, trace calcareous fossils, white-very light grey claystone matrix, moderately firm, clast supported, moderately calcareous, fair-good visual porosity, soft, no oil fluorescence. COALY BANDS: minor smeared disseminated brown coaly bands, soft, light grey-blue claystone matrix, weakly calcareous, rare calcareous fossils. 257.6-257.9m Sandstone (100%) SANDSTONE: white-very light greenish grey, moderately sorted fine-very fine subrounded-well sorted, common subangular-rounded fine-very fine translucent-opaque quartz with common iron oxide staining, common white-very light greenish grey rounded-well rounded fine granitic lithics, very light grey-light bluish grey claystone matrix, clast supported, friable, weakly calcareous, no visible cement, poor-fair visual porosity, no oil fluorescence. 257.9-258m Calcareous Sandstone (100%) CALCAREOUS SANDSTONE: white-very light greenish grey, moderately sorted, fine-very fine, common subangular-rounded fine-very fine translucent-opaque quartz with common iron oxide staining, rare fine black coaly material, trace calcareous fossils, white-pale blue claystone matrix, strong calcareous cement, hard, poor-fair visual porosity, faint petroliferous odour, no oil fluorescence.

REMARKS:

Recovered 10cm of Core 9. Faint petroliferous odour noted in the calcareous sandstone.

LAKES OIL N.L.					CORE REPORT No. 11

WELL NAME: 	Patrobus No.1		DATE: 07 OCT 05

| INTERVAL CORED | 258-261m |  |
| --- | --- | --- |
| CUT: 3m | RECOVERED: 2.83m | RECOVERY: 94% |
| GEOLOGIST: | Ingrid Campbell |  |

GENERALIZED LITHOLOGY OF INTERVAL:

Marly Fine Sandstone interbedded with Calcareous Sandstone with occasional Unconsolidated Sand intervals

Sedimentary bedding at 0 degrees. Unconsolidated Sandy Granitic wash 260.50-260.67m Generally sedimentary structurally amorphous except Calcareous Sandstone

| POROSITY | Poor-good visual porosity. |
| --- | --- |
| FLOURESCENCE | No oil fluorescence, dull yellow mineral fluorescence. |
| CUT | Nil. |
| STAIN | Nil. |

DESCRIPTION:

258.0-258.15m Calcareous Sandstone (100%) CALCAREOUS SANDSTONE: white-very light greenish grey, moderately sorted, fine-very fine, common subangular-rounded fine-very fine translucent-opaque quartz with common iron oxide staining, rare fine black coaly material, trace calcareous fossils, white-pale blue claystone matrix, strong calcareous cement, hard, poor-fair visual porosity, faint petroliferous odour, no oil fluorescence. 258.15-258.44m MARLY FINE SANDSTONE: medium grey-medium greenish grey, moderately sorted, subangular-subrounded, fine-very fine, abundant subangular-rounded fine-very fine translucent-opaque quartz with common iron oxide staining, trace basaltic lithics, trace carbonaceous material, common greenish grey-light greenish grey silty matrix, moderately consolidated, moderately calcareous, soft, poor-fair visual porosity, no oil fluorescence. 258.44-259.05m Calcareous Sandstone (100%) CALCAREOUS SANDSTONE: white-very light greenish grey, moderately sorted, fine-very fine, common subangular-rounded fine-very fine translucent-opaque quartz with common iron oxide staining, rare fine black coaly material, trace calcareous fossils, white-pale blue claystone matrix, strong calcareous cement, hard, poor-fair visual porosity, faint petroliferous odour, no oil fluorescence. 259.05-259.65m MARLY FINE SANDSTONE: medium grey-medium greenish grey, moderately sorted, subangular-subrounded, fine-very fine, abundant subangular-rounded fine-very fine translucent-opaque quartz with common iron oxide staining, trace basaltic lithics, trace carbonaceous material, common greenish grey-light greenish grey silty matrix, moderately consolidated, moderately calcareous, soft, poor-fair visual porosity, no oil fluorescence. 259.65-259.82m Calcareous Sandstone (100%) CALCAREOUS SANDSTONE: white-very light greenish grey, moderately sorted, fine-very fine, common subangular-rounded fine-very fine translucent-opaque quartz with common iron oxide staining, rare fine black coaly material, trace calcareous fossils, white-pale blue claystone matrix, strong calcareous cement, hard, poor-fair visual porosity, faint petroliferous odour, no oil fluorescence. 259.82-260.50m MARLY FINE SANDSTONE: medium grey-medium greenish grey, moderately sorted, subangular-subrounded, fine-very fine, abundant subangular-rounded fine-very fine translucent-opaque quartz with common iron oxide staining, trace basaltic lithics, trace carbonaceous material, common greenish grey-light greenish grey silty matrix, moderately consolidated, moderately calcareous, soft, poor-fair visual porosity, no oil fluorescence. 260.50-260.67m Unconsolidated Sand (100%) UNCONSOLIDATED SAND: light greenish grey-medium bluish grey, moderately sorted, fine-medium, subangular-rounded, dominant subangular-rounded fine-very fine translucent-opaque quartz with common iron oxide staining, common round-well rounded granitic lithics, trace carbonaceous material, trace brown silty matrix, moderately calcareous, no visible cement, unconsolidated, good-excellent visual porosity, no oil fluorescence. 260.67-260.83m Calcareous Sandstone (100%) CALCAREOUS SANDSTONE: white-very light greenish grey, moderately sorted, fine-very fine, common subangular-rounded fine-very fine translucent-opaque quartz with common iron oxide staining, rare fine black coaly material, trace calcareous fossils, white-pale blue claystone matrix, strong calcareous cement, hard, poor-fair visual porosity, faint petroliferous odour, no oil fluorescence. 260.83-261.00m No Recovery.

REMARKS:

LAKES OIL N.L.					CORE REPORT No. 12

WELL NAME: 	Patrobus No.1		DATE: 07 OCT 05

| INTERVAL CORED | 261-264m |  |
| --- | --- | --- |
| CUT: 3m | RECOVERED: 2.81m | RECOVERY: 94% |
| GEOLOGIST: | Ingrid Campbell |  |

GENERALIZED LITHOLOGY OF INTERVAL:

Calcareous Silty Marlstone with minor shelly interbeds overlying Greensand.

Sedimentary bedding at 0 degrees. Generally sedimentary structurally amorphous except for shelly interbeds and Marlstone/Greensand contact. Calcareous Silty Marlstone 261-262.9m Greensand 262.9-263.81m

| POROSITY | Moderate visual (Marl) Good visual (Greensand). |
| --- | --- |
| FLOURESCENCE | No oil fluorescence, dull yellow-blue mineral fluorescence. |
| CUT | Nil. |
| STAIN | Nil. |

DESCRIPTION:

261.0-262.9m Silty Marlstone (100%) SILTY MARLSTONE: olive green-dark tan, abundant very fine subangular-subrounded translucent-opaque quartz with common iron staining, common lithics, occasional interbeds of shelly fragments, moderately consolidated, poor-moderate visual porosity, no oil fluorescence. 262.9-263.55m Greensand (100%) GREENSAND: medium green-dark green, unconsolidated-moderately consolidated, abundant dark green-brown subrounded-rounded medium-coarse glauconitic nodules, minor shelly fragments, mostly pelecypod fragments, pyritic echinoid spines, bryozoan, fine-moderately fine clear-opaque quartz, minor lithics, calcareous cement, moderate-good visual porosity, moderate petroliferous odour, no oil fluorescence.

REMARKS:

Greensand: visual porosity varies from moderate to very good, petroliferous odour but no fluorescence or show detected.

LAKES OIL N.L.					CORE REPORT No. 13

WELL NAME: 	Patrobus No.1		DATE: 07 OCT 05

| INTERVAL CORED | 264-267m |  |
| --- | --- | --- |
| CUT: 3m | RECOVERED: 3.06m | RECOVERY: 102% |
| GEOLOGIST: | Ingrid Campbell |  |

GENERALIZED LITHOLOGY OF INTERVAL:

Greensand with band of Glauconitic Conglomerate.

Sedimentary bedding at 0 degrees. Generally sedimentary structurally amorphous except for shelly interbeds and upwards fining in the interval 265.31-265.90m

| POROSITY | Poor-moderate visual porosity |
| --- | --- |
| FLOURESCENCE | No oil fluorescence, dull blue-yellow mineral fluorescence. |
| CUT | Nil. |
| STAIN | Nil. |

DESCRIPTION:

264.0-264.05m Greensand (100%) GREENSAND: medium green-dark green, moderately consolidated, abundant dark green-brown subrounded-rounded medium-coarse glauconitic nodules, fine-coarse shelly fragments throughout, gastropods, fine-moderately fine clear-opaque quartz, minor lithics, calcareous cement, fair-moderate visual porosity, no oil fluorescence. 264.05-265.23m Greensand (100%) GREENSAND: medium green-dark green, unconsolidated-moderately consolidated, abundant dark green-brown subrounded-rounded medium-coarse glauconitic nodules, fine-moderately fine clear-opaque quartz, minor lithics, calcareous, fair-moderate visual porosity, no oil fluorescence. 265.23-265.31m Greensand (100%) GREENSAND: pale green-medium green, consolidated, abundant dark green-brown subrounded-rounded medium-coarse glauconitic nodules, fine-moderately fine clear-opaque quartz, coarse shell fragments, poor visual porosity, no oil fluorescence. 265.31-265.90m Greensand (100%) GREENSAND: medium green, consolidated, abundant dark green-brown subrounded-rounded medium-coarse glauconitic nodules, fine-moderately fine clear-opaque quartz, calcareous, fining upwards in interval, poor visual porosity, no oil fluorescence. 265.90-266.02m Greensand (100%) GREENSAND: medium green, consolidated, abundant dark green-brown subrounded-rounded medium-coarse glauconitic nodules, fine-moderately fine clear-opaque quartz, common medium-coarse shell fragments, trace pyrite, calcareous cement, hard, poor visual porosity, no oil fluorescence. 266.02-266.40m Glauconitic Conglomerate (100%) GLAUCONTIC CONGLOMERATE: medium green-grey green, coarse-very coarse shelly fragments, mud clasts, lithic fragments, poorly sorted, moderately consolidated. 266.40-266.48m Greensand (100%) GREENSAND: light green-medium green, fine-medium, abundant dark green-brown subrounded-rounded medium-coarse glauconitic nodules, fine-moderately fine clear-opaque quartz, calcareous matrix, fractured interval, hard, poor visual porosity, no oil fluorescence. 266.48-267m Shelly Greensand (100%) SHELLY GREENSAND: light green-medium green darker towards base, poorly sorted, consolidated, abundant dark green-brown subrounded-rounded medium-coarse glauconitic nodules, fine-moderately fine clear-opaque quartz, common coarse shell fragments, trace pyrite, calcareous cement, hard, poor visual porosity, no oil fluorescence.

REMARKS:

Recovered 6cm of core 12.