LAKES OIL N.L.

A.C.N. (004 247 214)

Patrobus No.1		PEP 155 (east)

DAILY GEOLOGICAL REPORT No. 4	Date: 09 Sep 05

Depth: 40m		Progress: 0m		Days from Spud: 04

Rig:			Drilltec		GL(ASL):		31.55m

Drilling Rep:	Tim O’Brien	RT (AGL):		1.55m

Geologist:		Ingrid Campbell	Last Casing:	00mm at 000m

Comments: Ream to bottom with 7.875” hole.

| Interval (mRT) | Hydrocarbon Show Summary | Gas |
| --- | --- | --- |

| Formation Tops: | Prognosed (mRT) | Actual٭ (mRT) | Actual٭ (mSS) | Difference٭ (High/Low) |
| --- | --- | --- | --- | --- |
| Pleistocene dune deposit | Absent | 1.55 | +33.1 | - |
| Haunted Hills Gravel | 1.55 | 36 | -4.45 | 34.45 Low |
| Jemmy’s Point Formation | 15 |  |  |  |
| Gippsland Limestone | 50 |  |  |  |
| Lakes Entrance Formation | 190 |  |  |  |
| Colquhuon Gravels | 360 |  |  |  |
| Granite Basement | 400 |  |  |  |
| Total Depth | 600 |  |  |  |

٭Provisional, based on mudlog

LAKES OIL N.L.

A.C.N. (004 247 214)

Patrobus No.1		PEP 155 (east)

DAILY GEOLOGICAL REPORT No. 4

Lithological and Fluorescence Description

| Interval (m) | Description |
| --- | --- |
|  | No new formation was drilled |

LAKES OIL N.L.				CUTTINGS DESCRIPTIONS

WELL NAME: 		Patrobus No.1		DATE 09 SEP 05

GEOLOGIST:		Ingrid Campbell		PAGE:	1

| Interval (m) | % | Description |
| --- | --- | --- |
| 039-042 |  |  |