LAKES OIL N.L.

A.C.N. (004 247 214)

Patrobus No.1		PEP 155 (east)

DAILY GEOLOGICAL REPORT No. 6	Date: 14 Sep 05

Depth: 48m		Progress: 6m		Days from Spud: 09

Rig:			Drilltec		GL(ASL):		31.55m

Drilling Rep:	Tim O’Brien	RT (AGL):		1.55m

Geologist:		Ingrid Campbell	Last Casing:	00mm at 000m

Comments: Drill through gravel with cable tool rig and run casing to 48m (not cemented).

| Interval (mRT) | Hydrocarbon Show Summary | Gas |
| --- | --- | --- |

| Formation Tops: | Prognosed (mRT) | Actual٭ (mRT) | Actual٭ (mSS) | Difference٭ (High/Low) |
| --- | --- | --- | --- | --- |
| Pleistocene dune deposit | Absent | 1.55 | +33.1 | - |
| Haunted Hills Gravel | 1.55 | 36 | -4.45 | 34.45 Low |
| Jemmy’s Point Formation | 15 | 45 | -12.9 | 30 Low |
| Gippsland Limestone | 50 |  |  |  |
| Lakes Entrance Formation | 190 |  |  |  |
| Colquhuon Gravels | 360 |  |  |  |
| Granite Basement | 400 |  |  |  |
| Total Depth | 600 |  |  |  |

٭Provisional, based on mudlog

LAKES OIL N.L.

A.C.N. (004 247 214)

Patrobus No.1		PEP 155 (east)

DAILY GEOLOGICAL REPORT No. 6

Lithological and Fluorescence Description

| Interval (m) | Description |
| --- | --- |
| 40-42 | HAUNTED HILLS GRAVELS Unconsolidated gravels (80%) grading to and interbedded with Unconsolidated sand (20%) UNCONSOLIDATED GRAVEL: medium to coarse gravel, poorly sorted mixed grains, common angular-subangular quartz, granitic, metamorphic lithics, fine grained volcanics, excellent visual porosity, no show. UNCONSOLIDATED SAND: medium to coarse grained, subangular-subround, poorly sorted, unconsolidated, mixed grains, excellent visual porosity, no show. |
| 42-48 | HAUNTED HILLS GRAVELS/JEMMY’S POINT FORMATION Unconsolidated gravels (20%) grading to Limestone (80%) UNCONSOLIDATED GRAVEL: medium to coarse gravel, poorly sorted mixed grains, common angular-subangular quartz, granitic, metamorphic lithics, fine grained volcanics, excellent visual porosity, no show. LIMESTONE: white-light grey, fine-very coarse, poorly sorted, fossiliferous limestone, crinoids, bryozoan, shell fragments, very fine matrix, soft, moderate-good visual porosity, no show. |

LAKES OIL N.L.				CUTTINGS DESCRIPTIONS

WELL NAME: 		Patrobus No.1		DATE 14 SEP 05

GEOLOGIST:		Ingrid Campbell		PAGE:	1

| Interval (m) | % | Description |
| --- | --- | --- |
| 039-042 | 80 | UNCONSOLIDATED GRAVEL: medium-coarse grained, sub-angular-angular, poorly sorted, unconsolidated, common subangular-angular quartz, granitic, metamorphic lithics, fine grained volcanic lithics |
|  | 20 | UNCONSOLIDATED SAND: medium to coarse grained, subangular-subround, poorly sorted, unconsolidated, mixed grains. |
| 042-045 | 20 | UNCONSOLIDATED GRAVEL: A/A |
|  | 80 | LIMESTONE: white-light grey, fine-very coarse, poorly sorted, fossiliferous limestone, crinoids, bryozoan, shell fragments, very fine matrix, soft. |
| 045-048 | 10 | UNCONSOLIDATED GRAVEL: A/A |
|  | 90 | LIMESTONE: A/A |