DRILLING / WELLWORK REPORT 24HRS TO 0500 HRS June 16, 2006

SAFETY:

DAYS SINCE LAST TRI:	PREVIOUS BEST TRI PERIOD

| RIG 453 | 29 | 363 |
| --- | --- | --- |
| CAMERON | 5484 | 5510 |
| HALLIBURTON | 3307 | 3302 |
| SCHLUMBERGER | 2086 | 2085 |
| ISDL | 29 | 647 |
| ISS | 21 | 2336 |

Well: WKF_W19A

Rig/Contractor: 	Rig 453	Report Date: June 16, 2006

Supervisor:.	Campbell, Glenn R.

Davis, Brian.

| AFE Number: | L0501G653 | Ave Angle: |  |
| --- | --- | --- | --- |
| Days to Complete: | 2 | AFE Cost/Days: | $5,200,000.00 |
| Daily Cost: | $756,693 |  |  |
| Total Cost: | $3,890,123 | Planned MD/TVD: | 2682.00/2363.00 |
| Casing Size: |  | Actual MD/TVD: | 2687.00/2373.41 |
| Mud Weight: |  | Tubing Size: |  |

| Objective: | WKF_W19A |
| --- | --- |
| Management Summary: | Run and land 2-7/8" completion. R/up & test Howco slickline. Function TRSSSV. RIH & seat N-test tool. Set packer w/ 4000 psi. POH & R/dn Slickline. P/tst packer seals. L/dn landing jt. Install BPV. N/dn BOP. Install & test tree. |
| Current: | Pressure Testing Xmas Tree |
| Planned: | Recover BPV. Install Deck Grating. Rig down and skid over W-31. |