DRILLING / WELLWORK REPORT 24HRS TO 0500 HRS October 25, 2006

| RIG 453 | 159 | 363 |
| --- | --- | --- |
| CAMERON | 1634 | 1634 |
| HALLIBURTON | 3422 | 3422 |
| SCHLUMBERGER | 2363 | 2363 |
| ISDL | 159 | 647 |
| ISS | 148 | 2357 |

Well: WKF_W23A

Rig/Contractor: 	Rig 453	Report Date: October 25, 2006

Supervisor:	George, Steel

Stead, Cory

| AFE Number: | L0501G660 | Ave Angle: |  |
| --- | --- | --- | --- |
| Days to Complete: | 14.2 | AFE Cost/Days: | $5,948,157 |
| Daily Cost: | $182,282 |  |  |
| Total Cost: | $2,940,425 | Planned MD/TVD: | 3339.00/2797.24 |
| Casing Size: |  | Actual MD/TVD: | 3338.00/2382.04 |
| Mud Weight: |  | Tubing Size: |  |

| Objective: | WKF_W23A |
| --- | --- |
| Management Summary: | POOH from 1271m to 1054m. Log OOH to 930m. POOH to BHA at 243m. L/out logging tools, logging garage & Locked Jar. P/U Drilling Jar. L/out drilling BHA. M/U cleanout BHA & RIH to 3280m. Circulate & condition mud. Held Trip Drills. |
| Current: | Circulating prior to washing/reaming to bottom. |
| Planned: | Wash to TD. Circulate hole clean. POOH to shoe. Circulate hole clean. POOH to BHA. C/out MPR's to 4½" x 7" VBR's. POOH & L/out BHA. Shell test. R/U & run 7" casing. |