Report for : Greg Doty / Sam Falkner / Mark Calicutt

Compiled by : Alex Djukanovic / Mark Smith

| WELL | WKF W26A |
| --- | --- |
| DATE | 23-12-2009 |
| REPORT # | 7 |
| MIDNIGHT ACTIVITY | Running in hole with 7.0” casing. |  | ROP DATA (LAST 24 hours) | m/hr | DEPTH (m) |
| MIDNIGHT DEPTH | 3832.07 mMDRT |  | MINIMUM |  |  |
| TVD | 2386.04 mMDRT |  | MAXIMUM |  |  |
| PROGRESS LAST 24 hrs | 0 m |  | AVERAGE |  |  |

| PRELIMINARY FIELD PICKS | ACTUAL TOP (mMDRT) | ACTUAL TOP (mTVDRT) | ACTUAL TOP (mTVDSS) RT to MSL | HIGH/ LOW (mTVD) | PROGNOSED TOP (mMDRT) | PROGNOSED TOP (mTVDRT) |
| --- | --- | --- | --- | --- | --- | --- |
| Base of High Velocity Channel | 2248.0 | 1481.5 | -1439.8 | 14.8 L | 2223.1 | 1466.7 |
| Top of Lakes Entrance Formation (Mid Miocene Marker) | 2940.0 | 1872.5 | -1830.8 | 4.2 H | 2942.0 | 1876.7 |
| Top of Latrobe Group | 3619.0 | 2262.2 | -2220.5 | 0.5 L | 3616.7 | 2261.7 |
| Top Coarse Clastics (SBP3) | - | - | - | - | 3651.8 | 2281.7 |
| Top M13L (PSB4) | - | - | - | - | 3665.8 | 2289.7 |
| Top M14 (SB13) | 3668.0 | 2290.2 | -2248.5 | 1.5 H | 3669.3 | 2291.7 |
| Top M15 | 3692.0 | 2303.7 | -2262.0 | 0 | 3690.4 | 2303.7 |
| OOWC | - | - | - | - | 3771.1 | 2349.7 |
| Total Depth | 3832.07 | 2386.04 | -2344.3 | 2.1 L | 3831.06 | 2383.90 |

| Current Formation | Latrobe Gp. |
| --- | --- |

| GAS DATA | DEPTH (m) | TOTAL GAS (U) | C1 % | C2 % | C3 % | C4 % | C5 % | H2S ppm |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| MAX (Reserval) | - | - | - | - | - | - | - | - |
| MAX (GFF) | - | - | - | - | - | - | - | - |
| BG (Reserval) | - | - | - | - | - | - | - | - |
| BG (GFF) | - | - | - | - | - | - | - | - |
| TRIP GAS (Reserval) | - | - | - | - | - | - | - | - |
| TRIP GAS (GFF) | - | - | - | - | - | - | - | - |
| CONNECTION GAS | - | - | - | - | - | - | - | - |

| BIT DATA | PRESENT BIT | PREVIOUS BIT |
| --- | --- | --- |
| BIT No. | 2 | 1 |
| SIZE (in) | 9.875 | 9.875 |
| MANUFACTURER/TYPE | REED Hycalog / RSX616S-A1 | REED Hycalog / RSX616M-A13 |
| JETS (/32 inch) | 8 x 16 | 8 x 16 |
| DEPTH IN (m) | 1762 | 733 |
| DEPTH OUT (m) | 3832 | 1762 |
| METRES ON RUN (m) | 2070 | 1029 |
| HRS ON BTM 24hrs/total | - / 27.3 | 13.7 |
| BIT CONDITION | - | 1-1-WT-A-X-IN-SD-DTF |
| RPM RANGE 24hrs | - | 80 – 159 |
| Pump Hrs 24 hrs / total | 7.7 / 64.9 | 29.1 |
| Krevs 24 hrs / total | - / 237 | 110.0 |

| 24 HOUR SUMMARY | Continue to back ream out of hole from 2396.0 mMDRT to inside of casing at 732.0 mMDRT. Circulate bottoms up inside the casing until shakers are clean. Conducted a flow check and then pumped a slug prior to pulling out of hole on elevators to 32.0 mMDRT. Lay down 9 7/8” drilling assembly as per Anadrill instructions. Clear and clean drill floor of excess equipment. Make up and run in hole to retire the wear bushing, break out and lay down same. Make up jetting tool. Run in hole with jetting tool assembly and jet the well head and BOP. Service top drive and blocks. Rig up Weatherford tong, FMS, handling gear and casing fill up hose. Pick up and make up 7.0” casing hanger and landing joints as per Cameron instructions. Pick up and make up cement head cross over to landing joint. Install FMS. Pick up and commence run in hole with 7.0” casing shoe to 39.0 mMDRT. Fill with mud and pick up shoe track to test floats, ok. Run in hole with 7.0” casing filling every joint monitoring the trip tank during the run. |
| --- | --- |
| 22-12-2009 5 AM UPDATE | Continue to run in hole with 7.0” casing to the 10 ½” casing shoe at 732 mMDRT. Switch over to rig pumps and fill the casing, continue to pump circulating the hole. Resume casing run from 732.0 mMDRT, filling every joint and monitoring the trip tank volumes during the run in hole. Current depth of casing at 0500 hours of 792.0 mMDRT. 3832.07 mMDRT (2386.04 mTVDRT) |