Report for : Dan Daniels / Mark Calicutt  / Andy Choy

Compiled by : Mark Smith

| WELL | WKF W5A |
| --- | --- |
| DATE | 11-11-2009 |
| REPORT # | 5 |
| MIDNIGHT ACTIVITY | Drilling 9-7/8” hole. |  | ROP DATA (LAST 24 hours) | m/hr | DEPTH (m) |
| MIDNIGHT DEPTH | 3299.0 mMDRT |  | MINIMUM | 19.1 | 3271.0 |
| TVD | 2346.1 mTVDRT |  | MAXIMUM | 101.4 | 2952.0 |
| PROGRESS LAST 24 hrs | 641.0 m |  | AVERAGE | 50.1 | 2658.0 – 3299.0 |

| PRELIMINARY FIELD PICKS | ACTUAL TOP (mMDRT) | ACTUAL TOP (mTVDRT) | ACTUAL TOP (mTVDSS) RT to MSL (41.7m) | HIGH/ LOW (mTVD) | PROGNOSED TOP (mMDRT) | PROGNOSED TOP (mTVDRT) |
| --- | --- | --- | --- | --- | --- | --- |
| Base of High Velocity Channel | 2158.0 | 1643.0 | -1601.3 | 1.3 L | 2153.9 | 1641.7 |
| Top of Lakes Entrance Formation | 2513.0 | 1886.9 | -1845.2 | 8.2 L | 2500.0 | 1878.7 |
| Top of Latrobe Group | 3188.0 | 2289.4 | -2247.7 | 17.7 L | 3147.3 | 2281.7 |
| Top P11 (FSP1) | 3235.0 | 2313.4 | -2271.7 | 13.7 L | 3203.2 | 2299.7 |
| Top Coarse Clastics (SBP3) / M12 | 3268.5 | 2330.4 | -2228.7 | 24.7 L | 3215.2 | 2305.7 |
| Top M13 (PSB7) | 3280.5 | 2336.5 | -2294.8 | 23.8 L | 3229.2 | 2312.7 |
| Top M14 (SB13) | 3322.0 | 2357.6 | -2315.9 | 10.9 L | 3297.2 | 2346.7 |
| Kingfish OOWC | 3318.2 | 2355.7 | -2314.0 | 0 | 3315.3 | 2355.7 |
| Top M15 | 3365.7 | 2380.0 | -2338.3 | 13.3 L | 3337.2 | 2366.7 |
| Total Depth | 3390.00 | 2392.50 | -2350.77 | 6.8 L | 3375.3 | 2385.7 |

| Current Formation | Latrobe Group: |
| --- | --- |

| GAS DATA | DEPTH (m) | TOTAL GAS (U) | C1 % | C2 % | C3 % | C4 % | C5 % | H2S ppm |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| MAX (Reserval) | 3295.0 | 130.1 | 0.769 | 0.233 | 0.260 | 0.180 | 0.057 | - |
| MAX (GFF) | - | - | - | - | - | - | - | - |
| BG (Reserval) | 2658.0-3299.0 | 15 | 0.258 | 0.010 | 0.004 | 0.001 | - | - |
| BG (GFF) | - | - | - | - | - | - | - | - |
| TRIP GAS (Reserval) | - | - | - | - | - | - | - | - |
| TRIP GAS (GFF) | - | - | - | - | - | - | - | - |
| CONNECTION GAS | - | - | - | - | - | - | - | - |

| BIT DATA | PRESENT BIT | PREVIOUS BIT |
| --- | --- | --- |
| BIT No. | 1 |  |
| SIZE (in) | 9-7/8 |  |
| MANUFACTURER/TYPE | Reed Hycalog RSR616S |  |
| JETS (/32 inch) | 8 x 16 |  |
| DEPTH IN (m) | 679.0 |  |
| DEPTH OUT (m) | - |  |
| METRES ON RUN (m) | 2620.0 |  |
| HRS ON BTM 24hrs/total | 12.8 / 40.6 |  |
| BIT CONDITION | - |  |
| RPM RANGE 24hrs | 89-161 |  |
| Pump Hrs 24 hrs / total | 19.8 / 80.9 |  |
| Krevs 24 hrs / total | 102.7 / 334.1 |  |

| 24 HOUR SUMMARY | Continue to back ream to 2570.0 mMDRT. Run in hole and wash last stand to bottom. Control drill at 50.0 m/hr while building mud volume and adding Baracarb to system. Drill and survey 9-7/8” hole from 2658.0 mMDRT to 2775.0 mMDRT. Monitor on trip while repairing mud pump stand pipe seal. Drill and survey 9-7/8” hole from 2775.0 mMDRT to 3066.0 mMDRT. Circulate and condition mud from 3066.0 mMDRT to 3066.0 mMDRT while working on electrical problem with mud pump #1 traction motor. Drill and survey 9-7/8” hole from 3066.0 mMDRT to 3124.0 mMDRT. Circulate and condition mud from 3124.0 mMDRT to 3096.0 mMDRT while working on electrical problem with mud pump #1 traction motor. Drill and survey 9-7/8” hole from 3124.0 mMDRT to 3299.0 mMDRT. |
| --- | --- |
| 12-11-2009 5 AM UPDATE | Drill and survey 9-7/8” hole from 3299.0 mMDRT to 3390.0 mMDRT Total Depth. Circulate and back ream from 3390.0 mMDRT to 3350.0 mMDRT, racking back 1 stand per bottoms up. 3390.0 mMDRT (2392.50 mTVDRT) |