Report for : Greg Doty / Sam Falkner

Compiled by : Gareth Munro / Phil Rady

| WELL | WKF W8A |
| --- | --- |
| DATE | 7-12-2009 |
| REPORT # | 9 |
| MIDNIGHT ACTIVITY | Drill ahead 9-7/8” production hole. |  | ROP DATA (LAST 24 hours) | m/hr | DEPTH (m) |
| MIDNIGHT DEPTH | 4351.0 m |  | MINIMUM | 24.5 | 4301.0 |
| TVD | 2272.3 m |  | MAXIMUM | 160.43 | 3916.0 |
| PROGRESS LAST 24 hrs | 497.0 |  | AVERAGE | 69.03 |  |

| PRELIMINARY FIELD PICKS | ACTUAL TOP (mMDRT) | ACTUAL TOP (mTVDRT) | ACTUAL TOP (mTVDSS) RT to MSL | HIGH/ LOW (mTVD) | PROGNOSED TOP (mMDRT) | PROGNOSED TOP (mTVDRT) |
| --- | --- | --- | --- | --- | --- | --- |
| Base of High Velocity Channel | 2304.0 | 1378.4 | -1336.73 | -3.3H | 2310.0 | 1381.7 |
| Mid Miocene Marker | 3838.0 | 1843.9 | -1802.16 | 2.2L | 3840.0 | 1841.7 |
| Top of Lakes Entrance Formation | 3973.0 | 1933.6 | -1891.9 | -8.1H | 3940.0 | 1941.7 |
| Top of Latrobe Group | 4352.5 | 2274.2 | -2232.5 | 3.1L | 4352.0 | 2271.1 |
| Top P1.1 West | 4382.0 | 2303.7 | -2262.0 | 7.0L | 4378.0 | 2297.7 |
| Top Coarse Clastics (SBP3) | 4397.0 | 2318.7 | -2277.0 | 7.0L | 4392.0 | 2311.7 |
| Top M1.3U (PSB7) | 4416.0 | 2337.7 | -2296.0 | 2.0L | 4416.0 | 2335.7 |
| PSB5 | 4422.0 | 2343.7 | -2302.0 | 2.0L | 4422.0 | 2341.7 |
| PSB4 | 4427.0 | 2348.7 | -2307.6 | 3.0L | 4426.0 | 2345.7 |
| Top M1.4U (SB13) | 4435.0 | 2356.7 | -2315.0 | 2.0L | 4435.0 | 2354.7 |
| Top M1.4L |  |  |  |  | 4452.0 | 2371.7 |
| M1.4C |  |  |  |  | 4458.0 | 2377.7 |
| M1.4C OOWC |  |  |  |  | 4459.0 | 2379.5 |
| Top M1.5 |  |  |  |  | 4468.0 | 2387.7 |
| M1.4B OOWC |  |  |  |  | 4469.0 | 2388.4 |
| Total Depth |  |  |  |  | 4529.0 | 2448.3 |

| Current Formation | Lakes Entrance |
| --- | --- |

| GAS DATA | DEPTH (m) | TOTAL GAS (U) | C1 % | C2 % | C3 % | C4 % | C5 % | H2S ppm |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| MAX (Reserval) | 3875.0 | 31.0 | 0.606 | 0.002 | 0.001 | 0.001 | 0.000 | - |
| MAX (GFF) | 3855.0 | 99.0 | 2.290 | 0.000 | 0.002 | 0.006 | 0.000 | - |
| BG (Reserval) | 3854.0 – 4351.0 | 17.1 | 0.318 | 0.003 | 0.001 | 0.002 | 0.000 | 0 |
| BG (GFF) | 3854.0 – 4351.0 | 50.1 | 1.012 | 0.001 | 0.001 | 0.004 | 0.000 | 0 |
| TRIP GAS (Reserval) | - | - | - | - | - | - | - | - |
| TRIP GAS (GFF) | - | - | - | - | - | - | - | - |
| CONNECTION GAS | - | - | - | - | - | - | - | - |

| BIT DATA | PRESENT BIT | PREVIOUS BIT |
| --- | --- | --- |
| BIT No. | 1 |  |
| SIZE (in) | 9-7/8 |  |
| MANUFACTURER/TYPE | Reed Hycalog RSR616S-A1 |  |
| JETS (/32 inch) | 8 x 16 |  |
| DEPTH IN (m) | 830.0 |  |
| DEPTH OUT (m) | - |  |
| METRES ON RUN (m) | 3521.0 |  |
| HRS ON BTM 24hrs/total | 7.2 / 43.7 |  |
| BIT CONDITION |  |  |
| RPM RANGE 24hrs | 90 - 160 |  |
| Pump Hrs 24 hrs / total | 12.3 / 87.7 |  |
| Krevs 24 hrs / total | 96.9 / 416.0 |  |

| 24 HOUR SUMMARY | Change out top drive internal service loom. Run in hole on elevators from 828.0 mMDRT to 2571.0 mMDRT whilst monitoring well on trip tanks and filling pipe every 10 stands. Conduct ESSO full XOM Accumulator volume BOP function test. Continue to run in hole to 3767.0 mMDRT, washing and reaming down to 3854.0 mMDRT whilst down linking Anadrill’s tools. Drill ahead 9-7/8” production hole from 3854.0 m to 4351.0 mMDRT as per Anadrill’s instructions. |
| --- | --- |
| 08-12-2009 5 AM UPDATE | Continue to drill ahead 9-7/8” production hole from 4351.0 m to 4472.0 mMDRT as per Anadrill’s instructions. 4472.0 mMDRT (2394.0 mTVDRT) |