Report for : Greg Doty / Sam Falkner

Compiled by : Gareth Munro / Phil Rady

| WELL | WKF W8A |
| --- | --- |
| DATE | 9-12-2009 |
| REPORT # | 11 |
| MIDNIGHT ACTIVITY | Conduct safety stand down. |  | ROP DATA (LAST 24 hours) | m/hr | DEPTH (m) |
| MIDNIGHT DEPTH | 4535.00 m |  | MINIMUM | - | - |
| TVD | 2455.57 m |  | MAXIMUM | - | - |
| PROGRESS LAST 24 hrs | 0.0 |  | AVERAGE | - |  |

| PRELIMINARY FIELD PICKS | ACTUAL TOP (mMDRT) | ACTUAL TOP (mTVDRT) | ACTUAL TOP (mTVDSS) RT to MSL | HIGH/ LOW (mTVD) | PROGNOSED TOP (mMDRT) | PROGNOSED TOP (mTVDRT) |
| --- | --- | --- | --- | --- | --- | --- |
| Base of High Velocity Channel | 2304.0 | 1378.4 | -1336.73 | -3.3H | 2310.0 | 1381.7 |
| Mid Miocene Marker | 3838.0 | 1843.9 | -1802.16 | 2.2L | 3840.0 | 1841.7 |
| Top of Lakes Entrance Formation | 3973.0 | 1933.6 | -1891.9 | -8.1H | 3940.0 | 1941.7 |
| Top of Latrobe Group | 4352.5 | 2274.2 | -2232.5 | 3.1L | 4352.0 | 2271.1 |
| Top P1.1 West | 4382.0 | 2303.7 | -2262.0 | 7.0L | 4378.0 | 2297.7 |
| Top Coarse Clastics (SBP3) | 4397.0 | 2318.7 | -2277.0 | 7.0L | 4392.0 | 2311.7 |
| Top M1.3U (PSB7) | 4416.0 | 2337.7 | -2296.0 | 2.0L | 4416.0 | 2335.7 |
| PSB5 | 4422.0 | 2343.7 | -2302.0 | 2.0L | 4422.0 | 2341.7 |
| PSB4 | 4427.0 | 2348.7 | -2307.0 | 3.0L | 4426.0 | 2345.7 |
| Top M1.4U (SB13) | 4435.0 | 2356.7 | -2315.0 | 2.0L | 4435.0 | 2354.7 |
| Top M1.4L | 4451.0 | 2372.7 | -2331.0 | 1.0L | 4452.0 | 2371.7 |
| M1.4C | 4458.0 | 2379.7 | -2338.0 | 2.0L | 4458.0 | 2377.7 |
| M1.4C OOWC | 4459.0 | 2380.7 | -2339.0 | 1.2L | 4459.0 | 2379.5 |
| Top M1.5 | 4466.0 | 2387.7 | -2346.0 | 0.0 | 4468.0 | 2387.7 |
| M1.4B OOWC | 4472.0 | 2393.7 | -2352.0 | 5.3L | 4469.0 | 2388.4 |
| Total Depth | 4535.0 | 2455.57 | -2413.87 | 7.27L | 4529.0 | 2448.3 |

| Current Formation | Latrobe Group |
| --- | --- |

| GAS DATA | DEPTH (m) | TOTAL GAS (U) | C1 % | C2 % | C3 % | C4 % | C5 % | H2S ppm |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| MAX (Reserval) | - | - | - | - | - | - | - | - |
| MAX (GFF) | - | - | - | - | - | - | - | - |
| BG (Reserval) | - | - | - | - | - | - | - | - |
| BG (GFF) | - | - | - | - | - | - | - | - |
| TRIP GAS (Reserval) | - | - | - | - | - | - | - | - |
| TRIP GAS (GFF) | - | - | - | - | - | - | - | - |
| CONNECTION GAS | - | - | - | - | - | - | - | - |

| BIT DATA | PRESENT BIT | PREVIOUS BIT |
| --- | --- | --- |
| BIT No. | 1 |  |
| SIZE (in) | 9-7/8 |  |
| MANUFACTURER/TYPE | Reed Hycalog RSR616S-A1 |  |
| JETS (/32 inch) | 8 x 16 |  |
| DEPTH IN (m) | 830.0 |  |
| DEPTH OUT (m) | 4535.0 |  |
| METRES ON RUN (m) | 3705.0 |  |
| HRS ON BTM 24hrs/total | 4.9 / 48.6 |  |
| BIT CONDITION | 2-1-WT-A-X-I-CT-TD |  |
| RPM RANGE 24hrs | 90 - 159 |  |
| Pump Hrs 24 hrs / total | 16.9 / 104.6 |  |
| Krevs 24 hrs / total | 2.2 / 418.2 |  |

| 24 HOUR SUMMARY | Continue to pump and back ream out of hole to 1822.0 mMDRT. Flow check well then pull out 10 stands wet to 1504.0 mMDRT before slugging pipe and continuing to pull out of hole to inside the 10-3/4” shoe. Conduct Derrick inspection whilst flow checking well. Pull out of hole and rack back BHA using rig tongs at times due to hi torqued connections. Clear rig floor of excess equipment and then conduct safety stand down.. |
| --- | --- |
| 10-12-2009 5 AM UPDATE | Continue Hazard Hunt. Grease TDS and replace section of armour wrap on Kelly hose. Make up drop ball cement assembly whilst HOWCO tests 4” TIW and extra 5-½” TIW valve. Bring aboard 4” drill pipe from boat. Strap pipe and run in hole 31 joints 4535.0 mMDRT (2455.57 mTVDRT) |