Report for : Dan Daniels / Sam Falkner / Mark Calicutt

Compiled by : Gareth Munro / Dan Dennis

| WELL | WKF W9A |
| --- | --- |
| DATE | 30-12-2009 |
| REPORT # | 6 |
| MIDNIGHT ACTIVITY | Drill ahead 9-7/8” production hole. |  | ROP DATA (LAST 24 hours) | m/hr | DEPTH (m) |
| MIDNIGHT DEPTH | 3183.0 mMDRT |  | MINIMUM | 25.31 | 3156.0 |
| TVD | 2095.5 mMDRT |  | MAXIMUM | 127.57 | 2661.0 |
| PROGRESS LAST 24 hrs | 881 m |  | AVERAGE | 66.24 |  |

| PRELIMINARY FIELD PICKS | ACTUAL TOP (mMDRT) | ACTUAL TOP (mTVDRT) | ACTUAL TOP (mTVDSS) RT to MSL | HIGH/ LOW (mTVD) | PROGNOSED TOP (mMDRT) | PROGNOSED TOP (mTVDRT) |
| --- | --- | --- | --- | --- | --- | --- |
| Base High Velocity Channel | 2206.0 | 1553.6 | -1511.9 | 18.1mH | 2239.2 | 1571.7 |
| Lakes Entrance Formation |  |  |  |  | 2956.5 | 1971.7 |
| Top Latrobe Gp. |  |  |  |  | 3475.2 | 2262.0 |
| Top Coarse Clastics (SBP3) |  |  |  |  | 3488.3 | 2264.7 |
| Top M13L |  |  |  |  | 3515.2 | 2269.7 |
| Top M14 |  |  |  |  | 3535.4 | 2286.7 |
| Top M15 |  |  |  |  | 3547.3 | 2301.7 |
| Top M17 |  |  |  |  | 3585.2 | 2323.7 |
| OOWC |  |  |  |  | 3629.0 | 2347.0 |
| TD |  |  |  |  | 3704.0 | 2389.5 |

| Current Formation | Lakes Entrance Formation |
| --- | --- |

| GAS DATA | DEPTH (m) | TOTAL GAS (U) | C1 % | C2 % | C3 % | C4 % | C5 % | H2S ppm |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| MAX (Reserval) | 2683.0 | 25.0 | 0.453 | 0.001 | 0.000 | 0.002 | 0.000 | - |
| MAX (GFF) | 3107.0 | 69.0 | 1.184 | 0.000 | 0.000 | 0.000 | 0.000 | - |
| BG (Reserval) | 2302 - 3183 | 11.8 | 0.224 | 0.001 | 0.000 | 0.001 | 0.000 | 0 |
| BG (GFF) | 2302 - 3183 | 22.8 | 0.397 | 0.000 | 0.000 | 0.000 | 0.000 | 0 |
| TRIP GAS (Reserval) | - | - | - | - | - | - | - | - |
| TRIP GAS (GFF) | - | - | - | - | - | - | - | - |
| CONNECTION GAS | - | - | - | - | - | - | - | - |

| BIT DATA | PRESENT BIT | PREVIOUS BIT |
| --- | --- | --- |
| BIT No. | 1 |  |
| SIZE (in) | 9-7/8 |  |
| MANUFACTURER/TYPE | Reed Hycalog / RSR616S-A1 |  |
| JETS (/32 inch) | 8 x 16 |  |
| DEPTH IN (m) | 923 |  |
| DEPTH OUT (m) | - |  |
| METRES ON RUN (m) | - |  |
| HRS ON BTM 24hrs/total | 13.3 / 38.4 |  |
| BIT CONDITION | - |  |
| RPM RANGE 24hrs | 152 – 181 |  |
| Pump Hrs 24 hrs / total | 20.4 / 56.2 |  |
| Krevs 24 hrs / total | 132.5 / 372.7 |  |

| 24 HOUR SUMMARY | Continue to drill 9-7/8” hole as per Anadrill instruction from 2302.0 to 2512.0 mMD. Continue to drill 9-7/8” hole and survey as per Anadrill instruction from 2512.0 to 2979.0 mMD. Circulate 3 bottoms up racking back 1 stand per bottoms up to clean hole prior to adding Barracarb. Continue to drill 9-7/8” hole as per Anadrill instruction from 2979.0 to 3183.0 mMD. |
| --- | --- |
| 31-12-2009 5 AM UPDATE | Continue to drill 9-7/8” hole as per Anadrill instruction from 3183.0 to 3370.0 mMD. Current operation at 0500hrs drilling ahead. 3370.00 mMDRT (2200.1 mTVDRT) |