ESSO AUSTRALIA LTD

CHECKSHOT PROCESSING REPORT

Vertical Incidence Checkshot Survey

BLACKBACK A-1A

| FIELD: | BLACKBACK |
| --- | --- |
| COUNTRY: | AUSTRALIA |
| COORDINATES: | 038 32' 31.677" S |
| : | 148 33' 11.274" E |
| CHECKSHOT SURVEY: | 23-Jun 1999 |
| REFERENCE No: |  |
| INTERVAL: | 3170-1250 m MD |
| Prepared by | Henry Cao |

CONTENTS

1.0		Acquisition Summary

2.0		Processing sequence

Figure 1	Stacked data, measured depth indexed

Figure 2	TWT and Interval Velocity from Checkshot Survey

A1		Navigation Data for Source Position

A2		Wellbore Trajectory Summary

1. Acquisition Summary

The aim of the checkshot survey at Blackback A-1A was to record the vertical transit time from the surface to the downhole tool in the well at 11 different levels. To achieve this, the airgun was suspended from a boat that followed the deviated well trajectory and fired remotely over a radio link.

A single G airgun with a 150 cubic inch chamber was used as the energy source and charged from high pressure bottled nitrogen.  The gun was fired at 1800 psi, 6 m below the sea level off the side of the boat.

A CSAT tool was used for downhole data acquisition. The Macha offset shooting equipment (OSE) was used to remotely fire the airgun and return the hydrophone signal to the Maxis logging unit. Pre-job checks determined a 3 msec delay in the hydrophone data transmission over the radio link, so a +3 msec correction has been applied to the raw transit times to compensate for the radio delay.

Navigation was supplied by Esso Australia Limited (see Appendix I). On average, the airgun locations were misplaced to their target positions (the surface projections of the pre-job determined downhole geophone locations) by 2.8 and 6.0 meters in easting (X) and northing (Y), respectively.  The standard deviations for the misplacement are 17.2 and 19.5 metres in easting and northing.

By comparing the pre-job target source positions with the surface projections of the actual downhole geophone locations, it was found that most discrepancies between these two were within 10 m.  The combined discrepancies (difference between the actual source position and the target source position and that between the target source position and the surface projection of the actual downhole sensor) can yield a maximum TWT difference of 0.3 ms from the true vertical TWT.  Therefore, all the data meet the accuracy requirement.

2. Processing Sequence

- Re-stack data using radio hydrophone channels as zero time reference. The break times from these stacks are very close (within 0.5 ms) to those shown on the field acquisition log print except for levels at 1970 and 2570 m MD where the Maxis picked earlier on the reference hydrophone channels.

- Add 3 msec to the one way times to compensate for radio delay.

- Enter surface gun co-ordinates, gun depth and hydrophone depth. The gun depth was 6 metres below sea level and the hydrophone depth was 4.5 metres below sea level.

- Enter well deviation and inclination data. The true vertical depths are computed using the “minimum radius of curvature” method.

- Compute vertical transit times based on the survey geometry. Interval velocities are derived from the vertical transit times and TVD’s.

Table 1 lists the key parameters and result of the checkshot survey.  Figure 1 shows the stacked Z-component data. The X and Y data were recorded but not required for checkshot processing so are not displayed. Figure 2 displays TWT and interval velocity computed from checkshot corrected transit times

# Table 1 Listing of key parameters for the checkshot survey

|  | MD | R_X | R_Y | R_Z | S_X | S_Y | S_Z | TT | TWT | Velocity |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | (m) | (m) | (m) | (m) | (m) | (m) | (m) | (s) | (s) | (m/s) |
|  | 421 |  |  | 395 |  |  | 6 | 0.2553 | 0.5266 | 1500 |
|  | 1250 | 635353 | 5733095 | 1151 | 635353 | 5733095 | 6 | 0.5712 | 1.1585 | 2393 |
|  | 1370 | 635347 | 5733195 | 1216 | 635347 | 5733205 | 6 | 0.5956 | 1.2073 | 2663 |
|  | 1570 | 635362 | 5733343 | 1350 | 635362 | 5733343 | 6 | 0.6417 | 1.2993 | 2912 |
|  | 1770 | 635397 | 5733441 | 1519 | 635397 | 5733440 | 6 | 0.6931 | 1.4021 | 3287 |
|  | 1970 | 635459 | 5733471 | 1715 | 635459 | 5733471 | 6 | 0.7472 | 1.5104 | 3621 |
|  | 2170 | 635527 | 5733448 | 1892 | 635527 | 5733448 | 6 | 0.7986 | 1.6132 | 3443 |
|  | 2370 | 635598 | 5733421 | 2077 | 635597 | 5733421 | 6 | 0.8513 | 1.7186 | 3511 |
|  | 2570 | 635671 | 5733392 | 2261 | 635670 | 5733391 | 6 | 0.8961 | 1.8082 | 4109 |
|  | 2770 | 635742 | 5733360 | 2445 | 635742 | 5733360 | 6 | 0.9444 | 1.9047 | 3811 |
|  | 2970 | 635817 | 5733326 | 2628 | 635816 | 5733326 | 6 | 1.0075 | 2.0310 | 2898 |
|  | 3170 | 635893 | 5733288 | 2809 | 635893 | 5733288 | 6 | 1.0696 | 2.1553 | 2914 |

Note that MD stands for measured depth, R and S for receiver and source, and X, Y and Z are easting, northing and TVD depth from MSL respectively.  TT stands for transit time, a time difference between the arrival times at the hydrophone and downhole geophone.  TWT is the two way time for a seismic wave traveling from the surface at MSL to the downhole geophone, and back to the mean sea level.  Velocity is the interval velocity derived between two neighboring levels.

Figure 1. Stacked Z-component data, traces indexed by measured depth

(A)

(B)

Figure 2. TWT and Interval Velocity derived from corrected transit times.

A1		Navigation Data for Source Position

|  | Acquisition Geometry Summary for Checkshot Survey at Blackback A-1A |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | Wellhead Position: |  | 635355.1E |  | 5732873.4N |  |  |  |
|  | Location | Bass Strait |  |  |  |  |  |  |
|  | Client | Esso Australia |  | BB A-1A |  |  |  |  |
|  | Navigated By |  | Date | 23/06/1999 |  |  |  |  |
|  |  |  | Actual |  | Target |  |  |  |
|  | MD | Shot # | Easting | Northing | Easting | Northing | dE | dN |
|  | 1250 | 1 | 635345.2 | 5733096.6 | 635353.4 | 5733094.6 | -8.2 | 2.0 |
|  |  | 2 | 635348.3 | 5733095.5 | 635353.4 | 5733094.6 | -5.1 | 0.9 |
|  |  | 3 | 635341.9 | 5733090.5 | 635353.4 | 5733094.6 | -11.5 | -4.1 |
|  |  | 4 | 635339.2 | 5733093.8 | 635353.4 | 5733094.6 | -14.2 | -0.8 |
|  |  | 5 | 635344.3 | 5733095.6 | 635353.4 | 5733094.6 | -9.1 | 1.0 |
|  |  | 6 | 635353.4 | 5733099.5 | 635353.4 | 5733094.6 | 0.0 | 4.9 |
|  |  | 7 | 635359.7 | 5733097.4 | 635353.4 | 5733094.6 | 6.3 | 2.8 |
|  |  | 8 | 635362.8 | 5733097.0 | 635353.4 | 5733094.6 | 9.4 | 2.4 |
|  |  | 9 | 635365.7 | 5733097.0 | 635353.4 | 5733094.6 | 12.3 | 2.4 |
|  | 2170 | 10 | 635550.8 | 5733425.1 | 635527.2 | 5733448.1 | 23.6 | -23.0 |
|  |  | 11 | 635556.5 | 5733424.8 | 635527.2 | 5733448.1 | 29.3 | -23.3 |
|  |  | 12 | 635551.2 | 5733425.6 | 635527.2 | 5733448.1 | 24.0 | -22.5 |
|  |  | 13 | 635563.2 | 5733434.1 | 635527.2 | 5733448.1 | 36.0 | -14.0 |
|  |  | 14 | 635566.8 | 5733434.8 | 635527.2 | 5733448.1 | 39.6 | -13.3 |
|  |  | 15 | 635548.6 | 5733438.3 | 635527.2 | 5733448.1 | 21.4 | -9.8 |
|  | 3170 | 16 | 635901.6 | 5733291.3 | 635893.1 | 5733287.8 | 8.5 | 3.5 |
|  |  | 17 | 635916.4 | 5733303.5 | 635893.1 | 5733287.8 | 23.3 | 15.7 |
|  |  | 18 | 635920.5 | 5733294.4 | 635893.1 | 5733287.8 | 27.4 | 6.6 |
|  |  | 19 | 635925.7 | 5733244.5 | 635893.1 | 5733287.8 | 32.6 | -43.3 |
|  |  | 20 | 635866.5 | 5733197.5 | 635893.1 | 5733287.8 | -26.6 | -90.3 |
|  |  | 21 | 635915.8 | 5733206.8 | 635893.1 | 5733287.8 | 22.7 | -81.0 |
|  |  | 22 | 635916.1 | 5733193.1 | 635893.1 | 5733287.8 | 23.0 | -94.7 |
|  |  | 23 | 635927.4 | 5733261.6 | 635893.1 | 5733287.8 | 34.3 | -26.2 |
|  |  | 24 | 635924.2 | 5733260.9 | 635893.1 | 5733287.8 | 31.1 | -26.9 |
|  | 2970 | 25 | 635804.9 | 5733306.0 | 635816.0 | 5733326.0 | -11.1 | -20.0 |
|  |  | 26 | 635810.4 | 5733318.8 | 635816.0 | 5733326.0 | -5.6 | -7.2 |
|  |  | 27 | 635802.2 | 5733322.2 | 635816.0 | 5733326.0 | -13.8 | -3.8 |
|  |  | 28 | 635803.9 | 5733336.3 | 635816.0 | 5733326.0 | -12.1 | 10.3 |
|  | 2770 | 29 | 635733.8 | 5733389.7 | 635742.0 | 5733360.0 | -8.2 | 29.7 |
|  |  | 30 | 635720.8 | 5733388.3 | 635742.0 | 5733360.0 | -21.2 | 28.3 |
|  |  | 31 | 635714.4 | 5733390.6 | 635742.0 | 5733360.0 | -27.6 | 30.6 |
|  |  | 32 | 635724.3 | 5733369.7 | 635742.0 | 5733360.0 | -17.7 | 9.7 |
|  |  | 33 | 635728.4 | 5733366.8 | 635742.0 | 5733360.0 | -13.6 | 6.8 |
|  |  | 34 | 635735.8 | 5733356.8 | 635742.0 | 5733360.0 | -6.2 | -3.2 |
|  |  | 35 | 635747.0 | 5733363.0 | 635742.0 | 5733360.0 | 5.0 | 3.0 |
|  |  | 36 | 635753.0 | 5733353.4 | 635742.0 | 5733360.0 | 11.0 | -6.6 |
|  | 2570 | 37 | 635681.2 | 5733374.4 | 635670.0 | 5733391.0 | 11.2 | -16.6 |
|  |  | 38 | 635682.7 | 5733373.9 | 635670.0 | 5733391.0 | 12.7 | -17.1 |
|  |  | 39 | 635683.4 | 5733375.1 | 635670.0 | 5733391.0 | 13.4 | -15.9 |
|  |  | 40 | 635683.7 | 5733374.3 | 635670.0 | 5733391.0 | 13.7 | -16.7 |
|  |  | 41 | 635681.6 | 5733370.8 | 635670.0 | 5733391.0 | 11.6 | -20.2 |
|  |  | 42 | 635683.5 | 5733372.3 | 635670.0 | 5733391.0 | 13.5 | -18.7 |
|  |  | 43 | 635687.6 | 5733371.7 | 635670.0 | 5733391.0 | 17.6 | -19.3 |
|  |  | 44 | 635685.8 | 5733373.6 | 635670.0 | 5733391.0 | 15.8 | -17.4 |
|  |  | 45 | 635684.4 | 5733384.9 | 635670.0 | 5733391.0 | 14.4 | -6.1 |
|  | 2370 | 46 | 635577.4 | 5733418.1 | 635597.0 | 5733421.0 | -19.6 | -2.9 |
|  |  | 47 | 635576.1 | 5733421.5 | 635597.0 | 5733421.0 | -20.9 | 0.5 |
|  |  | 48 | 635574.1 | 5733424.3 | 635597.0 | 5733421.0 | -22.9 | 3.3 |
|  |  | 49 | 635575.4 | 5733425.2 | 635597.0 | 5733421.0 | -21.6 | 4.2 |
|  |  | 50 | 635579.1 | 5733426.6 | 635597.0 | 5733421.0 | -17.9 | 5.6 |
|  |  | 51 | 635586.2 | 5733422.3 | 635597.0 | 5733421.0 | -10.8 | 1.3 |
|  |  | 52 | 635592.6 | 5733413.3 | 635597.0 | 5733421.0 | -4.4 | -7.7 |
|  |  | 53 | 635589.9 | 5733407.5 | 635597.0 | 5733421.0 | -7.1 | -13.5 |
|  |  | 54 | 635592.8 | 5733406.5 | 635597.0 | 5733421.0 | -4.2 | -14.5 |
|  | 2170 | 55 | 635530.6 | 5733439.2 | 635527.2 | 5733448.1 | 3.4 | -8.9 |
|  |  | 56 | 635529.2 | 5733442.0 | 635527.2 | 5733448.1 | 2.0 | -6.1 |
|  |  | 57 | 635531.9 | 5733451.0 | 635527.2 | 5733448.1 | 4.7 | 2.9 |
|  |  | 58 | 635531.6 | 5733453.4 | 635527.2 | 5733448.1 | 4.4 | 5.3 |
|  |  | 59 | 635528.0 | 5733454.4 | 635527.2 | 5733448.1 | 0.8 | 6.3 |
|  |  | 60 | 635527.1 | 5733454.5 | 635527.2 | 5733448.1 | -0.1 | 6.4 |
|  |  | 61 | 635524.8 | 5733454.3 | 635527.2 | 5733448.1 | -2.4 | 6.2 |
|  |  | 62 | 635523.7 | 5733448.7 | 635527.2 | 5733448.1 | -3.5 | 0.6 |
|  |  | 63 | 635515.9 | 5733447.0 | 635527.2 | 5733448.1 | -11.3 | -1.1 |
|  |  | 64 | 635513.8 | 5733439.7 | 635527.2 | 5733448.1 | -13.4 | -8.4 |
|  |  | 65 | 635520.3 | 5733436.0 | 635527.2 | 5733448.1 | -6.9 | -12.1 |
|  |  | 66 | 635522.0 | 5733432.8 | 635527.2 | 5733448.1 | -5.2 | -15.3 |
|  |  | 67 | 635529.1 | 5733434.2 | 635527.2 | 5733448.1 | 1.9 | -13.9 |
|  |  | 68 | 635528.4 | 5733446.5 | 635527.2 | 5733448.1 | 1.2 | -1.6 |
|  |  | 69 | 635525.4 | 5733464.4 | 635527.2 | 5733448.1 | -1.8 | 16.3 |
|  |  | 70 | 635517.8 | 5733454.3 | 635527.2 | 5733448.1 | -9.4 | 6.2 |
|  |  | 71 | 635515.2 | 5733446.8 | 635527.2 | 5733448.1 | -12.0 | -1.3 |
|  |  | 72 | 635516.9 | 5733445.7 | 635527.2 | 5733448.1 | -10.3 | -2.4 |
|  | 1970 | 73 | 635464.5 | 5733473.8 | 635459.0 | 5733471.0 | 5.5 | 2.8 |
|  |  | 74 | 635468.5 | 5733473.9 | 635459.0 | 5733471.0 | 9.5 | 2.9 |
|  |  | 75 | 635469.3 | 5733470.2 | 635459.0 | 5733471.0 | 10.3 | -0.8 |
|  |  | 76 | 635476.2 | 5733460.5 | 635459.0 | 5733471.0 | 17.2 | -10.5 |
|  |  | 77 | 635472.8 | 5733460.7 | 635459.0 | 5733471.0 | 13.8 | -10.3 |
|  |  | 78 | 635470.1 | 5733459.1 | 635459.0 | 5733471.0 | 11.1 | -11.9 |
|  |  | 79 | 635468.1 | 5733460.2 | 635459.0 | 5733471.0 | 9.1 | -10.8 |
|  |  | 80 | 635466.0 | 5733461.7 | 635459.0 | 5733471.0 | 7.0 | -9.3 |
|  |  | 81 | 635467.7 | 5733466.4 | 635459.0 | 5733471.0 | 8.7 | -4.6 |
|  | 1770 | 82 | 635396.3 | 5733448.7 | 635397.0 | 5733440.0 | -0.7 | 8.7 |
|  |  | 83 | 635385.7 | 5733436.5 | 635397.0 | 5733440.0 | -11.3 | -3.5 |
|  |  | 84 | 635379.9 | 5733431.1 | 635397.0 | 5733440.0 | -17.1 | -8.9 |
|  |  | 85 | 635381.5 | 5733412.6 | 635397.0 | 5733440.0 | -15.5 | -27.4 |
|  |  | 86 | 635379.4 | 5733416.8 | 635397.0 | 5733440.0 | -17.6 | -23.2 |
|  |  | 87 | 635382.0 | 5733421.1 | 635397.0 | 5733440.0 | -15.0 | -18.9 |
|  |  | 88 | 635374.5 | 5733440.9 | 635397.0 | 5733440.0 | -22.5 | 0.9 |
|  |  | 89 | 635388.5 | 5733453.1 | 635397.0 | 5733440.0 | -8.5 | 13.1 |
|  |  | 90 | 635380.4 | 5733441.8 | 635397.0 | 5733440.0 | -16.6 | 1.8 |
|  |  | 91 | 635395.2 | 5733418.1 | 635397.0 | 5733440.0 | -1.8 | -21.9 |
|  | 1570 | 92 | 635355.1 | 5733336.4 | 635362.0 | 5733342.0 | -6.9 | -5.6 |
|  |  | 93 | 635355.3 | 5733341.3 | 635362.0 | 5733342.0 | -6.7 | -0.7 |
|  |  | 94 | 635355.7 | 5733344.1 | 635362.0 | 5733342.0 | -6.3 | 2.1 |
|  |  | 95 | 635350.4 | 5733349.1 | 635362.0 | 5733342.0 | -11.6 | 7.1 |
|  |  | 96 | 635350.6 | 5733340.5 | 635362.0 | 5733342.0 | -11.4 | -1.5 |
|  |  | 97 | 635350.7 | 5733330.4 | 635362.0 | 5733342.0 | -11.3 | -11.6 |
|  |  | 98 | 635358.1 | 5733338.7 | 635362.0 | 5733342.0 | -3.9 | -3.3 |
|  |  | 99 | 635357.9 | 5733342.2 | 635362.0 | 5733342.0 | -4.1 | 0.2 |
|  |  | 100 | 635354.9 | 5733337.7 | 635362.0 | 5733342.0 | -7.1 | -4.3 |
|  |  | 101 | 635362.6 | 5733340.3 | 635362.0 | 5733342.0 | 0.6 | -1.7 |
|  | 1370 | 102 | 635324.2 | 5733190.8 | 635347.0 | 5733205.0 | -22.8 | -14.2 |
|  |  | 103 | 635347.1 | 5733216.2 | 635347.0 | 5733205.0 | 0.1 | 11.2 |
|  |  | 104 | 635339.5 | 5733197.4 | 635347.0 | 5733205.0 | -7.5 | -7.6 |
|  |  | 105 | 635341.4 | 5733191.2 | 635347.0 | 5733205.0 | -5.6 | -13.8 |
|  |  | 106 | 635326.7 | 5733187.7 | 635347.0 | 5733205.0 | -20.3 | -17.3 |
|  |  | 107 | 635413.2 | 5733282.3 | 635347.0 | 5733205.0 | 66.2 | 77.3 |
|  |  | 108 | 635327.3 | 5733204.4 | 635347.0 | 5733205.0 | -19.7 | -0.6 |
|  |  | 109 | 635342.3 | 5733211.9 | 635347.0 | 5733205.0 | -4.7 | 6.9 |
|  |  | 110 | 635341.8 | 5733202.8 | 635347.0 | 5733205.0 | -5.2 | -2.2 |
|  | 1250 | 111 | 635342.4 | 5733082.3 | 635353.4 | 5733094.6 | -11.0 | -12.3 |
|  |  | 112 | 635345.3 | 5733078.3 | 635353.4 | 5733094.6 | -8.1 | -16.3 |
|  |  | 113 | 635363.6 | 5733079.1 | 635353.4 | 5733094.6 | 10.2 | -15.5 |
|  |  | 114 | 635363.2 | 5733069.4 | 635353.4 | 5733094.6 | 9.8 | -25.2 |
|  |  | 115 | 635366.4 | 5733072.7 | 635353.4 | 5733094.6 | 13.0 | -21.9 |
|  |  | 116 | 635362.3 | 5733075.7 | 635353.4 | 5733094.6 | 8.9 | -18.9 |
|  |  | 117 | 635357.0 | 5733102.1 | 635353.4 | 5733094.6 | 3.6 | 7.5 |
|  |  | 118 | 635352.6 | 5733101.3 | 635353.4 | 5733094.6 | -0.8 | 6.7 |
|  |  | 119 | 635347.7 | 5733101.9 | 635353.4 | 5733094.6 | -5.7 | 7.3 |
|  |  | 120 | 635348.6 | 5733112.2 | 635353.4 | 5733094.6 | -4.8 | 17.6 |
|  |  | 121 | 635351.2 | 5733100.0 | 635353.4 | 5733094.6 | -2.2 | 5.4 |
|  | Mean Value |  |  |  |  |  | 2.8 | -6.0 |
|  | Std Dev |  |  |  |  |  | 17.2 | 19.5 |

A2	Wellbore Trajectory Summary and Downhole Geophone Positions

| Station | MD | Incl | Azim | TVD | VSec | N/-S | E/-W | DLS | Northing | Easting |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | (m) | (°) | (°) | (m) | (m) | (m) | (m) | (°/30m) | (m) | (m) |
| Tie-In | 0.0 | 0.00 | 0.00 | 0.0 | 0.0 | 0.00 | 0.00 | 0.00 | 5732873 | 635355 |
|  | 421.0 | 0.00 | 118.67 | 421.0 | 0.0 | 0.00 | 0.00 | 0.00 | 5732873 | 635355 |
|  | 424.4 | 0.44 | 118.67 | 424.4 | 0.0 | -0.01 | 0.01 | 3.88 | 5732873 | 635355 |
|  | 433.9 | 0.67 | 118.67 | 433.9 | 0.1 | -0.05 | 0.09 | 0.73 | 5732873 | 635355 |
|  | 443.6 | 1.22 | 118.67 | 443.6 | 0.1 | -0.13 | 0.23 | 1.70 | 5732873 | 635355 |
|  | 453.3 | 1.40 | 118.67 | 453.3 | 0.2 | -0.23 | 0.43 | 0.56 | 5732873 | 635356 |
|  | 463.0 | 1.35 | 118.67 | 463.0 | 0.3 | -0.35 | 0.63 | 0.15 | 5732873 | 635356 |
|  | 472.6 | 1.94 | 118.67 | 472.6 | 0.4 | -0.48 | 0.87 | 1.84 | 5732873 | 635356 |
|  | 482.3 | 1.67 | 118.67 | 482.3 | 0.6 | -0.62 | 1.14 | 0.84 | 5732873 | 635356 |
|  | 487.0 | 1.35 | 118.67 | 487.0 | 0.6 | -0.68 | 1.25 | 2.04 | 5732873 | 635356 |
|  | 491.1 | 1.06 | 118.67 | 491.1 | 0.7 | -0.72 | 1.33 | 2.12 | 5732873 | 635356 |
|  | 519.9 | 0.83 | 118.67 | 519.9 | 0.9 | -0.95 | 1.74 | 0.24 | 5732872 | 635357 |
|  | 548.9 | 0.85 | 112.10 | 548.9 | 1.1 | -1.13 | 2.13 | 0.10 | 5732872 | 635357 |
|  | 578.0 | 0.76 | 117.52 | 578.0 | 1.3 | -1.30 | 2.50 | 0.12 | 5732872 | 635358 |
|  | 607.0 | 0.44 | 120.87 | 607.0 | 1.4 | -1.45 | 2.76 | 0.33 | 5732872 | 635358 |
|  | 636.1 | 0.66 | 122.56 | 636.1 | 1.5 | -1.60 | 3.00 | 0.23 | 5732872 | 635358 |
|  | 650.0 | 0.56 | 118.40 | 650.0 | 1.6 | -1.67 | 3.13 | 0.24 | 5732872 | 635358 |
|  | 689.1 | 1.26 | 120.18 | 689.1 | 1.8 | -1.98 | 3.67 | 0.54 | 5732871 | 635359 |
|  | 719.2 | 1.50 | 65.10 | 719.2 | 2.3 | -1.98 | 4.31 | 1.29 | 5732871 | 635359 |
|  | 748.8 | 3.53 | 17.27 | 748.7 | 3.4 | -0.95 | 4.93 | 2.79 | 5732872 | 635360 |
|  | 807.9 | 6.57 | 13.29 | 807.6 | 7.5 | 4.08 | 6.25 | 1.55 | 5732877 | 635361 |
|  | 838.2 | 9.51 | 11.16 | 837.6 | 10.6 | 8.23 | 7.13 | 2.93 | 5732882 | 635362 |
|  | 865.4 | 12.94 | 8.40 | 864.3 | 14.4 | 13.45 | 8.01 | 3.83 | 5732887 | 635363 |
|  | 896.2 | 16.67 | 3.22 | 894.1 | 19.6 | 21.28 | 8.77 | 3.85 | 5732895 | 635364 |
|  | 924.9 | 20.03 | 0.25 | 921.3 | 25.1 | 30.29 | 9.02 | 3.65 | 5732904 | 635364 |
|  | 951.8 | 23.17 | 359.15 | 946.3 | 30.9 | 40.20 | 8.96 | 3.53 | 5732914 | 635364 |
|  | 981.6 | 25.16 | 358.42 | 973.4 | 37.8 | 52.37 | 8.70 | 2.03 | 5732926 | 635364 |
|  | 1009.8 | 28.29 | 359.43 | 998.6 | 45.0 | 65.06 | 8.47 | 3.36 | 5732938 | 635364 |
|  | 1038.9 | 31.04 | 0.21 | 1023.9 | 53.4 | 79.45 | 8.43 | 2.86 | 5732953 | 635364 |
|  | 1067.1 | 33.93 | 359.33 | 1047.8 | 62.3 | 94.63 | 8.36 | 3.11 | 5732968 | 635363 |
|  | 1096.2 | 36.75 | 358.31 | 1071.4 | 71.9 | 111.42 | 8.01 | 2.98 | 5732985 | 635363 |
|  | 1127.1 | 39.69 | 357.70 | 1095.7 | 82.5 | 130.51 | 7.34 | 2.88 | 5733004 | 635362 |
|  | 1155.9 | 43.87 | 354.25 | 1117.2 | 92.7 | 149.66 | 5.97 | 4.96 | 5733023 | 635361 |
|  | 1183.5 | 47.66 | 352.36 | 1136.5 | 102.3 | 169.30 | 3.65 | 4.37 | 5733043 | 635359 |
|  | 1212.1 | 51.37 | 354.08 | 1155.0 | 112.9 | 190.90 | 1.10 | 4.13 | 5733064 | 635356 |
|  | 1242.1 | 54.60 | 354.94 | 1173.1 | 125.0 | 214.73 | -1.19 | 3.30 | 5733088 | 635354 |
| Level 11 | 1250.0 |  |  | 1177.5 |  |  |  |  | 5733095 | 635353 |
|  | 1271.8 | 57.80 | 355.55 | 1189.6 | 137.8 | 239.34 | -3.24 | 3.27 | 5733113 | 635352 |
|  | 1289.2 | 60.26 | 355.87 | 1198.5 | 145.6 | 254.19 | -4.35 | 4.28 | 5733128 | 635351 |
|  | 1305.6 | 58.77 | 355.43 | 1206.9 | 153.1 | 268.31 | -5.42 | 2.81 | 5733142 | 635350 |
|  | 1316.8 | 56.98 | 356.26 | 1212.8 | 158.0 | 277.74 | -6.11 | 5.17 | 5733151 | 635349 |
|  | 1326.3 | 56.12 | 356.96 | 1218.1 | 162.3 | 285.68 | -6.58 | 3.27 | 5733159 | 635349 |
|  | 1347.0 | 56.53 | 357.77 | 1229.5 | 171.8 | 302.87 | -7.37 | 1.14 | 5733176 | 635348 |
|  | 1363.1 | 56.49 | 358.75 | 1238.4 | 179.3 | 316.31 | -7.78 | 1.52 | 5733190 | 635347 |
| Level 10 | 1370.0 |  |  | 1242.4 |  |  |  |  | 5733195 | 635347 |
|  | 1390.8 | 54.23 | 0.22 | 1254.2 | 192.5 | 339.11 | -7.99 | 2.77 | 5733212 | 635347 |
|  | 1423.5 | 51.09 | 2.35 | 1274.0 | 208.2 | 365.05 | -7.42 | 3.28 | 5733238 | 635348 |
|  | 1451.7 | 48.62 | 4.89 | 1292.2 | 222.0 | 386.61 | -6.06 | 3.33 | 5733260 | 635349 |
|  | 1477.9 | 46.73 | 7.60 | 1309.9 | 235.0 | 405.88 | -3.96 | 3.15 | 5733279 | 635351 |
|  | 1509.0 | 44.79 | 9.23 | 1331.5 | 250.5 | 427.87 | -0.71 | 2.19 | 5733301 | 635354 |
|  | 1536.5 | 43.39 | 10.65 | 1351.3 | 264.3 | 446.74 | 2.59 | 1.87 | 5733320 | 635358 |
|  | 1565.1 | 40.78 | 12.05 | 1372.5 | 278.3 | 465.55 | 6.36 | 2.91 | 5733339 | 635361 |
| Level 9 | 1570.0 |  |  | 1376.3 |  |  |  |  | 5733342 | 635362 |
|  | 1593.9 | 37.97 | 12.26 | 1394.8 | 291.9 | 483.39 | 10.20 | 2.93 | 5733357 | 635365 |
|  | 1622.7 | 36.16 | 13.24 | 1417.7 | 304.9 | 500.29 | 14.03 | 1.99 | 5733374 | 635369 |
|  | 1653.6 | 32.70 | 17.26 | 1443.2 | 318.5 | 517.17 | 18.60 | 4.01 | 5733390 | 635374 |
|  | 1684.0 | 31.03 | 21.55 | 1469.1 | 331.7 | 532.31 | 23.92 | 2.77 | 5733406 | 635379 |
|  | 1711.3 | 28.73 | 25.70 | 1492.8 | 343.4 | 544.77 | 29.35 | 3.40 | 5733418 | 635384 |
|  | 1740.5 | 26.25 | 29.79 | 1518.6 | 355.5 | 556.68 | 35.59 | 3.21 | 5733430 | 635391 |
|  | 1769.0 | 24.22 | 34.87 | 1544.4 | 366.8 | 566.97 | 42.08 | 3.12 | 5733440 | 635397 |
| Level 8 | 1770.0 |  |  | 1545.3 |  |  |  |  | 5733441 | 635397 |
|  | 1800.1 | 22.39 | 42.33 | 1573.0 | 378.6 | 576.57 | 49.71 | 3.35 | 5733450 | 635405 |
|  | 1831.8 | 21.60 | 52.57 | 1602.4 | 390.3 | 584.58 | 58.40 | 3.70 | 5733458 | 635413 |
|  | 1855.3 | 20.88 | 59.61 | 1624.3 | 398.8 | 589.34 | 65.47 | 3.37 | 5733463 | 635421 |
|  | 1883.6 | 20.21 | 68.69 | 1650.8 | 408.6 | 593.66 | 74.36 | 3.45 | 5733467 | 635429 |
|  | 1913.2 | 20.52 | 77.41 | 1678.6 | 418.3 | 596.66 | 84.21 | 3.08 | 5733470 | 635439 |
|  | 1942.3 | 20.68 | 85.05 | 1705.8 | 427.4 | 598.21 | 94.30 | 2.78 | 5733472 | 635449 |
| Level 7 | 1970.0 |  |  | 1731.7 |  |  |  |  | 5733471 | 635459 |
|  | 1970.9 | 21.09 | 95.65 | 1732.5 | 435.6 | 598.14 | 104.45 | 3.98 | 5733471 | 635460 |
|  | 1999.7 | 21.50 | 104.27 | 1759.4 | 442.8 | 596.33 | 114.72 | 3.29 | 5733470 | 635470 |
|  | 2026.2 | 20.95 | 112.15 | 1784.1 | 448.4 | 593.35 | 123.82 | 3.29 | 5733467 | 635479 |
|  | 2054.0 | 20.92 | 111.69 | 1810.1 | 453.7 | 589.63 | 133.05 | 0.18 | 5733463 | 635488 |
|  | 2081.0 | 20.87 | 110.40 | 1835.3 | 459.0 | 586.18 | 142.03 | 0.51 | 5733459 | 635497 |
|  | 2106.2 | 21.51 | 111.03 | 1858.8 | 464.0 | 582.95 | 150.55 | 0.81 | 5733456 | 635506 |
|  | 2136.2 | 21.18 | 111.14 | 1886.7 | 469.9 | 579.03 | 160.73 | 0.33 | 5733452 | 635516 |
|  | 2164.5 | 21.12 | 110.91 | 1913.1 | 475.5 | 575.36 | 170.27 | 0.11 | 5733449 | 635525 |
| Level 6 Repeat | 2170.0 |  |  | 1918.2 |  |  |  |  | 5733448 | 635527 |
|  | 2194.4 | 21.18 | 110.70 | 1941.0 | 481.4 | 571.53 | 180.35 | 0.10 | 5733445 | 635535 |
|  | 2221.9 | 21.46 | 110.57 | 1966.6 | 486.9 | 568.00 | 189.72 | 0.31 | 5733441 | 635545 |
|  | 2252.8 | 21.91 | 110.26 | 1995.3 | 493.2 | 564.02 | 200.41 | 0.45 | 5733437 | 635555 |
|  | 2281.7 | 22.15 | 110.72 | 2022.1 | 499.2 | 560.23 | 210.55 | 0.31 | 5733434 | 635566 |
|  | 2311.9 | 22.79 | 111.57 | 2050.0 | 505.5 | 556.07 | 221.31 | 0.71 | 5733429 | 635576 |
|  | 2340.6 | 23.16 | 111.09 | 2076.4 | 511.6 | 552.00 | 231.74 | 0.43 | 5733425 | 635587 |
| Level 5 | 2370.0 |  |  | 2103.5 |  |  |  |  | 5733421 | 635598 |
|  | 2370.6 | 23.11 | 111.25 | 2104.0 | 518.0 | 547.73 | 242.76 | 0.08 | 5733421 | 635598 |
|  | 2402.2 | 22.82 | 112.19 | 2133.1 | 524.6 | 543.17 | 254.20 | 0.44 | 5733416 | 635609 |
|  | 2427.7 | 23.03 | 112.23 | 2156.6 | 529.8 | 539.42 | 263.40 | 0.25 | 5733413 | 635618 |
|  | 2457.1 | 23.70 | 111.53 | 2183.6 | 536.0 | 535.08 | 274.21 | 0.74 | 5733408 | 635629 |
|  | 2485.1 | 23.95 | 112.07 | 2209.2 | 542.1 | 530.88 | 284.71 | 0.36 | 5733404 | 635640 |
|  | 2514.4 | 23.28 | 112.24 | 2236.1 | 548.3 | 526.44 | 295.60 | 0.69 | 5733400 | 635651 |
|  | 2544.3 | 22.77 | 112.52 | 2263.5 | 554.4 | 522.00 | 306.39 | 0.52 | 5733395 | 635661 |
| Level 4 | 2570.0 |  |  | 2287.3 |  |  |  |  | 5733392 | 635671 |
|  | 2572.0 | 22.48 | 112.64 | 2289.2 | 560.0 | 517.90 | 316.26 | 0.32 | 5733391 | 635671 |
|  | 2603.6 | 23.20 | 113.48 | 2318.2 | 566.3 | 513.10 | 327.53 | 0.75 | 5733386 | 635683 |
|  | 2632.5 | 23.44 | 113.12 | 2344.8 | 572.2 | 508.57 | 338.04 | 0.29 | 5733382 | 635693 |
|  | 2662.7 | 23.47 | 114.16 | 2372.5 | 578.2 | 503.75 | 349.05 | 0.41 | 5733377 | 635704 |
|  | 2687.9 | 22.78 | 113.51 | 2395.7 | 583.2 | 499.75 | 358.11 | 0.88 | 5733373 | 635713 |
|  | 2717.7 | 22.51 | 113.43 | 2423.2 | 589.1 | 495.18 | 368.63 | 0.27 | 5733368 | 635724 |
|  | 2747.3 | 23.23 | 113.94 | 2450.4 | 594.9 | 490.57 | 379.15 | 0.76 | 5733364 | 635734 |
| Level 3 | 2770.0 |  |  | 2471.3 |  |  |  |  | 5733360 | 635742 |
|  | 2776.9 | 23.86 | 114.08 | 2477.6 | 600.8 | 485.75 | 389.96 | 0.64 | 5733359 | 635745 |
|  | 2806.1 | 24.16 | 114.43 | 2504.2 | 606.7 | 480.88 | 400.78 | 0.34 | 5733354 | 635756 |
|  | 2833.9 | 24.08 | 115.09 | 2529.6 | 612.3 | 476.11 | 411.10 | 0.30 | 5733349 | 635766 |
|  | 2865.3 | 24.06 | 114.92 | 2558.3 | 618.5 | 470.71 | 422.70 | 0.07 | 5733344 | 635778 |
|  | 2891.6 | 24.25 | 114.71 | 2582.3 | 623.7 | 466.19 | 432.47 | 0.24 | 5733340 | 635787 |
|  | 2921.0 | 24.48 | 115.83 | 2609.1 | 629.6 | 461.00 | 443.45 | 0.53 | 5733334 | 635798 |
|  | 2950.4 | 24.46 | 114.98 | 2635.9 | 635.4 | 455.78 | 454.45 | 0.36 | 5733329 | 635809 |
| Level 2 | 2970.0 |  |  | 2653.7 |  |  |  |  | 5733326 | 635817 |
|  | 2979.9 | 24.69 | 116.16 | 2662.7 | 641.3 | 450.48 | 465.52 | 0.55 | 5733324 | 635821 |
|  | 3005.7 | 24.88 | 115.86 | 2686.1 | 646.4 | 445.73 | 475.25 | 0.26 | 5733319 | 635830 |
|  | 3069.3 | 25.26 | 116.84 | 2743.7 | 658.9 | 433.79 | 499.37 | 0.27 | 5733307 | 635854 |
|  | 3096.4 | 25.29 | 116.36 | 2768.2 | 664.3 | 428.59 | 509.74 | 0.23 | 5733302 | 635865 |
|  | 3125.9 | 25.43 | 116.57 | 2794.8 | 670.1 | 422.97 | 521.03 | 0.17 | 5733296 | 635876 |
|  | 3154.2 | 25.60 | 117.00 | 2820.4 | 675.7 | 417.48 | 531.91 | 0.27 | 5733291 | 635887 |
| Level 1 | 3170.0 |  |  | 2834.6 |  |  |  |  | 5733288 | 635893 |
|  | 3179.9 | 25.62 | 117.24 | 2843.6 | 680.7 | 412.40 | 541.83 | 0.12 | 5733286 | 635897 |
|  | 3210.0 | 26.05 | 116.45 | 2870.7 | 686.7 | 406.48 | 553.53 | 0.55 | 5733280 | 635909 |
|  | 3241.7 | 26.17 | 116.33 | 2899.1 | 693.2 | 400.28 | 566.02 | 0.12 | 5733274 | 635921 |
|  | 3255.2 | 26.29 | 116.26 | 2911.2 | 696.0 | 397.65 | 571.35 | 0.28 | 5733271 | 635926 |
|  | 3272.0 | 26.35 | 116.20 | 2926.3 | 699.5 | 394.35 | 578.04 | 0.12 | 5733268 | 635933 |