LAKES OIL Ltd

DAILY DRILLING REPORT

| WELL : | WOMBAT-1 | REPORT No. : | 24 | DFS: | 24 | DATE : | 12 Jan 2004 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 2400 DEPTH : | 1745m PBTD | LAST DEPTH : | 1745m | 24 HR PROGRESS : | 0m | PTD : | 1800m |
| TOTAL FUEL : |  | FUEL USAGE : |  | DAYCOST : $ | 91,838 | CUM. COST : $ | 1,467,636 |
| 0600 OPS : | RIH with 154mm bit |
| Next 24 hr OPS: | Displace to new mud. Test BOP’s. Drill out shoe. Drill 154mm hole. |
| Site Personnel: | Peter Dwyer – Supervisor. |

| BIT INFORMATION |  | OPS BREAKDOWN |  | MUD PROPERTIES |
| --- | --- | --- | --- | --- |
| Bit Number | 6 |  |  | Drilling |  |  | Density | 1.09 | S.G. |
| Size (mm) | 154 |  |  | Tripping | 1.5 |  | Viscosity | 50 | Sec |
| Make | Security |  |  | Surveys |  |  | Water Loss |  | Cc |
| Type | XS4 |  |  | Reaming/work tight hole |  |  | pH | 7.5 | Strip |
| IADC Code | 2.1.7 |  |  | Testing/tools |  |  | Filter Cake |  | 32 nd |
| Serial Number | 10408404 |  |  | Circulate Sample |  |  | PV / YP | 13/31 | Cp/lb/100’ |
| Nozzles (32) | 2x10, 1x9 |  |  | Casing |  |  | Gels | 1/3 | S/m |
| Depth in (m) | 1767 |  |  | Cementing |  |  | Sand |  | % Vol |
| Depth out (m) |  |  |  | Wireline |  |  | Solids |  | % Vol |
| Total Metres |  |  |  | Circulate & Condition |  |  | Oil |  | % Vol |
| Hours |  |  |  | Rig Service/slip & cut |  |  | K+ | 75,656 | Mg/l |
| WOB (kg) |  |  |  | Test BOP's | 2.5 |  | Chlorides |  | Mg/l |
| RPM |  |  |  | Repairs |  |  | PHPA |  |  |
| Condition |  |  |  | Drill Out |  |  | ALC - 50 |  |  |
| Impact Force |  |  |  | Wait On Cement |  |  | Daily Cost $ | 10,565 |
| Jet Velocity |  |  |  | Nipple Up BOPs | 13.0 |  | Cum Cost $ | 96,524 |
| B.H.A.: | Bit, boot basket, bit sub, 2 x 4-3/4” DC’s, stabilizer, 20 x 4-3/4” DC’s, drilling jars, 2 x 4-3/4” DC’s |
| HOURLY OPERATIONS SUMMARY (0000 – 2400) |  | SURVEYS |  | CHEMICALS USED |
| From | To | Operation |  |  | ° at |  | m |  | Type | Amount |
| 0700 | 0800 | Re-commence day rate operations. |  |  | ° at |  | m |  | AMC PAC-R | 9 |
|  |  | Test 244mm casing/178mm liner to 19,000kPa. |  |  | ° at |  | m |  | Sodium Sulphite |  |
| 0800 | 1100 | Rig out BOP’s |  |  | ° at |  | m |  | Barite |  |
| 1100 | 1300 | Install wellhead B section. Test seals to 19,000kPa. |  |  | ° at |  | m |  | Drillzan | 7 |
| 1300 | 2100 | Install BOP’s. Test |  |  | ° at |  | m |  | KCl Tech | 354 |
| 2100 | 2230 | Function and pressure test BOP’s to 19,000kPa. |  |  | ° at |  | m |  | PHPA/Soda Ash | 1/0 |
| 2230 | 2400 | Pick up 154mm BHA. |  |  | ° at |  | m |  | Caustic Soda |  |
|  |  |  |  | PUMP 1 |  | PUMP 2 |
|  |  |  |  | Liner | 140 | mm |  | Liner | 140 | mm |
|  |  |  |  | Pressure |  | kPa |  | Pressure |  | KPa |
|  |  |  |  | A.V. DP |  | m/min |  | A.V. DP |  | m/min |
|  |  |  |  | A.V. DC |  | m/min |  | A.V. DC |  | m/min |
|  |  |  |  | SPM |  |  | SPM |  |
|  |  |  |  | LPM |  |  | LPM |  |
|  |  |  |  | CEMENT DATA |  | LAST CASING |
|  |  |  |  | Sacks | 335 |  | Size | 178 | mm |
|  |  |  |  | Class | A |  | Weight | 38.7 | Kg/m |
|  |  |  |  | % |  |  |  | Grade | K55 |  |
|  |  |  |  | % |  |  |  | Connection | BTC |  |
|  |  |  |  | % |  |  |  | Joints | 48 |  |
|  |  |  |  | % |  |  |  | Length | 561 | m |
|  |  |  |  | Av. Wt | 15.8ppg |  | Shoe | 1757 | m |

,66