LAKES OIL Ltd

DAILY DRILLING REPORT

| WELL : | WOMBAT-1 | REPORT No. : | 34 | DFS: | 34 | DATE : | 22 Jan 2004 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 2400 DEPTH : | 1977mPBTD | LAST DEPTH : | 1990m | 24 HR PROGRESS : | 0m | PTD : | 2000m |
| TOTAL FUEL : |  | FUEL USAGE : |  | DAYCOST : $ | 55,003 | CUM. COST : $ | 1,874,314 |
| 0600 OPS : | Preparing brine and slimhole tubulars |
| Next 24 hr OPS: | Run in hole with 114mm scraper. Run CBL |
| Site Personnel: | Peter Dwyer – Supervisor. |

| BIT INFORMATION |  | OPS BREAKDOWN |  | MUD PROPERTIES |
| --- | --- | --- | --- | --- |
| Bit Number |  |  |  | Drilling | 5.5 |  | Density | 1.12 | S.G. |
| Size (mm) |  |  |  | Tripping |  |  | Viscosity | 34 | Sec |
| Make |  |  |  | Surveys |  |  | Water Loss | 6.5 | Cc |
| Type |  |  |  | Reaming/work tight hole |  |  | pH | 9.0 | Strip |
| IADC Code |  |  |  | Testing/tools |  |  | Filter Cake | 1 | 32 nd |
| Serial Number |  |  |  | Circulate Sample |  |  | PV / YP | 8/10 | Cp/lb/100’ |
| Nozzles (32) |  |  |  | Casing | 17.5 |  | Gels | ‘1/2 | S/m |
| Depth in (m) |  |  |  | Cementing | 1.0 |  | Sand | Tr | % Vol |
| Depth out (m) |  |  |  | Wireline |  |  | Solids | 2.9 | % Vol |
| Total Metres |  |  |  | Circulate & Condition |  |  | Oil |  | % Vol |
| Hours |  |  |  | Rig Service/slip & cut |  |  | K+ | 45,934 | Mg/l |
| WOB (kg) |  |  |  | Test BOP's |  |  | Chlorides | 48,000 | Mg/l |
| RPM |  |  |  | Repairs |  |  | PHPA | 0.3 |  |
| Condition |  |  |  | Coring |  |  | ALC - 50 |  |  |
| Impact Force |  |  |  | Wait On Cement |  |  | Daily Cost $ | 0 |
| Jet Velocity |  |  |  | Nipple Up BOPs |  |  | Cum Cost $ | 110,929 |
| B.H.A.: |  |
| HOURLY OPERATIONS SUMMARY (0000 – 2400) |  | SURVEYS |  | CHEMICALS USED |
| From | To | Operation |  |  | ° at |  | m |  | Type | Amount |
| 0000 | 0230 | POH with 156mm bit |  |  | ° at |  | m |  | AMC PAC-R |  |
| 0230 | 0730 | Rig up and run 26 jts 114mm 11.6# K55 BTC liner |  |  | ° at |  | m |  | Sodium Sulphite |  |
| 0730 | 0800 | Make up liner hanger and circulate liner volume |  |  | ° at |  | m |  | Barite |  |
| 0800 | 1300 | RIH with landing string |  |  | ° at |  | m |  | Drillzan |  |
| 1300 | 1400 | Make up head and circulate casing |  |  | ° at |  | m |  | KCl Tech |  |
| 1400 | 1430 | Set liner with 1200psi. Shear ballseat with 2200psi |  |  | ° at |  | m |  | PHPA/Soda Ash |  |
| 1430 | 1530 | Mix and pump 122sx 1.90 SG cement. Displace with |  |  | ° at |  | m |  | Caustic Soda |  |
|  |  | Mud. Bump plug with 1500psi. Check floats |  |  |  |  |
| 1530 | 1600 | Set packer and reverse out cement XS |  | PUMP 1 |  | PUMP 2 |
| 1600 | 1700 | Rig down surface equipment |  | Liner | 140 | mm |  | Liner | 140 | mm |
| 1700 | 2030 | POH |  | Pressure |  | kPa |  | Pressure |  | KPa |
| 2030 | 2100 | Lay down liner running tool |  | A.V. DP |  | m/min |  | A.V. DP |  | m/min |
| 2100 | 2400 | Pick up 178mm scraper. RIH |  | A.V. DC |  | m/min |  | A.V. DC |  | m/min |
|  |  |  |  | SPM |  |  | SPM |  |
|  |  |  |  | LPM |  |  | LPM |  |
|  |  |  |  | CEMENT DATA |  | LAST CASING |
|  |  |  |  | Sacks | 335 |  | Size | 178 | mm |
|  |  |  |  | Class | A |  | Weight | 38.7 | Kg/m |
|  |  |  |  | % |  |  |  | Grade | K55 |  |
|  |  |  |  | % |  |  |  | Connection | BTC |  |
|  |  |  |  | % |  |  |  | Joints | 48 |  |
|  |  |  |  | % |  |  |  | Length | 561 | m |
|  |  |  |  | Av. Wt | 15.8ppg |  | Shoe | 1757 | m |

,66