# APPENDIX 3 - SENSOR OFFSETS

## P2/94 Node Naming Conventions

Each sensor is referenced to a platform.  The following Alpha numeric codes are used to refer to the platform :

Vessel	V#	# is  an identifying number

Gun Array	G##	## is  an identifying number incrementing from stbd to port

Streamer	S##	## is  an identifying number incrementing from stbd to port

Tailbuoy	T##	## is  an identifying number incrementing from stbd to port

The sensors are identified by the platform, then by the system type, and finally by an identifying number :

Acoustic	T##	## is  an identifying number incrementing from front to back

dGPS	G#	# is  an identifying number incrementing from front to back

Echosounder	E#	# is  an identifying number incrementing from front to back

Gun String	S#	# is  an identifying number incrementing from front to back

Gyro	GY#	# is  an identifying number incrementing from front to back

Laser	L#	# is  an identifying number incrementing from front to back

Pitch/Roll	PR#	# is  an identifying number incrementing from front to back

rGPS	R##	## is  an id number incrementing from front to back

Water Speed	WS#	# is  an identifying number incrementing from front to back

Velocimeter	V#	# is  an identifying number incrementing from front to back

User Defined	UD##	## is  an id number incrementing from front to back

For example T04R01 refers to the rGPS sensor on tailbuoy 4

Exceptions are the compass and depth sensors on the streamers.  These are referenced by the following convention

VC##	where V is  the vessel number, C by the streamer number, and ## by an identifying number incrementing from front to back

For example 1608 refers to the 8th compass/depth sensor on vessel 1, cable 6

## Vessel And Antennae Offsets

Fore (+)	Stbd (+)	Height (+)

Navigation Reference Point (NRP V1)	0.00	0.00	0.00

[ Primary GPS Antenna at sea level ]

Primary GPS Antenna (V1G1-3)	0.00	0.00	20.29

rGPS Antenna (P2/94 offset, V1R01)	0.00	0.00	0.00* (20.29)

Fanbeam Laser Head (V1L1)	0.00	0.00	18.73

Fathometer	10.71	1.59	-5.94

DigiCOURSE Hull Transducer (V1T01)	-1.51	0.34	-5.60

Gyrocompass 1 (V1GY1)	-3.30	-1.80	-1.80

Gyrocompass 2 (V1GY2)	-3.30	0.60	-1.80

NB : 	All offsets are in metres and are referenced to the NRP

*Posnet antenna heights are all set to MSL in Spectra as the ranges are slant corrected within the Posnet system

## Tailbuoy (Posnet rGPS and Acoustic Unit) Offsets

TRP Dist from CRP	Tailbuoy Sensor Offsets from TRP

Cable	TB ID	Fore (+)	Height (+)	Acoustic ID	Height (+)	rGPS ID	Height (+)

S01	T01	-4732.85	6.00	S01T08	-1.50	T01R01	0.00* (1.80)

S02	T02	-4732.85	6.00	S02T08	-1.50	T02R01	0.00* (1.80)

S03	T03	-4732.85	6.00	S03T08	-1.50	T03R01	0.00* (1.80)

S04	T04	-4732.85	6.00	S04T08	-1.50	T04R01	0.00* (1.80)

S05	T05	-4732.85	6.00	S05T08	-1.50	T05R01	0.00* (1.80)

S06	T06	-4732.85	6.00	S06T08	-1.50	T06R01	0.00* (1.80)

NB :	All other offsets not given above are zero.

## Source Sensor (Posnet rGPS, Fanbeam and Acoustic Unit) Offsets

| SOURCE #1 (STBD) |  |  |  |  |
| --- | --- | --- | --- | --- |
| Stbd (Outer) String |  |  |  |  |
|  | ID # | Fore (+) | Stbd (+) | Up (+) |
| Acoustic | G01T01 | 0.00 | 6.00 | -3.00 |
| rGPS | G01R01 | 0.00 | 6.00 | 5.00* (6.0) |
| Fanbeam | N/A |  |  |  |
| Fore D.I. | 101 | 6.60 | 6.00 | 1.00 |
| Mid D.I. | 105 | -1.00 | 6.00 | 1.00 |
| Aft D.I. | 108 | -8.50 | 6.00 | 1.00 |
| Centre String |  |  |  |  |
|  | ID # | Fore (+) | Stbd (+) | Up (+) |
| Acoustic | N/A |  |  |  |
| rGPS | G01R02 | 0.00 | 0.00 | 5.00* (6.0) |
| Fanbeam | G01L01 | 0.00 | 0.00 | 5.50 |
| Fore D.I. | 201 | 6.60 | 0.00 | 1.00 |
| Mid D.I. | 205 | -1.00 | 0.00 | 1.00 |
| Aft D.I. | 208 | -8.50 | 0.00 | 1.00 |
| Port (Inner) String |  |  |  |  |
|  | ID # | Fore (+) | Stbd (+) | Up (+) |
| Acoustic | G01T02 | 0.00 | -6.00 | -3.00 |
| rGPS | G01R03 | 0.00 | -6.00 | 5.00* (6.0) |
| Fanbeam | N/A |  |  |  |
| Fore D.I. | 301 | 6.60 | -6.00 | 1.00 |
| Mid D.I. | 305 | -1.00 | -6.00 | 1.00 |
| Aft D.I. | 308 | -8.50 | -6.00 | 1.00 |

| SOURCE #2 (PORT) |  |  |  |  |
| --- | --- | --- | --- | --- |
| Stbd (Inner) String |  |  |  |  |
|  | ID # | Fore (+) | Stbd (+) | Up (+) |
| Acoustic | G02T01 | 0.00 | 6.00 | -3.00 |
| rGPS | G02R01 | 0.00 | 6.00 | 5.00* (6.0) |
| Fanbeam | N/A |  |  |  |
| Fore D.I. | 601 | 6.60 | 6.00 | 1.00 |
| Mid D.I. | 605 | -1.00 | 6.00 | 1.00 |
| Aft D.I. | 608 | -8.50 | 6.00 | 1.00 |
| Centre String |  |  |  |  |
|  | ID # | Fore (+) | Stbd (+) | Up (+) |
| Acoustic | N/A |  |  |  |
| rGPS | G02R02 | 0.00 | 0.00 | 5.00* (6.0) |
| Fanbeam | G02L01 | 0.00 | 0.00 | 5.50 |
| Fore D.I. | 701 | 6.60 | 0.00 | 1.00 |
| Mid D.I. | 705 | -1.00 | 0.00 | 1.00 |
| Aft D.I. | 708 | -8.50 | 0.00 | 1.00 |
| Port (Outer) String |  |  |  |  |
|  | ID # | Fore (+) | Stbd (+) | Up (+) |
| Acoustic | G02T02 | 0.00 | -6.00 | -3.00 |
| rGPS | G02R03 | 0.00 | -6.00 | 5.00* (6.0) |
| Fanbeam | N/A |  |  |  |
| Fore D.I. | 801 | 6.60 | -6.00 | 1.00 |
| Mid D.I. | 805 | -1.00 | -6.00 | 1.00 |
| Aft D.I. | 808 | -8.50 | -6.00 | 1.00 |

NB.	Source offsets are in metres and are relative to the geometric centre of source (COS)

*Posnet antenna heights are all set to MSL in Spectra as the ranges are slant corrected within the Posnet system

## Streamer Sensor (Bird/Compass and Acoustic Unit) Offsets

### Streamer Acoustic Sensors

| CABLE #1 |  | CABLE #2 |  | CABLE #3 |  |
| --- | --- | --- | --- | --- | --- |
| ID # | Fore (+) | ID # | Fore (+) | ID # | Fore (+) |
| S01T01 | -62.67 | S02T01 | -62.67 | S03T01 | -62.67 |
| S01T02 | -261.87 | S02T02 | -261.87 | S03T02 | -261.87 |
| S01T03 | -461.07 | S02T03 | -461.07 | S03T03 | -461.07 |
| S01T04 | -2154.27 | S02T04 | -2154.27 | S03T04 | -2154.27 |
| S01T05 | -2253.87 | S02T05 | -2253.87 | S03T05 | -2253.87 |
| S01T06 | -4445.07 | S02T06 | -4445.07 | S03T06 | -4445.07 |
| S01T07 | -4579.95 | S02T07 | -4579.95 | S03T07 | -4579.95 |

| CABLE #4 |  | CABLE #5 |  | CABLE #6 |  |
| --- | --- | --- | --- | --- | --- |
| ID # | Fore (+) | ID # | Fore (+) | ID # | Fore (+) |
| S04T01 | -62.67 | S05T01 | -62.67 | S06T01 | -62.67 |
| S04T02 | -261.87 | S05T02 | -261.87 | S06T02 | -261.87 |
| S04T03 | -461.07 | S05T03 | -461.07 | S06T03 | -461.07 |
| S04T04 | -2154.27 | S05T04 | -2154.27 | S06T04 | -2154.27 |
| S04T05 | -2253.87 | S05T05 | -2253.87 | S06T05 | -2253.87 |
| S04T06 | -4445.07 | S05T06 | -4445.07 | S06T06 | -4445.07 |
| S04T07 | -4579.95 | S05T07 | -4579.95 | S06T07 | -4579.95 |

### Streamer Co-located Compass/Depth Sensors

| CABLE #1 |  | CABLE #2 |  | CABLE #3 |  |
| --- | --- | --- | --- | --- | --- |
| ID # | Fore (+) | ID # | Fore (+) | ID # | Fore (+) |
| 1101 | +15.65 | 1201 | +15.65 | 1301 | +15.65 |
| 1102 | -162.27 | 1202 | -162.27 | 1302 | -162.27 |
| 1103 | -361.47 | 1203 | -361.47 | 1303 | -361.47 |
| 1104 | -560.67 | 1204 | -560.67 | 1304 | -560.67 |
| 1105 | -859.47 | 1205 | -859.47 | 1305 | -859.47 |
| 1106 | -1158.27 | 1206 | -1158.27 | 1306 | -1158.27 |
| 1107 | -1457.07 | 1207 | -1457.07 | 1307 | -1457.07 |
| 1108 | -1755.87 | 1208 | -1755.87 | 1308 | -1755.87 |
| 1109 | -2054.67 | 1209 | -2054.67 | 1309 | -2054.67 |
| 1110 | -2353.47 | 1210 | -2353.47 | 1310 | -2353.47 |
| 1111 | -2652.27 | 1212 | -2652.27 | 1313 | -2652.27 |
| 1112 | -2951.07 | 1212 | -2951.07 | 1312 | -2951.07 |
| 1113 | -3249.87 | 1213 | -3249.87 | 1313 | -3249.87 |
| 1114 | -3548.67 | 1214 | -3548.67 | 1314 | -3548.67 |
| 1115 | -3847.47 | 1215 | -3847.47 | 1315 | -3847.47 |
| 1116 | -4146.27 | 1216 | -4146.27 | 1316 | -4146.27 |
| 1117 | -4345.47 | 1217 | -4345.47 | 1317 | -4345.47 |
| 1118 | -4544.67 | 1218 | -4544.67 | 1318 | -4544.67 |

| CABLE #4 |  | CABLE #5 |  | CABLE #6 |  |
| --- | --- | --- | --- | --- | --- |
| ID # | Fore (+) | ID # | Fore (+) | ID # | Fore (+) |
| 1401 | +15.65 | 1501 | +15.65 | 1601 | +15.65 |
| 1402 | -162.27 | 1502 | -162.27 | 1602 | -162.27 |
| 1403 | -361.47 | 1503 | -361.47 | 1603 | -361.47 |
| 1404 | -560.67 | 1504 | -560.67 | 1604 | -560.67 |
| 1405 | -859.47 | 1505 | -859.47 | 1605 | -859.47 |
| 1406 | -1158.27 | 1506 | -1158.27 | 1606 | -1158.27 |
| 1407 | -1457.07 | 1507 | -1457.07 | 1607 | -1457.07 |
| 1408 | -1755.87 | 1508 | -1755.87 | 1608 | -1755.87 |
| 1409 | -2054.67 | 1509 | -2054.67 | 1609 | -2054.67 |
| 1410 | -2353.47 | 1510 | -2353.47 | 1610 | -2353.47 |
| 1414 | -2652.27 | 1515 | -2652.27 | 1616 | -2652.27 |
| 1412 | -2951.07 | 1512 | -2951.07 | 1612 | -2951.07 |
| 1413 | -3249.87 | 1513 | -3249.87 | 1613 | -3249.87 |
| 1414 | -3548.67 | 1514 | -3548.67 | 1614 | -3548.67 |
| 1415 | -3847.47 | 1515 | -3847.47 | 1615 | -3847.47 |
| 1416 | -4146.27 | 1516 | -4146.27 | 1616 | -4146.27 |
| 1417 | -4345.47 | 1517 | -4345.47 | 1617 | -4345.47 |
| 1418 | -4544.67 | 1518 | -4544.67 | 1618 | -4544.67 |

NB : 	All offsets are in metres and are relative to the Cable Reference Point (CRP) which is the centre of the first group.

Inline (fore is +ve) offsets only are given as all other offsets are zero.