| WELL | WKF W-31A |
| --- | --- |
| DATE | 03-07-2006 |
| DAY # | 13 |
| MIDNIGHT ACTIVITY | Circulate hole clean and work string at TD (3450.0m MDRT). |  | ROP DATA (LAST 24 hours) | m/hr | DEPTH (m) |
| MIDNIGHT DEPTH | 3450.0m MDRT |  | MINIMUM | 5.9 | 2914.0 |
| TVD | 2373.23m TVDRT |  | MAXIMUM | 120.3 | 3313.0 |
| PROGRESS LAST 24 hrs | 380.0m |  | AVERAGE | 63.1 | 3070.0-3450.0 |

|  | TOP (mMDRT) | TOP (mTVDRT) | TOP (mTVDSS) RTtoMSL (33.4m) | HIGH/ LOW (mTVD) | PROGNOSED TOP (mMDRT) | PROGNOSED TOP (mTVDRT) |
| --- | --- | --- | --- | --- | --- | --- |
| Base of Miocene | 2016.0 | 1433.5 | -1400.1 | 0.1LOW | 2015.3 | 1433.4 |
| Lakes Entrance | 2935.5 | 2034.6 | -2001.2 | 1.2LOW | 2933.0 | 2033.4 |
| Top of Latrobe | 3288.0 | 2264.9 | -2231.5 | 4.5LOW | 3280.0 | 2260.4 |
| Top P 1.1 sand | 3328.0 | 2291.9 | -2258.5 | 0.5HIGH | 3329.0 | 2292.4 |
| Base P 1.1 sand | 3340.0 | 2300.0 | -2266.6 | 2.6LOW | 3340.0 | 2297.4 |
| Top M1.2 L | 3357.0 | 2311.5 | -2278.1 | 0.1LOW | 3358.0 | 2311.4 |
| Base M1.2L | 3364.0 | 2316.2 | -2282.8 | 0.8LOW | 3364.0 | 2315.4 |
| Top M1.3 | 3373.5 | 2322.6 | -2289.2 | 1.2LOW | 3373.0 | 2321.4 |
| Top PS5 Sand | 3379.5 | 2326.6 | -2293.2 | 1.2LOW | 3379.0 | 2325.4 |
| Top PS4 Sand | 3383.5 | 2329.3 | -2295.9 | 0.9LOW | 3384.0 | 2328.4 |
| Top M1.3 L | 3402.5 | 2341.9 | -2308.5 | 3.5LOW | 3399.0 | 2338.4 |
| Top 1.4 Coals | 3429.0 | 2359.4 | -2326.0 | 1.0LOW | 3430.0 | 2358.4 |
| Total depth | 3450.0 | 2373.2 | -2339.8 | 9.8LOW | 3438.0 | 2363.4 |

| Current Formation | LATROBE FORMATION: 60% Sandstone, 25% Siltstone, 15%Calcareous Claystone. |
| --- | --- |

| GAS DATA | DEPTH (m) | TOTAL GAS (U) | C1 % | C2 % | C3 % | iC4 % | nC4 % | C5 % |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| MAX (FCP/FGP) | 3333.5 | 79.0 | 0.184 | 0.078 | 0.094 | 0.034 | 0.056 | 0.055 |
| MAX (Reserval) | 3333.5 | 304.0 | 1.364 | 0.388 | 0.562 | 0.192 | 0.285 | 0.213 |
| BG (FCP/FGP) | 3070.0-3450.0 | 11.0 | 0.094 | 0.009 | 0.007 |  |  |  |
| BG (Reserval) | 3070.0-3450.0 | 21.0 | 0..026 | 0.201 | 0.004 | 0.006 |  |  |
| TRIP GAS (FCP) |  |  |  |  |  |  |  |  |
| TRIP GAS Reserval) |  |  |  |  |  |  |  |  |

| BIT DATA | PRESENT BIT | LAST BIT |
| --- | --- | --- |
| BIT No. | 2 | 1 |
| SIZE (in) | 8 ½” | 12¼” |
| MANUFACTURER/TYPE | Smith S616PX | Security EBXS C15 |
| JETS (/32 inch) | 6 x 20 | 3 x 18 |
| DEPTH IN (m) | 2974.0 | 1242.0 |
| DEPTH OUT (m) | 3450.0 | 1300.0 |
| METRES ON RUN (m) | 656.0 | 58.0 |
| HRS ON BTM 24hrs/total | 8 / 15.4 | 2.0 / 2.0 |
| BIT CONDITION | In | NG |
| RPM RANGE LAST 24 hrs | TDRPM:115 MMRPM:170 | TDRPM: 60-118 |
| Pump Hrs 24 hrs / total | 20.4 / 68.2 | 14.7 / 14.7 |
| Krevs 24 hrs / total | 134 / 251 | 12 / 12 |
| 24 HOUR SUMMARY | Drill steer and survey 8 ½” hole from 3070.0m MDRT to 3082.0m MDRT, circulate for 1x circulation due to high pick up weights. Drill, steer and survey 8 ½” hole from 3082.0m MDRT to 3146.0m MDRT, working string on connections. Circulate hole clean whilst racking back 1 stand per half hour to 3083.0m MDRT. Wash and ream from 3083.0m MDRT to 3146.0m MDRT. Drill, steer and survey 8 ½” hole from 3082.0m MDRT to TD at 3450.0m MDRT. Circulate hole clean whilst racking back 1 stand per half hour to 3427.0m MDRT. |
| 05:00 AM UPDATE 04-07-2006. DEPTH @ 05:00 hours | Circulate hole clean whiilst racking back 1 stand per half hour from 3427.0m MDRT to 3339.0m MDRT. Flow check, pump heavy weight slug and pull out of hole from 3339.0m MDRT to 2790.0m MDRT. 3450.0 mMDRT (2373.23 mTVDRT) |