DRILLING / WELLWORK REPORT 24HRS TO 0500 HRS FEBRUARY 20, 2007

SAFETY:

DAYS SINCE LAST TRI:	PREVIOUS BEST TRI PERIOD

| ISDL RIG 453 | 277 | 363 |
| --- | --- | --- |
| ISDL RIG 175 | 199 | 199 |
| CAMERON | 1752 | 1752 |
| HALLIBURTON | 3556 | 3556 |
| SCHLUMBERGER | 2461 | 2461 |
| ISS | 269 | 2357 |

Well: HLA_A24

Rig/Contractor: 	Rig 453	Report Date: February 20, 2007

Supervisor:	Bareswill, J R (Dicky)

Smith, Gary G

| AFE Number: AFE Number: | L0501G208 | Ave Angle: |  |
| --- | --- | --- | --- |
| Days on AFE | 27.5 | AFE Cost/Days: | $6,635,763 |
| Daily Cost: | $384,630 |  |  |
| Total Cost: | $6,733,660 | Planned MD/TVD: | 2,984.99/2,616.57 |
| Casing Size: |  | Actual MD/TVD: | 2,991.00/2,452.97 |
| Mud Weight: |  | Tubing Size: |  |

| Objective: | HLA_A24 |
| --- | --- |
| Management Summary: | R/u Hall W/L, proper tools sourced from another platform, removed BOPS, installed and tested tree, Tested lubricator, Made W/L runs, pressure up in increments to 4000 psi to set packer, Pulled dummy from SSSV profile, Pulled RN plug at 2674m, Set SSSV at 140m-4000 psi on control line, Pumping down tubing to test packer seal at report time. |
| Current: | Testing Packer Seal |
| Planned: | Skid to HLA A16 |

DRILLING / WELLWORK REPORT 24HRS TO 0500 HRS FEBRUARY 20, 2007

SAFETY:

DAYS SINCE LAST TRI:	PREVIOUS BEST TRI PERIOD

| ISDL RIG 453 | 277 | 363 |
| --- | --- | --- |
| ISDL RIG 175 | 199 | 199 |
| CAMERON | 1752 | 1752 |
| HALLIBURTON | 3556 | 3556 |
| SCHLUMBERGER | 2461 | 2461 |
| ISS | 269 | 2357 |

Well: FTA _A12a

Rig/Contractor: 	Rig 175	Report Date: February 20, 2007

Supervisor:	Steel, George

Bennett, James

| AFE Number: AFE Number: | L0501H000 | Ave Angle: |  |
| --- | --- | --- | --- |
| Days on AFE | 39.71 | AFE Cost/Days: | $10,210,000 |
| Daily Cost: | $181,983 |  |  |
| Total Cost: | $6,745,830 | Planned MD/TVD: |  |
| Casing Size: |  | Actual MD/TVD: |  |
| Mud Weight: |  | Tubing Size: |  |

| Objective: | FTA_A12a |
| --- | --- |
| Management Summary: | Skid rig package to west side to allow for Production to perform maintenance on gas turbine. Pin Block to top drive assy., and secure service loops in derrick, perform boom inspection and grease A frame on west crane, installing drain lines for mud pit modules, installing wind walls on rig floor and prepare same |
| Current: | General rig up operations |
| Planned: | Continue rig up |