| Depth m/hr | Lith % | Glenaire-1A (Sidetrack) 152mm hole. Glenaire-1 was plugged back from 3306m (T.D.) to 3041m for sidetrack due to excessive deviation. | TG u % |
| --- | --- | --- | --- |
| 3045 (3) | 100 | Cement. | 6 (80:6:5:4:5) |
| 3048 (2.5) | 100 | Cement. | 8 (80:6:5:4:5) |
| 3051 (1.5) | 100 | Cement. | 8 (80:6:5:4:5) |
| 3054 (11) | 100 | Cement. | 11 (80:6:5:4:5) |
| 3057 (20) | 100 | Cement. | 14 (80:6:5:4:5) |
| 3060 (5) | 100 | Cement. | 15 (82:7:5:2:3) |
| 3063 (0.6) | 100 Trace | Cement. SILTY CLAYSTONE, medium to dark grey to medium brown grey, abundant very fine altered feldspar grains in part, trace black carbonaceous flecks and detritus, common micromica, hard, subfissile. | 8 (82:7:5:2:3) (82:7:5:2:3) |
| 3066 (0.7) | Trace 60 40 | Cement. SILTY CLAYSTONE, as above. SANDSTONE, off white to light brown, silty to very fine, subangular to subrounded, moderately sorted, strong silica and calcareous cements, abundant off white argillaceous matrix – matrix supported, abundant altered feldspar grains, trace green grey brown red and black volcanogenic lithics, trace quartz grains, trace fine brown mica flakes, trace black carbonaceous detritus, hard, no visual porosity, no oil fluorescence. | 5 (82:7:5:2:3) |
| 3069 (1.1) | 30 70 | SILTY CLAYSTONE, as above. SANDSTONE, as above. | 1 (82:7:5:2:3) |
| 3072 (1.6) | 70 30 | SILTY CLAYSTONE, as above. SANDSTONE, as above. | 10.5 (82:8:5:5:tr) |
| 3075 (1.2) | 100 Trace | SILTY CLAYSTONE, as above. SANDSTONE, as above. | 3.0 (82:8:5:5:tr) |
| 3078 (2.1) | 100 Trace | SILTY CLAYSTONE, as above. SANDSTONE, as above. | 4.2 (84:8:6:2:tr) |
| 3081 (2.3) | 100 Trace | SILTY CLAYSTONE, as above. SANDSTONE, as above. | 10.5 (84:8:6:2:tr) |
| 3084 (2.4) | 100 Trace | SILTY CLAYSTONE, as above. SANDSTONE, as above. | 17.5 (83:9:5:2:1) |
| 3087 (2.9) | 100 | SILTY CLAYSTONE, as above. | 10.9 (83:9:5:2:1) |
| 3090 (3.1) | 90 10 | SILTY CLAYSTONE, medium to dark grey to medium brown grey, abundant very fine altered feldspar grains in part, trace black carbonaceous flecks and detritus, common micromica, hard, subfissile. SANDSTONE, as above. | 14.1 (83:9:5:2:1) |
| 3093 (3.2) | 100 Trace | SILTY CLAYSTONE, as above. SANDSTONE, as above. | 14.6 (83:9:5:2:1) |
| 3096 (3.0) | 100 Trace | SILTY CLAYSTONE, as above. SANDSTONE, as above. | 19.2 (85:8:4:2:1) |
| 3099 (2.5) | 90 10 | SILTY CLAYSTONE, medium to dark grey to medium brown grey, abundant very fine altered feldspar grains in part, trace black carbonaceous flecks and detritus, common black coal detritus, common micromica, hard, subfissile. SANDSTONE, as above. | 28 (85:8:4:2:1) |
| 3102 (2.3) | 100 Trace | SILTY CLAYSTONE, medium to dark grey to medium brown grey, abundant very fine altered feldspar grains in part, trace black carbonaceous flecks and detritus, common micromica, hard, subfissile. SANDSTONE, as above. | 16.7 (85:8:4:2:1) |
| 3105 (2.8) | 80 20 | SILTY CLAYSTONE, as above. SANDSTONE, as above. | 10.5 (85:7:5:3:tr) |
| 3108 (3.2) | 90 10 | SILTY CLAYSTONE, as above. SANDSTONE, as above. | 5.2 (85:7:5:3:tr) |
| 3111 (3.0) | 60 40 | SILTY CLAYSTONE, as above. SANDSTONE, off white to light brown, silty to occasionally fine, dominantly very fine, subangular to subrounded, moderately sorted, strong silica and calcareous cements, abundant off white argillaceous matrix – matrix supported, abundant altered feldspar grains, trace green grey brown red and black volcanogenic lithics, trace quartz grains, trace fine brown mica flakes, trace black carbonaceous detritus, hard, no visual porosity, no oil fluorescence. | 5.4 (80:8:5:4:3) |
| 3114 (2.1) | 80 20 | SILTY CLAYSTONE, as above. SANDSTONE, as above. | 4.6 (80:8:5:4:3) |
| 3117 (2.2) | 70 30 | SILTY CLAYSTONE, as above. SANDSTONE, as above. | 5.3 (82:8:7:3:tr) |
| 3120 (2.1) | 80 20 | SILTY CLAYSTONE, as above. SANDSTONE, as above. | 4.0 (82:8:7:3:tr) |
| 3123 (2.8) | 90 10 | SILTY CLAYSTONE, medium to dark grey to medium brown grey, abundant very fine altered feldspar grains in part, common black carbonaceous flecks and detritus, common micromica, hard, subfissile. SANDSTONE, off white to light brown, silty to very fine, subangular to subrounded, moderately sorted, strong silica and calcareous cements, abundant off white argillaceous matrix – matrix supported, abundant altered feldspar grains, trace green grey brown red and black volcanogenic lithics, trace quartz grains, trace fine brown mica flakes, trace black carbonaceous detritus, hard, no visual porosity, no oil fluorescence. | 56 (82:8:6:3:1) |
| 3126 (3.1) | 90 10 | SILTY CLAYSTONE, as above. SANDSTONE, as above. | 881 (80:9:8:2:1) |
| 3129 |  |  |  |
| 3132 |  |  |  |
| 3135 |  |  |  |
| 3138 |  |  |  |
| 3141 |  |  |  |
| 3144 |  |  |  |
| 3147 |  |  |  |
| 3150 |  |  |  |
| 3153 |  |  |  |
| 3156 |  |  |  |
| 3159 |  |  |  |
| 3162 |  |  |  |
| 3165 |  |  |  |
| 3168 |  |  |  |
| 3171 |  |  |  |
| 3174 |  |  |  |
| 3177 |  |  |  |
| 3180 |  |  |  |
| 3183 |  |  |  |
| 3186 |  |  |  |
| 3189 |  |  |  |
| 3192 |  |  |  |
| 3195 |  |  |  |
| 3198 |  |  |  |
| 3201 |  |  |  |