| Depth m/hr | Lith % | Glenaire-1A (Sidetrack) 152mm hole. Glenaire-1 was plugged back from 3306m (T.D.) to 3041m for sidetrack due to excessive deviation. | TG u % |
| --- | --- | --- | --- |
| 3045 (3) | 100 | Cement. | 6 (80:6:5:4:5) |
| 3048 (2.5) | 100 | Cement. | 8 (80:6:5:4:5) |
| 3051 (1.5) | 100 | Cement. | 8 (80:6:5:4:5) |
| 3054 (11) | 100 | Cement. | 11 (80:6:5:4:5) |
| 3057 (20) | 100 | Cement. | 14 (80:6:5:4:5) |
| 3060 (5) | 100 | Cement. | 15 (82:7:5:2:3) |
| 3063 (0.6) | 100 Trace | Cement. SILTY CLAYSTONE, medium to dark grey to medium brown grey, abundant very fine altered feldspar grains in part, trace black carbonaceous flecks and detritus, common micromica, hard, subfissile. | 8 (82:7:5:2:3) (82:7:5:2:3) |
| 3066 (0.7) | Trace 60 40 | Cement. SILTY CLAYSTONE, as above. SANDSTONE, off white to light brown, silty to very fine, subangular to subrounded, moderately sorted, strong silica and calcareous cements, abundant off white argillaceous matrix – matrix supported, abundant altered feldspar grains, trace green grey brown red and black volcanogenic lithics, trace quartz grains, trace fine brown mica flakes, trace black carbonaceous detritus, hard, no visual porosity, no oil fluorescence. | 5 (82:7:5:2:3) |
| 3069 (1.1) | 30 70 | SILTY CLAYSTONE, as above. SANDSTONE, as above. | 1 (82:7:5:2:3) |
| 3072 (1.6) | 70 30 | SILTY CLAYSTONE, as above. SANDSTONE, as above. | 10.5 (82:8:5:5:tr) |
| 3075 (1.2) | 100 Trace | SILTY CLAYSTONE, as above. SANDSTONE, as above. | 3.0 (82:8:5:5:tr) |
| 3078 (2.1) | 100 Trace | SILTY CLAYSTONE, as above. SANDSTONE, as above. | 4.2 (84:8:6:2:tr) |
| 3081 (2.3) | 100 Trace | SILTY CLAYSTONE, as above. SANDSTONE, as above. | 10.5 (84:8:6:2:tr) |
| 3084 (2.4) | 100 Trace | SILTY CLAYSTONE, as above. SANDSTONE, as above. | 17.5 (83:9:5:2:1) |
| 3087 (2.9) | 100 | SILTY CLAYSTONE, as above. | 10.9 (83:9:5:2:1) |
| 3090 (3.1) | 90 10 | SILTY CLAYSTONE, medium to dark grey to medium brown grey, abundant very fine altered feldspar grains in part, trace black carbonaceous flecks and detritus, common micromica, hard, subfissile. SANDSTONE, as above. | 14.1 (83:9:5:2:1) |
| 3093 (3.2) | 100 Trace | SILTY CLAYSTONE, as above. SANDSTONE, as above. | 14.6 (83:9:5:2:1) |
| 3096 (3.0) | 100 Trace | SILTY CLAYSTONE, as above. SANDSTONE, as above. | 19.2 (85:8:4:2:1) |
| 3099 (2.5) | 90 10 | SILTY CLAYSTONE, medium to dark grey to medium brown grey, abundant very fine altered feldspar grains in part, trace black carbonaceous flecks and detritus, common black coal detritus, common micromica, hard, subfissile. SANDSTONE, as above. | 28 (85:8:4:2:1) |
| 3102 (2.3) | 100 Trace | SILTY CLAYSTONE, medium to dark grey to medium brown grey, abundant very fine altered feldspar grains in part, trace black carbonaceous flecks and detritus, common micromica, hard, subfissile. SANDSTONE, as above. | 16.7 (85:8:4:2:1) |
| 3105 (2.8) | 80 20 | SILTY CLAYSTONE, as above. SANDSTONE, as above. | 10.5 (85:7:5:3:tr) |
| 3108 (3.2) | 90 10 | SILTY CLAYSTONE, as above. SANDSTONE, as above. | 5.2 (85:7:5:3:tr) |
| 3111 (3.0) | 60 40 | SILTY CLAYSTONE, as above. SANDSTONE, off white to light brown, silty to occasionally fine, dominantly very fine, subangular to subrounded, moderately sorted, strong silica and calcareous cements, abundant off white argillaceous matrix – matrix supported, abundant altered feldspar grains, trace green grey brown red and black volcanogenic lithics, trace quartz grains, trace fine brown mica flakes, trace black carbonaceous detritus, hard, no visual porosity, no oil fluorescence. | 5.4 (80:8:5:4:3) |
| 3114 (2.1) | 80 20 | SILTY CLAYSTONE, as above. SANDSTONE, as above. | 4.6 (80:8:5:4:3) |
| 3117 (2.2) | 70 30 | SILTY CLAYSTONE, as above. SANDSTONE, as above. | 5.3 (82:8:7:3:tr) |
| 3120 (2.1) | 80 20 | SILTY CLAYSTONE, as above. SANDSTONE, as above. | 4.0 (82:8:7:3:tr) |
| 3123 (2.8) | 90 10 | SILTY CLAYSTONE, medium to dark grey to medium brown grey, abundant very fine altered feldspar grains in part, common black carbonaceous flecks and detritus, common micromica, hard, subfissile. SANDSTONE, off white to light brown, silty to very fine, subangular to subrounded, moderately sorted, strong silica and calcareous cements, abundant off white argillaceous matrix – matrix supported, abundant altered feldspar grains, trace green grey brown red and black volcanogenic lithics, trace quartz grains, trace fine brown mica flakes, trace black carbonaceous detritus, hard, no visual porosity, no oil fluorescence. | 56 (82:8:6:3:1) |
| 3126 (3.1) | 90 10 | SILTY CLAYSTONE, as above. SANDSTONE, as above. | 881 (80:9:8:2:1) |
| 3129 (3.0) | 90 10 | SILTY CLAYSTONE, as above. SANDSTONE, as above. | 75 (80:9:8:2:1) |
| 3132 (3.5) | 100 Trace | SILTY CLAYSTONE, as above. SANDSTONE, as above. | 42 (80:9:8:2:1) |
| 3135 (3.2) | 100 | SILTY CLAYSTONE, as above. | 26 (80:9:8:2:1) |
| 3138 (3.0) | 100 | SILTY CLAYSTONE, as above. | 7 (81:8:6:3:2) |
| 3141 (2.7) | 100 | SILTY CLAYSTONE, as above. | 5 (81:8:6:3:2) |
| 3144 (2.5) | 100 | SILTY CLAYSTONE, as above. | 20 (84:7:5:3:tr) |
| 3147 (2.6) | 90 10 | SILTY CLAYSTONE, as above. SANDSTONE, as above. | 46 (84:7:5:3:tr) |
| 3150 (2.5) | 30 70 | SILTY CLAYSTONE, medium to dark grey to medium brown grey, abundant very fine altered feldspar grains in part, trace black carbonaceous flecks and detritus, common micromica, hard, subfissile. SANDSTONE, off white to light brown, very fine to fine, dominantly fine, subangular to subrounded, moderately sorted, strong silica and calcareous cements, abundant off white argillaceous matrix – matrix supported, abundant altered feldspar grains, trace green grey brown red and black volcanogenic lithics, trace quartz grains, trace fine brown mica flakes, trace black carbonaceous detritus, hard, no visual porosity, no oil fluorescence. | 235 (80:8:7:3:2) |
| 3153 (2.5) | 80 20 Trace Fluor | SILTY CLAYSTONE, medium to dark grey to medium brown grey, very carbonaceous in part – grades to coal, abundant very fine altered feldspar grains in part, trace black carbonaceous flecks and detritus, common micromica, hard, subfissile. SANDSTONE, as above. COAL, black, subvitreous to vitreous, subconchoidal fracture, hard, brittle. FLUORESCENCE, the sandstone has dull orange mineral fluorescence, no cut, the coal has no fluorescence but gives a weak pale yellow crush cut. | 2538 (77:9:8:4:2) |
| 3156 (2.2) | 100 Trace | SILTY CLAYSTONE, medium to dark grey to medium brown grey, abundant very fine altered feldspar grains in part, trace black carbonaceous flecks and detritus, common micromica, hard, subfissile. SANDSTONE, off white to light brown, silty to very fine, subangular to subrounded, moderately sorted, strong silica and calcareous cements, abundant off white argillaceous matrix – matrix supported, abundant altered feldspar grains, trace green grey brown red and black volcanogenic lithics, trace quartz grains, trace fine brown mica flakes, trace black carbonaceous detritus, hard, no visual porosity, no oil fluorescence. | 1320 (75:9:9:5:2) |
| 3159 (2.2) | 90 10 | SILTY CLAYSTONE, as above. SANDSTONE, as above. | 209 (75:9:9:5:2) |
| 3162 (2.1) | 80 20 | SILTY CLAYSTONE, as above. SANDSTONE, as above. | 163 (75:9:8:5:3) |
| 3165 (2.5) | 100 | SILTY CLAYSTONE, as above. | 948 (76:9:8:5:2) |
| 3168 (3.0) | 100 | SILTY CLAYSTONE, as above. | 73 (76:9:8:5:2) |
| 3171 (2.5) | 90 10 | SILTY CLAYSTONE, medium to dark grey to medium brown grey, abundant very fine altered feldspar grains in part, trace black carbonaceous flecks and detritus, trace calcite lined fractures, common micromica, hard, subfissile. SANDSTONE, off white to light brown, silty to very fine, subangular to subrounded, moderately sorted, strong silica and calcareous cements, abundant off white argillaceous matrix – matrix supported, abundant altered feldspar grains, trace green grey brown red and black volcanogenic lithics, trace quartz grains, trace fine brown mica flakes, trace black carbonaceous detritus, trace calcite lined fractures, hard, no visual porosity, no oil fluorescence. | 84 (76:9:8:5:2) |
| 3174 (2.0) | 90 10 | SILTY CLAYSTONE, as above. SANDSTONE, as above. | 101 (81:8:6:3:2) |
| 3177 (1.8) | 100 Trace | SILTY CLAYSTONE, medium to dark grey to medium brown grey, abundant very fine altered feldspar grains in part, trace black carbonaceous flecks and detritus, common micromica, hard, subfissile. SANDSTONE, off white to light brown, silty to very fine, subangular to subrounded, moderately sorted, strong silica and calcareous cements, abundant off white argillaceous matrix – matrix supported, abundant altered feldspar grains, trace green grey brown red and black volcanogenic lithics, trace quartz grains, trace fine brown mica flakes, trace black carbonaceous detritus, hard, no visual porosity, no oil fluorescence. | 40 (81:8:6:3:2) |
| 3180 (2.0) | 80 20 | SILTY CLAYSTONE, as above. SANDSTONE, as above. | 330 (80:9:6:3:2) |
| 3183 (2.4) | 80 20 | SILTY CLAYSTONE, as above. SANDSTONE, as above. | 74 (80:9:6:3:2) |
| 3186 (22) | 80 20 | SILTY CLAYSTONE, as above. SANDSTONE, as above. | 81 (80:9:6:3:2) |
| 3189 (24) | 70 30 | SILTY CLAYSTONE, medium to dark grey to medium brown grey, abundant very fine altered feldspar grains in part, trace black carbonaceous flecks and detritus, common micromica, hard, subfissile. SANDSTONE, off white to light brown, silty to fine, dominantly very fine, subangular to subrounded, moderately sorted, strong silica and calcareous cements, abundant off white argillaceous matrix – matrix supported, abundant altered feldspar grains, trace green grey brown red and black volcanogenic lithics, trace quartz grains, trace fine brown mica flakes, trace black carbonaceous detritus, hard, no visual porosity, no oil fluorescence. | 194 (80:9:6:3:2) |
| 3192 (40) | 40 30 30 Fluor | SILTY CLAYSTONE, medium to dark grey to medium brown grey, abundant very fine altered feldspar grains in part, trace black carbonaceous flecks and detritus, very carbonaceous in part, common micromica, hard, subfissile. SANDSTONE, off white to light brown, silty to fine, dominantly very fine, subangular to subrounded, moderately sorted, strong silica and calcareous cements, abundant off white argillaceous matrix – matrix supported, abundant altered feldspar grains, trace green grey brown red and black volcanogenic lithics, trace quartz grains, trace fine brown mica flakes, trace fine black carbonaceous detritus, hard, no visual porosity, no oil fluorescence. COAL, black to very dark grey, very argillaceous in part, earthy to subvitreous lustre, irregular/contused fracture, hard, brittle. FLUORESCENCE, the sandstone has dull orange mineral fluorescence, no cut, the coal has no fluorescence but gives a weak pale yellow crush cut. Well flowing oil/gas cut mud – probably from fractures associated with the sand/coal. Crude is green, waxy, on the heavier end of a light crude, Gives a bright pale greenish yellow white fluorescence with a milky white cut. | 159 (61:12:13:9:5) |
| 3195 (26) | 70 30 | SILTY CLAYSTONE, medium to dark grey to medium brown grey, abundant very fine altered feldspar grains in part, trace black carbonaceous flecks and detritus, common micromica, hard, subfissile. SANDSTONE, off white to light brown, silty to occasionally fine, dominantly very fine, subangular to subrounded, moderately sorted, strong silica and calcareous cements, abundant off white argillaceous matrix – matrix supported, abundant altered feldspar grains, trace green grey brown red and black volcanogenic lithics, trace quartz grains, trace fine brown mica flakes, trace black carbonaceous detritus, hard, no visual porosity, no oil fluorescence. | 4561 (61:12:13:9:5) |
| 3198 (28) | 80 20 | SILTY CLAYSTONE, as above. SANDSTONE, as above. | 3519 (61:12:13:9:5) |
| 3201 (28) | 80 20 | SILTY CLAYSTONE, as above. SANDSTONE, as above. | 3199 (61:12:13:9:5) |
| 3204 (35) | 80 20 | SILTY CLAYSTONE, as above. SANDSTONE, as above. | 2248 (61:12:13:9:5) |
| 3207 (33) | 70 30 | SILTY CLAYSTONE, as above. SANDSTONE, as above. | 780 (61:12:13:9:5) |
| 3210 (21) | 100 | SILTY CLAYSTONE, as above. | 877 (77:8:6:5:4) |
| 3213 (24) | 100 | SILTY CLAYSTONE, as above. | 542 (77:8:6:5:4) |
| 3216 (27) | 100 Trace | SILTY CLAYSTONE, medium to dark grey to medium brown grey, abundant very fine altered feldspar grains in part, trace black carbonaceous flecks and coaly detritus, common micromica, hard, subfissile. SANDSTONE, off white to light brown, silty to very fine, subangular to subrounded, moderately sorted, strong silica and calcareous cements, abundant off white argillaceous matrix – matrix supported, abundant altered feldspar grains, trace green grey brown red and black volcanogenic lithics, trace quartz grains, trace fine brown mica flakes, trace black carbonaceous detritus, hard, no visual porosity, no oil fluorescence. | 4056 (60:12:15:9:4) |
| 3219 (22) | 100 Trace | SILTY CLAYSTONE, medium to dark grey to medium brown grey, abundant very fine altered feldspar grains in part, trace black carbonaceous flecks and detritus, common micromica, hard, subfissile. SANDSTONE, as above. | 2003 (60:12:15:9:4) |
| 3222 (18) | 90 10 | SILTY CLAYSTONE, as above. SANDSTONE, as above. | 220 (60:12:15:9:4) |
| 3225 (3.0) | 90 10 | SILTY CLAYSTONE, as above. SANDSTONE, as above. | 290 (57:11:14:11:7) |
| 3228 (6.0) | 90 10 | SILTY CLAYSTONE, as above. SANDSTONE, off white to light brown, silty to fine, dominantly very fine, subangular to subrounded, moderately sorted, strong silica and calcareous cements, abundant off white argillaceous matrix – matrix supported, abundant altered feldspar grains, trace green grey brown red and black volcanogenic lithics, trace quartz grains, trace fine brown mica flakes, trace black carbonaceous detritus, hard, no visual porosity, no oil fluorescence. | 3131 (59:11:14:10:6) |
| 3231 (16) | 90 10 | SILTY CLAYSTONE, as above. SANDSTONE, as above. | 180 (83:7:5:2:3) |
| 3234 (18) | 70 30 | SILTY CLAYSTONE, as above. SANDSTONE, as above. | 453 (79:8:6:4:3) |
| 3237 (19) | 60 10 30 Fluor | SILTY CLAYSTONE, medium to dark grey to medium brown grey, abundant very fine altered feldspar grains in part, very carbonaceous in part – grades to coal, trace black carbonaceous flecks and detritus, common micromica, hard, subfissile. SANDSTONE, as above. COAL, black to very dark grey, very argillaceous in part, earthy to subvitreous lustre, irregular to blocky fracture, hard, brittle. FLUORESCENCE, the sandstone has dull orange mineral fluorescence, no cut, the coal has no fluorescence but gives a weak pale yellow crush cut. | 1503 (79:8:6:4:3) |
| 3240 (11) | 90 10 | SILTY CLAYSTONE, medium to dark grey to medium brown grey, abundant very fine altered feldspar grains in part, trace black carbonaceous flecks and detritus, common micromica, hard, subfissile. SANDSTONE, as above. | 173 (79:8:6:4:3) |
| 3243 (8.0) | 100 Trace | SILTY CLAYSTONE, as above. SANDSTONE, off white to light brown, silty to very fine, subangular to subrounded, moderately sorted, strong silica and calcareous cements, abundant off white argillaceous matrix – matrix supported, abundant altered feldspar grains, trace green grey brown red and black volcanogenic lithics, trace quartz grains, trace fine brown mica flakes, trace black carbonaceous detritus, hard, no visual porosity, no oil fluorescence. | 123 (85:6:3:8:3) |
| 3246 (2.5) | 90 10 | SILTY CLAYSTONE, as above. SANDSTONE, as above. | 4436 (58:11:14:11:6) |
| 3249 (1.2) | 90 10 | SILTY CLAYSTONE, as above. SANDSTONE, as above. | 1513 (77:8:6:5:4) |
| 3252 (9) | 100 Trace | SILTY CLAYSTONE, as above. SANDSTONE, as above. | 4521 (60:11:13:10:6) |
| 3255 (16) | 100 Trace | SILTY CLAYSTONE, as above. SANDSTONE, as above. | 185 (79:8:6:4:3) |
| 3258 (11) | 100 Trace | SILTY CLAYSTONE, as above. SANDSTONE, as above. | 150 (79:8:6:4:3) |
| 3261 (11) | 90 Trace 10 Fluor | SILTY CLAYSTONE, medium to dark grey to medium brown grey, abundant very fine altered feldspar grains in part, very carbonaceous in part – grades to coal, trace black carbonaceous flecks and detritus, common micromica, hard, subfissile SANDSTONE, as above. COAL, black to very dark grey, very argillaceous in part, earthy to subvitreous lustre, irregular to blocky fracture, hard, brittle. FLUORESCENCE, the sandstone has dull orange mineral fluorescence, no cut, the coal has no fluorescence but gives a weak pale yellow crush cut. | 598 (64:10:11:9:6) |
| 3264 (7) | 40 60 | SILTY CLAYSTONE, medium to dark grey to medium brown grey, abundant very fine altered feldspar grains in part, trace black carbonaceous flecks and detritus, common micromica, hard, subfissile. SANDSTONE, off white to light brown, silty to fine, dominantly very fine, subangular to subrounded, moderately sorted, strong silica and calcareous cements, abundant off white argillaceous matrix – matrix supported, abundant altered feldspar grains, trace green grey brown red and black volcanogenic lithics, trace quartz grains, trace fine brown mica flakes, trace black carbonaceous detritus, hard, no visual porosity, no oil fluorescence. | 4381 (64:10:11:9:6) |
| 3267 (2.5) | 90 10 | SILTY CLAYSTONE, as above. SANDSTONE, off white to light brown, silty to very fine, subangular to subrounded, moderately sorted, strong silica and calcareous cements, abundant off white argillaceous matrix – matrix supported, abundant altered feldspar grains, trace green grey brown red and black volcanogenic lithics, trace quartz grains, trace fine brown mica flakes, trace black carbonaceous detritus, hard, no visual porosity, no oil fluorescence. | 4451 (60:12:16:9:4) |
| 3270 (1.3) | 90 10 | SILTY CLAYSTONE, as above. SANDSTONE, as above. | 1306 (60:12:16:9:4) |
| 3273 (1.6) | 100 Trace | SILTY CLAYSTONE, as above. SANDSTONE, off white to light brown, silty to very fine, subangular to subrounded, moderately sorted, strong silica and calcareous cements, abundant off white argillaceous matrix – matrix supported, abundant altered feldspar grains, trace green grey brown red and black volcanogenic lithics, trace quartz grains, trace fine brown mica flakes, trace black carbonaceous detritus, hard, no visual porosity, no oil fluorescence. | 1337 (60:12:16:9:4) |
| 3276 (20) | 80 20 | SILTY CLAYSTONE, as above. SANDSTONE, off white to light brown, silty to fine, dominantly very fine, subangular to subrounded, moderately sorted, strong silica and calcareous cements, abundant off white argillaceous matrix – matrix supported, abundant altered feldspar grains, trace green grey brown red and black volcanogenic lithics, trace quartz grains, trace fine brown mica flakes, trace black carbonaceous detritus, hard, no visual porosity, no oil fluorescence. | 124 (81:7:5:4:3) |
| 3279 (24) | 100 Trace | SILTY CLAYSTONE, medium to dark grey to medium brown grey, abundant very fine altered feldspar grains in part, common black carbonaceous flecks and detritus, common micromica, hard, subfissile SANDSTONE, as above. | 145 (81:7:5:4:3) |
| 3282 (11) | 100 Trace | SILTY CLAYSTONE, as above. SANDSTONE, off white to light brown, silty to very fine, subangular to subrounded, moderately sorted, strong silica and calcareous cements, abundant off white argillaceous matrix – matrix supported, abundant altered feldspar grains, trace green grey brown red and black volcanogenic lithics, trace quartz grains, trace fine brown mica flakes, trace black carbonaceous detritus, hard, no visual porosity, no oil fluorescence. | 641 (81:6:6:4:3) |
| 3285 (19) | 100 Trace | SILTY CLAYSTONE, as above. SANDSTONE, as above. | 295 (81:6:6:4:3) |
| 3288 (31) | 100 Trace | SILTY CLAYSTONE, as above. SANDSTONE, as above. | 287 (81:6:6:4:3) |
| 3291 (28) | 100 Trace | SILTY CLAYSTONE, as above. SANDSTONE, as above. | 280 (81:6:6:4:3) |
| 3294 (35) | 90 10 | SILTY CLAYSTONE, as above. SANDSTONE, off white to light brown, silty to fine, dominantly very fine, subangular to subrounded, moderately sorted, strong silica and calcareous cements, abundant off white argillaceous matrix – matrix supported, abundant altered feldspar grains, trace green grey brown red and black volcanogenic lithics, trace quartz grains, trace fine brown mica flakes, trace black carbonaceous detritus, hard, no visual porosity, no oil fluorescence. | 4305 (70:10:8:7:5) |
| 3297 (32) | 70 30 | SILTY CLAYSTONE, as above. SANDSTONE, as above. | 3485 (70:10:8:7:5) |
| 3300 (33) | 50 50 | SILTY CLAYSTONE, as above. SANDSTONE, as above. | 2011 (62:11:13:16:4) |
| 3303 (2.0) | 90 10 | SILTY CLAYSTONE, as above. SANDSTONE, as above. | 727 (62:11:13:16:4) |
| 3306 (1.4) | 90 10 | SILTY CLAYSTONE, as above. SANDSTONE, as above. | 587 (76:7:6:6:5) |
| 3309 (18) | 80 20 | SILTY CLAYSTONE, as above. SANDSTONE, as above. | 4572 (57:11:15:12:5) |
| 3312 (12) | 100 | SILTY CLAYSTONE, medium to dark grey to medium brown grey, abundant very fine altered feldspar grains in part, common black carbonaceous flecks and detritus, trace calcite lined fractures, common micromica, hard, subfissile | 1197 (62:11:13:16:4) |
| 3315 (11) | 100 Trace | SILTY CLAYSTONE, medium to dark grey to medium brown grey, abundant very fine altered feldspar grains in part, common black carbonaceous flecks and detritus, common micromica, hard, subfissile SANDSTONE, as above. | 347 (83:7:4:3:3) |
| 3318 (9) | 90 10 | SILTY CLAYSTONE, as above. SANDSTONE, as above. | 1324 (87:6:3:2:2) |
| 3321 (8) | 90 Trace 10 Fluor | SILTY CLAYSTONE, medium to dark grey to medium brown grey, abundant very fine altered feldspar grains in part, common black carbonaceous flecks and detritus, very carbonaceous in part – grades to coal, common micromica, hard, subfissile. SANDSTONE, as above. COAL, black to very dark grey, very argillaceous – grades to carbonaceous claystone, earthy lustre, irregular to blocky fracture, hard. FLUORESCENCE, the sandstone has dull orange mineral fluorescence, no cut, the coal has no fluorescence but gives a weak pale yellow crush cut. | 639 (87:6:3:2:2) |
| 3324 (10) | 100 Trace | SILTY CLAYSTONE, medium to dark grey to medium brown grey, abundant very fine altered feldspar grains in part, common black carbonaceous flecks and detritus, common micromica, hard, subfissile SANDSTONE, as above. | 390 (70:8:10:7:5) |
| 3327 (8) | 100 Trace | SILTY CLAYSTONE, as above. SANDSTONE, as above. | 273 (59:12:15:7:6) |
| 3330 (9) | 100 Trace | SILTY CLAYSTONE, as above. SANDSTONE, as above. | 4578 (59:12:15:7:6) |
| 3333 (11) | 100 | SILTY CLAYSTONE, as above | 443 (76:7:6:6:5) |
| 3336 (13) | 100 | SILTY CLAYSTONE, medium to dark grey to medium brown grey, abundant very fine altered feldspar grains in part, common black carbonaceous flecks and detritus, very carbonaceous in part – grades to coal, common micromica, hard, subfissile. | 157 (63:11:13:9:4) |
| 3339 (32) | 100 | SILTY CLAYSTONE, as above | 4287 (63:11:13:9:4) |
| 3342 (20) | 100 Trace | SILTY CLAYSTONE, medium to dark grey to medium brown grey, abundant very fine altered feldspar grains in part, common black carbonaceous flecks and detritus, common micromica, hard, subfissile SANDSTONE, as above. | 319 (65:10:11:9:5) |
| 3345 (10) | 100 Trace | SILTY CLAYSTONE, as above. SANDSTONE, as above. | 4237 (65:10:11:9:5) |
| 3348 (7) | 100 Trace | SILTY CLAYSTONE, as above. SANDSTONE, as above. | 120 (65:10:11:9:5) |
| 3351 (6) | 100 Trace | SILTY CLAYSTONE, as above. SANDSTONE, as above. | 85 (80:7:5:4:3) |
| 3354 (8) | 30 70 | SILTY CLAYSTONE, as above. SANDSTONE, off white to light brown, very fine to fine, dominantly very fine, subangular to subrounded, moderately sorted, strong silica and calcareous cements, abundant off white argillaceous matrix – matrix supported, abundant altered feldspar grains, trace green grey brown red and black volcanogenic lithics, trace quartz grains, trace fine brown mica flakes, trace black carbonaceous detritus, hard, no visual porosity, no oil fluorescence. | 115 (80:7:5:4:3) |
| 3357 (8) | 80 20 | SILTY CLAYSTONE, medium to dark grey to medium brown grey, abundant very fine altered feldspar grains in part, common black carbonaceous flecks and detritus, trace calcite lined fractures, common micromica, hard, subfissile SANDSTONE, as above. | 3908 (75:9:7:5:4) |
| 3360 (1.5) | 100 Trace | SILTY CLAYSTONE, as above. SANDSTONE, as above. | 4583 (75:8:6:6:5) |
| 3363 (1.4) | 100 | SILTY CLAYSTONE, medium to dark grey to medium brown grey, abundant very fine altered feldspar grains in part, trace to common black carbonaceous flecks and detritus, common micromica, hard, subfissile | 472 (75:8:6:6:5) |
| 3366 (4.8) | 90 10 | SILTY CLAYSTONE, as above. SANDSTONE, off white to light brown, silty to very fine, subangular to subrounded, moderately sorted, strong silica and calcareous cements, abundant off white argillaceous matrix – matrix supported, abundant altered feldspar grains, trace green grey brown red and black volcanogenic lithics, trace quartz grains, trace fine brown mica flakes, trace black carbonaceous detritus, hard, no visual porosity, no oil fluorescence. | 4426 (59:11:14:11:5) |
| 3369 (10) | 100 Trace | SILTY CLAYSTONE, as above. SANDSTONE, as above. | 211 (75:8:6:6:5) |
| 3372 (8) | 70 30 | SILTY CLAYSTONE, as above. SANDSTONE, as above. | 150 (75:8:6:6:5) |
| 3375 (18) | 100 | SILTY CLAYSTONE, as above. | 145 (75:8:6:6:5) |
| 3378 (15) | 100 Trace | SILTY CLAYSTONE, as above. SANDSTONE, as above. | 170 (75:8:6:6:5) |
| 3381 (14) | 90 10 | SILTY CLAYSTONE, as above. SANDSTONE, off white to light brown, very fine to fine, dominantly very fine, subangular to subrounded, moderately sorted, strong silica and calcareous cements, abundant off white argillaceous matrix – matrix supported, abundant altered feldspar grains, trace green grey brown red and black volcanogenic lithics, trace quartz grains, trace fine brown mica flakes, trace black carbonaceous detritus, hard, no visual porosity, no oil fluorescence. | 190 (75:8:6:6:5) |
| 3384 (8) | 60 40 | SILTY CLAYSTONE, as above. SANDSTONE, as above. | 155 (75:8:6:6:5) |
| 3387 |  |  |  |
| 3390 |  |  |  |
| 3393 |  |  |  |
| 3396 |  |  |  |
| 3399 |  |  |  |
| 3402 |  |  |  |
| 3405 |  |  |  |
| 3408 |  |  |  |
| 3411 |  |  |  |
| 3414 |  |  |  |
| 3417 |  |  |  |
| 3420 |  |  |  |
| 3423 |  |  |  |
| 3426 |  |  |  |
| 3429 |  |  |  |
| 3432 |  |  |  |
| 3435 |  |  |  |
| 3438 |  |  |  |
| 3441 |  |  |  |
| 3444 |  |  |  |
| 3447 |  |  |  |
| 3450 |  |  |  |
| 3453 |  |  |  |
| 3456 |  |  |  |
| 3459 |  |  |  |
| 3462 |  |  |  |
| 3465 |  |  |  |
| 3468 |  |  |  |
| 3471 |  |  |  |
| 3474 |  |  |  |
| 3477 |  |  |  |
| 3480 |  |  |  |
| 3483 |  |  |  |
| 3486 |  |  |  |
| 3489 |  |  |  |
| 3492 |  |  |  |
| 3495 |  |  |  |
| 3498 |  |  |  |
| 3501 |  |  |  |
| 3504 |  |  |  |
| 3507 |  |  |  |
| 3510 |  |  |  |
| 3513 |  |  |  |
| 3516 |  |  |  |
| 3519 |  |  |  |
| 3522 |  |  |  |
| 3525 |  |  |  |
| 3528 |  |  |  |
| 3531 |  |  |  |
| 3534 |  |  |  |
| 3537 |  |  |  |
| 3540 |  |  |  |
| 3543 |  |  |  |
| 3546 |  |  |  |
| 3549 |  |  |  |
| 3552 |  |  |  |
| 3555 |  |  |  |
| 3558 |  |  |  |
| 3561 |  |  |  |
| 3564 |  |  |  |
| 3567 |  |  |  |
| 3570 |  |  |  |
| 3573 |  |  |  |
| 3576 |  |  |  |
| 3579 |  |  |  |
| 3582 |  |  |  |
| 3585 |  |  |  |
| 3588 |  |  |  |
| 3591 |  |  |  |
| 3594 |  |  |  |
| 3597 |  |  |  |
| 3600 |  |  |  |