DRILLING / WELLWORK REPORT 24HRS TO 0500 HRS October 10, 2006

| RIG 453 | 145 | 363 |
| --- | --- | --- |
| CAMERON | 1620 | 1620 |
| HALLIBURTON | 3408 | 3408 |
| SCHLUMBERGER | 2349 | 2349 |
| ISDL | 145 | 647 |
| ISS | 134 | 2350 |

Well: WKF_W23

Rig/Contractor: 	Rig 453	Report Date: October 10, 2006

Supervisor:	Campbell, Glenn R.

Davis, Brian

| AFE Number: | 40000460 | Ave Angle: |  |
| --- | --- | --- | --- |
| Days to Complete: | 7.0 | AFE Cost/Days: | $1,278,800 |
| Daily Cost: | $175,833 |  |  |
| Total Cost: | $1,302,447 | Planned MD/TVD: |  |
| Casing Size: |  | Actual MD/TVD: |  |
| Mud Weight: |  | Tubing Size: |  |

| Objective: | WKF_W23 |
| --- | --- |
| Management Summary: | N/up BOP and shell test to 300/3000 psi. M/up & RIH with casing cutter. Cut casing @ 726m & POH. M/up casing spear and engage. Pull casing hanger to rig floor. L/out cutoff joint. Lay out 4 joints and establish circulation. Circulate hole clean. Lay down 7-5/8' casing. Conduct trip drills. R/dn WFD. Service Rig. Lay out Baker tools. |
| Current: | Laying out Baker Tools. |
| Planned: | Set Cement Kickoff Plug. |