DRILLING / WELLWORK REPORT 24HRS TO 0500 HRS October 11, 2006

| RIG 453 | 146 | 363 |
| --- | --- | --- |
| CAMERON | 1621 | 1621 |
| HALLIBURTON | 3409 | 3409 |
| SCHLUMBERGER | 2350 | 2350 |
| ISDL | 146 | 647 |
| ISS | 135 | 2351 |

Well: WKF_W23A

Rig/Contractor: 	Rig 453	Report Date: October 11, 2006

Supervisor:	Campbell, Glenn R.

Davis, Brian

| AFE Number: | L0501G660 | Ave Angle: |  |
| --- | --- | --- | --- |
| Days to Complete: | 0.2 | AFE Cost/Days: | $5,948,157 |
| Daily Cost: | $33,538 |  |  |
| Total Cost: | $33,538 | Planned MD/TVD: |  |
| Casing Size: |  | Actual MD/TVD: |  |
| Mud Weight: |  | Tubing Size: |  |

| Objective: | WKF_W23A |
| --- | --- |
| Management Summary: | Rig released from P&A Operations to Drill Well Operations. Change BOP rams for tapered drill string. Pressure test BOP’s. |
| Current: | Pressure Testing BOP’s. |
| Planned: | Change TDS Saver Sub. |

Report for WKF_W23 overleaf

Well: WKF_W23

Rig/Contractor: 	Rig 453	Report Date: October 11, 2006

Supervisor:	Campbell, Glenn R.

Davis, Brian

| AFE Number: | 40000460 | Ave Angle: |  |
| --- | --- | --- | --- |
| Days to Complete: | 7.9 | AFE Cost/Days: | $1,670,300 |
| Daily Cost: | $151,807 |  |  |
| Total Cost: | $1,454,254 | Planned MD/TVD: |  |
| Casing Size: |  | Actual MD/TVD: |  |
| Mud Weight: |  | Tubing Size: |  |

| Objective: | WKF_W23A |
| --- | --- |
| Management Summary: | L/dn tools. Run wear bushing. L/dn 3½” HWDP. RIH w/ OEDP. Set cement kickoff plug. Reverse circulate. POH & L/dn excess 4” DP (Due to setback limitations). POH to surface. P/up 5” DP and rack in mast. Clear rig floor. Service Rig. Held Trip Drills. Recovered wear bushing. Jet wellhead. M/up BOP test assembly. Pressure test Cement Plug #3/Surface Casing to 1000 psi/15 min. Change over to Drilling AFE. |
| Current: | P&A Ops complete. Rig released to Drill Well. |
| Planned: | P&A Ops complete. Rig released to Drill Well. |