| WELL | WKF-W23A |
| --- | --- |
| DATE | 22-10-2006 |
| DAY # | 13 |
| MIDNIGHT ACTIVITY | Pulling out of hole at 1050.0 mMDRT. |  | ROP DATA (LAST 24 hours) | M/hr | DEPTH (m) |
| MIDNIGHT DEPTH | 3338.0 mMDRT |  | MINIMUM | 2.14 | 3335.0 |
| TVD | 2382.0 mTVDRT |  | MAXIMUM | 30.24 | 3226.5 |
| PROGRESS LAST 24 hrs | 81.0 m |  | AVERAGE | 13.3 | 3257.0-3338.0 |

-

| PRELIMINARY FIELD PICKS | ACTUAL TOP (mMDRT) | ACTUAL TOP (mTVDRT) | ACTUAL TOP (mTVDSS) RT to MSL (33.43m) | HIGH/ LOW (mTVD) | PROGNOSED TOP (mMDRT) | PROGNOSED TOP (mTVDRT) |
| --- | --- | --- | --- | --- | --- | --- |
| High Velocity Channel | 2000.5 | 1497.4 | -1464.0 | 56.0 HIGH | 2085.0 | 1553.4 |
| Lakes Entrance | 2709.0 | 1961.0 | -1927.6 | 2.4 HIGH | 2711.2 | 1963.4 |
| Top of Latrobe | 3150.0 | 2254.4 | -2221.0 | 2.0 LOW | 3148.8 | 2252.4 |
| M1.2 sand (TARGET) | 3162.5 | 2262.9 | -2229.5 | 2.5 HIGH | 3168.5 | 2265.4 |
| Top M1.3U PS6 sand | 3180.0 | 2274.8 | -2241.4 | 1.6 HIGH | 3185.2 | 2276.4 |
| Top M1.3U PS4 sand | 3192.5 | 2283.3 | -2249.9 | 0.9 LOW | 3194.3 | 2282.4 |
| Top M1.3 L PS3 sand | 3208.0 | 2293.9 | -2260.5 | 0.5 LOW | 3210.9 | 2293.4 |
| Base of M1.3L sands | 3219.0 | 2301.4 | -2268.0 | 1.0 LOW | 3221.5 | 2300.4 |
| M1.4L section (Coals) | 3232.0 | 2310.2 | -2276.8 | 1.8 LOW | 3233.7 | 2308.4 |
| Top of M1.5 sand | 3251.5 | 2323.4 | -2290.0 | 3.0 LOW | 3251.8 | 2320.4 |
| Top of M1.7 sand | 3269.5 | 2335.6 | -2302.2 | 0.2 LOW | 3274.5 | 2335.4 |
| Total Depth | 3338.0 | 2382.0 | -2384.6 | 3.6 LOW | 3339.7 | 2378.4 |

| Current Formation | Latrobe Group: Sandstone, Siltstone, Claystone, Coal. |
| --- | --- |

| GAS DATA | DEPTH (m) | TOTAL GAS (U) | C1 % | C2 % | C3 % | iC4 % | nC4 % | C5 % |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| MAX (FCP/FGP) | 3258.0 | 24.0 | 0.263 | 0.015 | 0.017 | 0.006 | 0.009 | 0.005 |
| MAX (Reserval) | 3271.0 | 102.0 | 0.426 | 0.073 | 0.115 | 0.054 | 0.086 | 0.085 |
| BG (FCP/FGP) | 3257.0-3338.0 | 14.0 | 0.118 | 0.006 | 0.008 | 0.003 | 0.005 | 0.004 |
| BG (Reserval) | 3257.0-3338.0 | 44.0 | 0.114 | 0.017 | 0.041 | 0.025 | 0.040 | 0.049 |
| TRIP GAS (FCP) | 3257.0 | 48.0 | 0.688 | 0.016 | 0.022 | 0.017 | 0.014 | 0.016 |
| TRIP GAS Reserval) | 3257.0 | 87.0 | 1.182 | 0.019 | 0.037 | 0.021 | 0.034 | 0.039 |

| BIT DATA | PRESENT BIT | LAST BIT |
| --- | --- | --- |
| BIT No. | 2 | 1 |
| SIZE (in) | 8½ | 8½ |
| MANUFACTURER/TYPE | Smith Gfi11YODVPD | Smith S73VPX |
| JETS (/32 inch) | 3 x 30 | 6 x 20 |
| DEPTH IN (m) | 3257.0 | 651.0 |
| DEPTH OUT (m) | 3338.0 | 3257.0 |
| METRES ON RUN (m) | 81.0 | 2606.0 |
| HRS ON BTM 24hrs/total | 6.1 / 6.1 | 102.5 |
| BIT CONDITION |  | 2-2-WT-A-X-2/16-PN-ROP |
| RPM RANGE LAST 24 hrs | TDRPM: 110-115 / MMRPM: 170-180 |  |
| Pump Hrs 24 hrs / total | 10.4 / 10.4 | 2.2 / 170.6 |
| Krevs 24 hrs / total | 107 / 107 | 1562 |
| 24 HOUR SUMMARY | Run in hole from 1310.0 mMDRT to 1620.0 mMDRT. Rig floor to 5” drill pipe and run in hole from 1620.0 mMDRT to 2480.0 mMDRT.0 mMDRT. Wash and ream tight hole from 2325.0 mMDRT to 2338.0 mMDRT. Continue to run in hole from 2338.0 mMDRT to 3257.0 mMDRT, wash and ream through tight spots at 2768.0 mMDRT, 2814.0 mMDRT, 3060.0 mMDRT. Precautionary wash and ream last 2 stands to bottom. Rotate and work string whilst circulating 1½ times bottoms up to condition mud until hole clean. Drill and survey hole from 3257.0 mMDRT to well TD of 3338.0 mMDRT. Rotate and work string whilst circulating 2½ times bottoms up to condition mud until hole clean. Rack 1 stand every ½ hr from 3338.0 mMDRT to 3257.0 mMDRT. Flow check, ok, pull out of hole with 4” drill pipe from 3257.0 mMDRT to 1620.0 mMDRT. Dress rig floor to 4” drill pipe and pull out of hole from 1620.0 mMDRT to 1050.0 mMDRT. |
| 05:00 AM UPDATE 23-10-2006. DEPTH AT 05:00 hours | Continue to pull out of hole from 1050.0 mMDRT to 708.0 mMDRT. Rotate and work string whilst circulating 2 times bottoms up until hole clean. Continue to pull out of hole with 4” drill pipe from 708.0 mMDRT to 595.0 mMDRT, Conduct rig sevice. Continue to pull out of hole with 4” drill pipe from 595.0 mMDRT to 192.0 mMDRT, rig to HWDP. Continue to pull out of hole with HWDP. Break down and rack back BHA. 3338.0 mMDRT (2382.0 mTVDRT) |