DRILLING / WELLWORK REPORT 24HRS TO 0500 HRS October 12, 2006

| RIG 453 | 146 | 363 |
| --- | --- | --- |
| CAMERON | 1622 | 1622 |
| HALLIBURTON | 3410 | 3410 |
| SCHLUMBERGER | 2351 | 2351 |
| ISDL | 147 | 647 |
| ISS | 136 | 2352 |

Well: WKF_W23A

Rig/Contractor: 	Rig 453	Report Date: October 12, 2006

Supervisor:	Campbell, Glenn R.

Davis, Brian

Stead, Cory

| AFE Number: | L0501G660 | Ave Angle: |  |
| --- | --- | --- | --- |
| Days to Complete: | 1.2 | AFE Cost/Days: | $5,948,157 |
| Daily Cost: | $267,609 |  |  |
| Total Cost: | $301,147 | Planned MD/TVD: | 3339.00/3004.71 |
| Casing Size: |  | Actual MD/TVD: | 672.00/636.88 |
| Mud Weight: |  | Tubing Size: |  |

| Objective: | WKF_W23A |
| --- | --- |
| Management Summary: | Pressure Tested BOP's. Mixed new mud system. Ran Wear Bushing. Changed out TDS saver sub. Made up and shallow tested 8½" steerable BHA. RIH and tagged TOC @ 605m. Conducted Power Choke Drill and displaced to 9.0 ppg mud. Drilled out cement to 651m. Recorded SCR's. Drilled 8½" hole to 660m. Time drilled and kicked off the cement plug from 660m to 672m. Circulated and conditioned mud. Conducted PIT to 12.5 ppg EMW. |
| Current: | Conducting PIT |
| Planned: | Drill & Survey 8½" Production Hole. |