DRILLING / WELLWORK REPORT 24HRS TO 0500 HRS JANUARY 26, 2007

SAFETY:

DAYS SINCE LAST TRI:	PREVIOUS BEST TRI PERIOD

| ISDL RIG 453 | 252 | 363 |
| --- | --- | --- |
| ISDL RIG 175 | 176 | 176 |
| CAMERON | 1727 | 1727 |
| HALLIBURTON | 3531 | 3531 |
| SCHLUMBERGER | 2436 | 2436 |
| ISS | 244 | 2357 |

Well: HLA_A4

Rig/Contractor: 	Rig 453	Report Date: January 26, 2007

Supervisor:	Stead, Cory

Bigby, Brigham

| AFE Number: AFE Number: | L0501H209 | Ave Angle: |  |
| --- | --- | --- | --- |
| Days to Complete: | 2.0 | AFE Cost/Days: | $800,000 |
| Daily Cost: | $208,332 |  |  |
| Total Cost: | $404,180 | Planned MD/TVD: |  |
| Casing Size: |  | Actual MD/TVD: |  |
| Mud Weight: |  | Tubing Size: |  |

| Objective: | HLA_A4 |
| --- | --- |
| Management Summary: | R/U slickline. RIH, retrieve SSSV at 123m MDWL & POOH. RIH, retrieve B-mandrel at 772 m MDWL & POOH. RIH & set x-plug at 1452m MDWL. R/U & run gyro. RIH & set B-mandrel w/ bull plug at 772m MDWL. Test plugs to 1000 psi. RIH & set SSSV at 123m MDWL. Rig released to HLA A24 drill well. |
| Current: | Rig released to HLA A24. Preparing to skid rig. |
| Planned: | Skid to A24 well centre. Install mud pump. N/U diverter. M/U BHA, RIH & test diverter. Drill out cement. Shoot gyro. Circ. well to flocculated gelled SW. Drill 12-1/4" hole section. |