DRILLING / WELLWORK REPORT 24HRS TO 0500 HRS JANUARY 30, 2007

SAFETY:

DAYS SINCE LAST TRI:	PREVIOUS BEST TRI PERIOD

| ISDL RIG 453 | 256 | 363 |
| --- | --- | --- |
| ISDL RIG 175 | 178 | 178 |
| CAMERON | 1731 | 1731 |
| HALLIBURTON | 3535 | 3535 |
| SCHLUMBERGER | 2440 | 2440 |
| ISS | 2478 | 2357 |

Well: HLA_A4

Rig/Contractor: 	Rig 453	Report Date: January 30, 2007

Supervisor:	Stead, Cory

Bigby, Brigham

| AFE Number: AFE Number: | L0501G208 | Ave Angle: |  |
| --- | --- | --- | --- |
| Days to Complete: | 6.5 | AFE Cost/Days: | $6,507,763 |
| Daily Cost: | $208,529 |  |  |
| Total Cost: | $1,327,737 | Planned MD/TVD: | 2,984.99/ |
| Casing Size: |  | Actual MD/TVD: |  |
| Mud Weight: |  | Tubing Size: |  |

| Objective: | HLA_A24 |
| --- | --- |
| Management Summary: | PTSM's. Wait on weather. L/out BHA on pipedeck. M/up jetting BHA and RIH. Tag TOC @ 177.5m. Displace well to gell based sea water. Jet drill and survey to 269m. POOH w/ jetting BHA from 269m to 150m. Repair mud pump #2 suction problem. |
| Current: | POOH w/ jetting BHA. |
| Planned: | POOH w/ jetting BHA. M/up steerable BHA. RIH |