LAKES OIL N.L

DAILY DRILLING REPORT

| WELL : | Hazelwood-1 | REPORT No. : | 30 | DFS: | 29 | DATE : | 22-04-07 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 2400 DEPTH : | 1920m | LAST DEPTH : | 1889m | 24 HR PROGRESS: | 31m | PTD : | 2,700 |
| TOTAL FUEL : | 13,600 | FUEL USAGE : | 1,600 | DAYCOST : $ |  | CUM. COST : $ |  |
| 0600 OPS : | Drilled 216mm hole from 1920m to 1943m |
| Next 24 Hrs Op | Drill ahead |
| Site Personnel: | Lou DeVattimo - Supervisor |

| BIT INFORMATION |  | OPS BREAKDOWN |  | MUD PROPERTIES |
| --- | --- | --- | --- | --- |
| Bit Number | 7 | Core Bit # 1 |  | Drilling | 9.5 |  | Density | 1.104 | S.G. |
| Size (mm) | 216 | 216mm |  | Tripping | 10.5 |  | Viscosity | 40 | Sec |
| Make | Reed | Corpro |  | Surveys |  |  | Water Loss | 8.0 | Cc |
| Type | TD41A | PDC |  | Sip & Cut block line | 1.0 |  | pH | 10.5 | Strip |
| IADC Code | 4-1-7 | M626 |  | Wash and ream | 1.0 |  | Filter Cake | 1 | 32 nd |
| Serial Number | BN4935 | CM468 |  | Circulate Sample |  |  | PV / YP | 7 / 7 | Cp/lb/100’ |
| Nozzles (32) | 14-14-14 |  |  | Casing |  |  | Gels | 1 / 2 | S/m |
| Depth in (m) | 1889 | 1886 |  | Cementing |  |  | Sand | tr | % Vol |
| Depth out (m) |  |  |  | BOP |  |  | Solids | 6.1 | % Vol |
| Total Metres | 31 | 3.00 |  | Circulate & Condition |  |  | Oil |  | % Vol |
| Hours | 9.5 | 1.5 |  | Rig Service |  |  | K+ |  | Mg/l |
| WOB (kg) | 12.5 | 6000 |  | Make up BHA |  |  | Chlorides | 1,100 | Mg/l |
| RPM | 90 | 70 |  | Drill out Cmt |  |  | PHPA | 0.09 |  |
| Condition |  | No wear |  | Repair rig |  |  | KCL |  |  |
| Impact Force | 216 |  |  | Wait On Cement |  |  | Daily Cost $ | 155 |
| Jet Velocity | 178 |  |  | Coring | 2.0 |  | Cum Cost $ | 52,279 |
| B.H.A.: 8 | 216mm Bit-Bit Sub - NMDC--Stab-11 x 6- 1/4” Drill Collar-Jars- 1 x 6-1/4’ Drill Collars- 4 x HWDP |
| HOURLY OPERATIONS SUMMARY (0000 – 2400) |  | SURVEYS |  | CHEMICALS USED |
| From | To | Operation |  | 39.5@108 | ° at | 1628 | m |  | Type | Amount |
| 0000 | 04:30 | Tripped out with core barrel |  | 43 @ 110 | ° at | 1722 | m |  | Aus-Gel |  |
| 04:30 | 06:30 | Remove inner barrel then layed out the core barrel |  | 45@ 113 | ° at | 1778 | m |  | Pac L |  |
| 06:30 | 10;30 | Tripped in hole to shoe with 216mm bit |  | 40@ 114 | ° at | 1874 | m |  | Pac - R | 1 |
| 10:30 | 11:30 | Slipped and cut block-line |  | 20 | ° at | 1340 | m |  | Barite |  |
| 11;30 | 13:30 | Tripped in hole from shoe to 1863m |  | 20 plus | ° at | 1440 | m |  | Citric acid |  |
| 13:30 | 14:30 | Picked up Kelly washed and reamed to 1889m |  | 28.5 | ° at | 1460 | m |  | PHPA/ KCL |  |
| 14;30 | 24:00 | Drilled 216mm hole from 1889m to 1920m |  | 37 | ° at | 1553 | m |  | Caustic Soda |  |
|  |  |  |  | PUMP 1 |  | PUMP 2 |
|  |  |  |  | Liner | 108 | mm |  | Liner | 108 | mm |
|  |  |  |  | Pressure | 16,000 | kPa |  | Pressure |  | KPa |
|  |  |  |  | A.V. DP | 118 | f/min |  | A.V. DP |  | f/min |
|  |  |  |  | A.V. DC | 186 | f/min |  | A.V. DC |  | f/min |
|  |  | Coring equipment arrived 19th April ex Perth |  | SPM | 120 |  | SPM |  |
|  |  |  |  | GPM | 251 |  | GPM |  |
|  |  |  |  | CEMENT DATA |  | LAST CASING |
|  |  |  |  | Sacks Halliburton | 900 |  | Size | 244 | mm |
|  |  |  |  | Class Bulk |  |  | Weight | 36 | Lb/ft |
|  |  |  |  | % |  |  |  | Grade | K-55 |  |
|  |  |  |  | % |  |  |  | Connection | B.T.C |  |
|  |  |  |  | % |  |  |  | Joints | 110 |  |
|  |  |  |  | % |  |  |  | Length | 1291.00 | m |
| Days since | LTA | 329 |  | Av. Wt |  |  | Shoe | 1296m from RKB | m |

,66