LAKES OIL N.L

DAILY DRILLING REPORT

| WELL : | Hazelwood-1 | REPORT No. : | 32 | DFS: | 31 | DATE : | 24-04-07 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 2400 DEPTH : | 2006m | LAST DEPTH : | 2006m | 24 HR PROGRESS: | 0m | PTD : | 2,700 |
| TOTAL FUEL : | 15,500 | FUEL USAGE : | 2,100 | DAYCOST : $ |  | CUM. COST : $ |  |
| 0600 OPS : | Rig on repair rate waiting on engine transmission to arrive |
| Next 24 Hrs Op | Repair rig then trip in hole from shoe to bottom at 2006m and drill ahead with 194mm bit |
| Site Personnel: | Lou DeVattimo - Supervisor |

| BIT INFORMATION |  | OPS BREAKDOWN |  | MUD PROPERTIES |
| --- | --- | --- | --- | --- |
| Bit Number | 7 | 8 |  | Drilling |  |  | Density | 1.128 | S.G. |
| Size (mm) | 216 | 194 |  | Tripping |  |  | Viscosity | 44 | Sec |
| Make | Reed | Reed |  | Surveys |  |  | Water Loss | 8.0 | Cc |
| Type | TD41A | E4478PC |  | Sip & Cut block line |  |  | pH | 10.5 | Strip |
| IADC Code | 4-1-7 |  |  | Wash and ream |  |  | Filter Cake | 1 | 32 nd |
| Serial Number | BN4935 | A50984 |  | Circulate Sample |  |  | PV / YP | 9 / 6 | Cp/lb/100’ |
| Nozzles (32) | 14-14-14 | 16-16-16- 16 |  | Casing |  |  | Gels | 2 / 3 | S/m |
| Depth in (m) | 1889 | 2006 |  | Cementing |  |  | Sand | tr | % Vol |
| Depth out (m) |  |  |  | BOP |  |  | Solids | 7.5 | % Vol |
| Total Metres | 116 |  |  | Circulate & Condition |  |  | Oil |  | % Vol |
| Hours | 32.5 |  |  | Rig Service |  |  | K+ |  | Mg/l |
| WOB (kg) | 12.5 |  |  | Make up BHA |  |  | Chlorides | 1,100 | Mg/l |
| RPM | 90 |  |  | Drill out Cmt |  |  | PHPA | 0.08 |  |
| Condition | BT-BT-CT-A-E-I-NO-RIG |  |  | Repair rig | 24.00 |  | KCL |  |  |
| Impact Force | 216 |  |  | Wait On Cement |  |  | Daily Cost $ | 325 |
| Jet Velocity | 178 |  |  | Coring |  |  | Cum Cost $ | 53,380 |
| B.H.A.: 9 | 194mm Bit-Bit Sub - NMDC-- -7 x 6- 1/4” Drill Collar-Jars- 1 x 6-1/4’ Drill Collars- 6 x HWDP 148.67m |
| HOURLY OPERATIONS SUMMARY (0000 – 2400) |  | SURVEYS |  | CHEMICALS USED |
| From | To | Operation |  | 39.5@108 | ° at | 1628 | m |  | Type | Amount |
| 0000 |  | Stopped drilling due to only one engine operative |  | 43 @ 110 | ° at | 1722 | m |  | Aus-Gel |  |
|  | 01:30 | Pulled out and layed out 13 jnts pipe using the Kelly |  | 45@ 113 | ° at | 1778 | m |  | Pac L |  |
| 01:30 | 03:30 | Tripped back to the shoe |  | 40@ 114 | ° at | 1874 | m |  | Pac - R | 5 |
| 03:30 | 04:00 | Cleared the rig floor |  | 40@ 112 | ° at | 1950 | m |  | Barite |  |
| 04:00 | 15:00 | Removed the transmission from rig motor # 1 |  | 20 plus | ° at | 1440 | m |  | Citric acid |  |
| 15:00 | 17:00 | Pumped slug then tripped out to 168m |  | 28.5 | ° at | 1460 | m |  | PHPA/ KCL |  |
| 17:00 | 17:30 | Layed out 4 drill collars and the stabilizer |  | 37 | ° at | 1553 | m |  | Caustic Soda |  |
| 17:30 | 18:30 | Repaired drive shaft |  |  |  |  |
| 18:30 | 21:00 | Made up 194mm bit and new BHA |  | PUMP 1 |  | PUMP 2 |
| 21:00 | 23:00 | Tripped in hole to 1292m |  | Liner | 108 | mm |  | Liner | 108 | mm |
| 23:00 | 24:00 | Picked up Kelly broke circulation secured well |  | Pressure | 16,000 | kPa |  | Pressure |  | KPa |
|  |  |  |  | A.V. DP | 118 | f/min |  | A.V. DP |  | f/min |
|  |  |  |  | A.V. DC | 186 | f/min |  | A.V. DC |  | f/min |
|  |  | Rig on repair rate for 24 hrs and until drilling assembly |  | SPM | 120 |  | SPM |  |
|  |  | on bottom and drilling again |  | GPM | 251 blocked jet |  | GPM |  |
|  |  |  |  | CEMENT DATA |  | LAST CASING |
|  |  |  |  | Sacks Halliburton | 900 |  | Size | 244 | mm |
|  |  |  |  | Class Bulk |  |  | Weight | 36 | Lb/ft |
|  |  |  |  | % |  |  |  | Grade | K-55 |  |
|  |  |  |  | % |  |  |  | Connection | B.T.C |  |
|  |  |  |  | % |  |  |  | Joints | 110 |  |
|  |  |  |  | % |  |  |  | Length | 1291.00 | m |
| Days since | LTA | 332 |  | Av. Wt |  |  | Shoe | 1296m from RKB | m |

,66