LAKES OIL N.L

DAILY DRILLING REPORT

| WELL : | Hazelwood-1 | REPORT No. : | 34 | DFS: | 33 | DATE : | 26-04-07 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 2400 DEPTH : | 2061m | LAST DEPTH : | 2013m | 24 HR PROGRESS: | 47m | PTD : | 2,700 |
| TOTAL FUEL : | 12,000 | FUEL USAGE : | 2,500 | DAYCOST : $ |  | CUM. COST : $ |  |
| 0600 OPS : | Drilling 194mm hole from 2052m to 2061m |
| Next 24 Hrs Op | Drill ahead |
| Site Personnel: | Lou De-Vattimo - Supervisor |

| BIT INFORMATION |  | OPS BREAKDOWN |  | MUD PROPERTIES |
| --- | --- | --- | --- | --- |
| Bit Number | 7 | 8 |  | Drilling | 24.00 |  | Density | 1.140 | S.G. |
| Size (mm) | 216 | 194 |  | Tripping |  |  | Viscosity | 41 | Sec |
| Make | Reed | Reed |  | Surveys |  |  | Water Loss | 7.5 | Cc |
| Type | TD41A | E4478PC |  | Sip & Cut block line |  |  | pH | 9.5 | Strip |
| IADC Code | 4-1-7 |  |  | Wash and ream |  |  | Filter Cake | 1 | 32 nd |
| Serial Number | BN4935 | A50984 |  | Circulate Sample |  |  | PV / YP | 9 / 8 | Cp/lb/100’ |
| Nozzles (32) | 14-14-14 | 16-16-16- 16 |  | Casing |  |  | Gels | 2 / 3 | S/m |
| Depth in (m) | 1889 | 2006 |  | Cementing |  |  | Sand | tr | % Vol |
| Depth out (m) |  |  |  | BOP |  |  | Solids | 8.2 | % Vol |
| Total Metres | 116 | 54 |  | Circulate & Condition |  |  | Oil |  | % Vol |
| Hours | 32.5 | 26.5 |  | Rig Service |  |  | K+ |  | Mg/l |
| WOB (kg) | 12.5 | 12.5 |  | Make up BHA |  |  | Chlorides | 1,100 | Mg/l |
| RPM | 90 |  |  | Drill out Cmt |  |  | PHPA | 0.08 |  |
| Condition | BT-BT-CT-A-E-I-NO- |  |  | Repair rig |  |  | KCL |  |  |
| Impact Force | 216 | 223 |  | Wait On Cement |  |  | Daily Cost $ | 931 |
| Jet Velocity | 178 | 137 |  | Coring |  |  | Cum Cost $ | 54,311 |
| B.H.A.: 9 | 194mm Bit-Bit Sub - NMDC-- -7 x 6- 1/4” Drill Collar-Jars- 1 x 6-1/4’ Drill Collars- 6 x HWDP 148.67m |
| HOURLY OPERATIONS SUMMARY (0000 – 2400) |  | SURVEYS |  | CHEMICALS USED |
| From | To | Operation |  | 39.5@108 | ° at | 1628 | m |  | Type | Amount |
| 0000 | 24;00 | Drilled 194mm hole from 2013m to 2052m |  | 43 @ 110 | ° at | 1722 | m |  | Aus-Gel |  |
|  |  |  |  | 45@ 113 | ° at | 1778 | m |  | Pac L |  |
|  |  |  |  | 40@ 114 | ° at | 1874 | m |  | Pac - R | 6 |
|  |  |  |  | 40@ 112 | ° at | 1950 | m |  | Barite |  |
|  |  |  |  |  | ° at |  | m |  | Citric acid |  |
|  |  |  |  |  | ° at |  | m |  | PHPA/ KCL |  |
|  |  |  |  |  | ° at |  | m |  | Caustic Soda |  |
|  |  |  |  | PUMP 1 |  | PUMP 2 |
|  |  |  |  | Liner | 108 | mm |  | Liner | 108 | mm |
|  |  |  |  | Pressure | 5,600 | kPa |  | Pressure | 5,600 | KPa |
|  |  |  |  | A.V. DP | 217 | f/min |  | A.V. DP | 217 | f/min |
|  |  |  |  | A.V. DC | 430 | f/min |  | A.V. DC | 430 | f/min |
|  |  |  |  | SPM | 80 |  | SPM | 80 |
|  |  |  |  | GPM | 162 |  | GPM | 162 |
|  |  |  |  | CEMENT DATA |  | LAST CASING |
|  |  |  |  | Sacks Halliburton | 900 |  | Size | 244 | mm |
|  |  |  |  | Class Bulk |  |  | Weight | 36 | Lb/ft |
|  |  |  |  | % |  |  |  | Grade | K-55 |  |
|  |  |  |  | % |  |  |  | Connection | B.T.C |  |
|  |  |  |  | % |  |  |  | Joints | 110 |  |
|  |  |  |  | % |  |  |  | Length | 1291.00 | m |
| Days since | LTA | 334 |  | Av. Wt |  |  | Shoe | 1296m from RKB | m |

,66