LAKES OIL N.L

DAILY DRILLING REPORT

| WELL : | Hazelwood-1 | REPORT No. : | 10 | DFS: | 9 | DATE : | 2-04-07 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 2400 DEPTH : | 951m | LAST DEPTH : | 895 | 24 HR PROGRESS: | 56m | PTD : | 2,700 |
| TOTAL FUEL : | 11,000 | FUEL USAGE : | 3,000 | DAYCOST : $ |  | CUM. COST : $ |  |
| 0600 OPS : | Drilled 311mm hole from 951m to 988m |
| Next 24 Hrs Op | Drill ahead –run survey –drill ahead |
| Site Personnel: | Lou DeVattimo - Supervisor |

| BIT INFORMATION |  | OPS BREAKDOWN |  | MUD PROPERTIES |
| --- | --- | --- | --- | --- |
| Bit Number | 1 | 2 |  | Drilling | 9.50 |  | Density | 1.062 | S.G. |
| Size (mm) | 400 | 311mm |  | Tripping |  |  | Viscosity | 29 | Sec |
| Make | Smith | Reed |  | Surveys |  |  | Water Loss | 20.0 | Cc |
| Type | GX-1VC | DX8-140A |  | Rigged up |  |  | pH | 9.0 | Strip |
| IADC Code | 2-1-7 | S323 |  | Testing/tools |  |  | Filter Cake | 1 | 32 nd |
| Serial Number | MM4714 | 206579 |  | Circulate Sample |  |  | PV / YP | 2/ 2 | Cp/lb/100’ |
| Nozzles (32) | 18-22-22 | 7 x 14 |  | Casing |  |  | Gels | 1 / 1 | S/m |
| Depth in (m) | 293.00 | 556 |  | Cementing |  |  | Sand | tr | % Vol |
| Depth out (m) | 556 |  |  | Surveys | 0.50 |  | Solids | 3.5 | % Vol |
| Total Metres | 263 | 395 |  | Circulate & Condition |  |  | Oil |  | % Vol |
| Hours | 30.00 | 68.5 |  | Rig Service |  |  | K+ |  | Mg/l |
| WOB (kg) | 5min-12max | 10-12 |  | Pick up BHA |  |  | Chlorides | 1,80 | Mg/l |
| RPM | 100 | 90 |  | Drill out Cmt |  |  | PHPA |  |  |
| Condition | T-2 B-2 In gauge |  |  | Repair rig | 14:00 |  | KCL | 0.5 % |  |
| Impact Force | 461 | 656 |  | Wait On Cement |  |  | Daily Cost $ | 325 |
| Jet Velocity | 176 | 263 |  | Test BOPs |  |  | Cum Cost $ | 14,473 |
| B.H.A.: | 311mm Bit-Bit Sub-N.B.S-2 x 8” Drill Collars- Stabilizer-Crossover sub- 8 x 6-1/4” Drill Collars-NMDC-2 x 6-1/4 Drill Collar- 4 x HWDP |
| HOURLY OPERATIONS SUMMARY (0000 – 2400) |  | SURVEYS |  | CHEMICALS USED |
| From | To | Operation |  | 8deg plus | ° at | 258 | m |  | Type | Amount |
| 0000 | 01:30 | Repaired V-Drive bearing housing ( Circulated ) |  | 12 deg | ° at | 319 | m |  | Aus-Gel |  |
| 01:30 | 03:00 | Drilled 311 mm hole from 895m to 904m |  | 11 deg | ° at | 357 | m |  | Dextrid |  |
| 03:00 | 06:00 | Chain drive on rotary drive collapsed (Circulated ) |  | 9 deg | ° at | 414 | m |  | Pac - R |  |
| 06:00 | 06:30 | Ran survey at 870m ( mis-run ) |  | 3 deg | ° at | 471 | m |  | Barite | 30 |
| 06:30 | 08:00 | Tripped back to shoe at 420m |  | 2 deg | ° at | 546 | m |  | Bulk Barite |  |
| 08:00 | 11:00 | Wait on chain parts to arrive |  | 2 deg | ° at | 581 | m |  | PHPA/ KCL |  |
| 11:00 | 13:00 | Repaired chain coupling |  | 1.5 deg | ° at | 742 | m |  | Caustic Soda |  |
| 13:00 | 14:30 | Tripped back in hole from 420m to 855m |  |  |  |  |
| 14:30 | 16:00 | Picked up Kelly then washed to bottom at 904m |  | PUMP 1 |  | PUMP 2 |
| 16:00 | 24:00 | Drilled 311mm hole from 904m to 951m |  | Liner | 108 | mm |  | Liner | 108 | mm |
|  |  |  |  | Pressure | 6,600 | kPa |  | Pressure | 6,600 | KPa |
|  |  |  |  | A.V. DP | 100 | f/min |  | A.V. DP | 100 | f/min |
|  |  |  |  | A.V. DC | 151 | f/min |  | A.V. DC | 151 | f/min |
|  |  |  |  | SPM | 127 |  | SPM | 127 |
|  |  |  |  | LPM | 1,200 |  | LPM | 1,200 |
|  |  |  |  | CEMENT DATA |  | LAST CASING |
|  |  |  |  | Sacks Halliburton |  |  | Size | 340 | mm |
|  |  |  |  | Class Bulk |  |  | Weight | 81 | Kg/m |
|  |  |  |  | % |  |  |  | Grade | K-55 |  |
|  |  |  |  | % |  |  |  | Connection | B.T.C |  |
|  |  |  |  | % |  |  |  | Joints | 38 |  |
|  |  |  |  | % |  |  |  | Length | 420.00 | m |
| Days since | LTA |  |  | Av. Wt |  |  | Shoe | 420 m from RKB | m |

,66