LAKES OIL N.L

DAILY DRILLING REPORT

| WELL : | Hazelwood-1 | REPORT No. : | 20 | DFS: | 19 | DATE : | 12-04-07 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 2400 DEPTH : | 1379m | LAST DEPTH : | 1335m | 24 HR PROGRESS: | 44m | PTD : | 2,700 |
| TOTAL FUEL : | 11,00 | FUEL USAGE : | 2,600 | DAYCOST : $ |  | CUM. COST : $ |  |
| 0600 OPS : | Drilled 216mm hole from 1379m to 1431m |
| Next 24 Hrs Op | Drill ahead - survey at 1440m |
| Site Personnel: | Lou DeVattimo - Supervisor |

| BIT INFORMATION |  | OPS BREAKDOWN |  | MUD PROPERTIES |
| --- | --- | --- | --- | --- |
| Bit Number | 4 |  |  | Drilling | 9.50 |  | Density | 1.092 | S.G. |
| Size (mm) | 216 |  |  | Tripping | 11.50 |  | Viscosity | 35 | Sec |
| Make | Reed |  |  | Surveys | 0.50 |  | Water Loss | 8.00 | Cc |
| Type | DSX-104GH |  |  | Sip & Cut block line | 1.50 |  | pH | 11.0 | Strip |
| IADC Code | M 223 |  |  | Wash and ream |  |  | Filter Cake | 1 | 32 nd |
| Serial Number | 109683 |  |  | Circulate Sample |  |  | PV / YP | 9 / 8 | Cp/lb/100’ |
| Nozzles (32) | 5 x 14 |  |  | Casing |  |  | Gels | 2 / 3 | S/m |
| Depth in (m) | 1298 |  |  | Cementing |  |  | Sand | tr | % Vol |
| Depth out (m) |  |  |  | Surveys |  |  | Solids | 5.3 | % Vol |
| Total Metres | 81 |  |  | Circulate & Condition | 1.00 |  | Oil |  | % Vol |
| Hours | 14.50 |  |  | Rig Service |  |  | K+ |  | Mg/l |
| WOB (kg) | 3,000 |  |  | Make up BHA |  |  | Chlorides | 1,800 | Mg/l |
| RPM | 100 |  |  | Drill out Cmt |  |  | PHPA | 0.15 |  |
| Condition |  |  |  | Repair rig |  |  | KCL |  |  |
| Impact Force | 352 |  |  | Wait On Cement |  |  | Daily Cost $ | 3,072 |
| Jet Velocity | 178 |  |  | F.I.T |  |  | Cum Cost $ | 42,556 |
| B.H.A.: 4 | 216mm PDC Bit-.Bit Sub-NMDC- Stab-1 x 6-1/4” Drill Collar-Stabilizer-12 x 6-1/4” Drill Collars-Jars- 2 x 6-1/4’ Drill Collars- 4 x HWDP |
| HOURLY OPERATIONS SUMMARY (0000 – 2400) |  | SURVEYS |  | CHEMICALS USED |
| From | To | Operation |  | 5 | ° at | 841 | m |  | Type | Amount |
| 0000 | 03;30 | Drilled 216mm hole from 1335m to 1350m |  | 3 | ° at | 944 | m |  | Aus-Gel |  |
| 03;30 | 04;00 | Ran survey on wireline |  | 6.5 | ° at | 1140 | m |  | Pac L |  |
| 04:00 | 04:30 | Drilled 216mm hole from 1350m to 1353m |  | 15 | ° at | 1268 | m |  | Pac - R | 17 |
| 04:30 | 05:30 | Circulated hole clean prior to trip out for BHA change |  | 20 | ° at | 1340 | m |  | Barite | 40 |
| 05;30 | 10:00 | Tripped out of hole |  |  | ° at |  | m |  | Citric acid |  |
| 10:00 | 10:30 | Changed position of stabilizer picked up one drill collar |  |  | ° at |  | m |  | PHPA/ KCL |  |
| 10:30 | 11:30 | Tripped back in hole to 450m |  |  | ° at |  | m |  | Caustic Soda |  |
| 11:30 | 12:30 | Pulled back out to re-arrange BHA |  |  |  |  |
| 12:30 | 13:00 | Changed BHA stabilizer positions |  | PUMP 1 |  | PUMP 2 |
| 13;00 | 16:30 | Tripped in hole to 1291m |  | Liner | 108 | mm |  | Liner | 108 | mm |
| 16:30 | 18:00 | Slipped and cut block line |  | Pressure | 5,600 | kPa |  | Pressure | 5,600 | KPa |
| 18;00 | 18;30 | Tripped in hole to1353m |  | A.V. DP | 197 | f/min |  | A.V. DP | 197 | f/min |
| 18;30 | 24:00 | Drilled 216mm hole from 1353m to `1379m |  | A.V. DC | 309 | f/min |  | A.V. DC | 309 | f/min |
|  |  |  |  | SPM | 100 |  | SPM | 100 |
|  |  |  |  | GPM | 210 |  | GPM | 210 |
|  |  |  |  | CEMENT DATA |  | LAST CASING |
|  |  |  |  | Sacks Halliburton | 900 |  | Size | 244 | mm |
|  |  |  |  | Class Bulk |  |  | Weight | 36 | Lb/ft |
|  |  |  |  | % |  |  |  | Grade | K-55 |  |
|  |  |  |  | % |  |  |  | Connection | B.T.C |  |
|  |  |  |  | % |  |  |  | Joints | 110 |  |
|  |  |  |  | % |  |  |  | Length | 1291.00 | m |
| Days since | LTA |  |  | Av. Wt |  |  | Shoe | 1296m from RKB | m |

,66