LAKES OIL N.L

DAILY DRILLING REPORT

| WELL : | Hazelwood-1 | REPORT No. : | 3 | DFS: | 2 | DATE : | 26-03-07 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 2400 DEPTH : | 556m | LAST DEPTH : | 483m(rkb) | 24 HR PROGRESS: | 73.00m | PTD : |  |
| TOTAL FUEL : |  | FUEL USAGE : |  | DAYCOST : $ |  | CUM. COST : $ |  |
| 0600 OPS : | Tripped out for Casing-Rigged up for casing-running 13-3/8” casing |
| Next 24 Hrs Op | Run casing shoe will be at 550.50m-cement same-W.O.C-install the BOP |
| Site Personnel: | Lou DeVattimo - Supervisor |

| BIT INFORMATION |  | OPS BREAKDOWN |  | MUD PROPERTIES |
| --- | --- | --- | --- | --- |
| Bit Number | 1 |  |  | Drilling | 15.0 |  | Density | 1.116 | S.G. |
| Size (mm) | 400 |  |  | Tripping | 3.5 |  | Viscosity | 42 | Sec |
| Make | Smith |  |  | Surveys |  |  | Water Loss | 13.5 | Cc |
| Type | GX-1VC |  |  | Rigged up |  |  | pH | 10.5 | Strip |
| IADC Code | 2-1-7 |  |  | Testing/tools |  |  | Filter Cake | 1 | 32 nd |
| Serial Number | MM4714 |  |  | Circulate Sample |  |  | PV / YP | 10 / 18 | Cp/lb/100’ |
| Nozzles (32) | 18-22-22 |  |  | Casing |  |  | Gels | 4 / 10 | S/m |
| Depth in (m) | 293.00 |  |  | Cementing |  |  | Sand | tr | % Vol |
| Depth out (m) | 556 |  |  | Surveys | 0.5 |  | Solids | 3.9 | % Vol |
| Total Metres | 263 |  |  | Circulate & Condition | 1.0 |  | Oil |  | % Vol |
| Hours | 30.00 |  |  | Rig Service | 0.5 |  | K+ |  | Mg/l |
| WOB (kg) | 5min-12max |  |  | Pick up BHA |  |  | Chlorides | 1,100 | Mg/l |
| RPM | 100 |  |  | Drill out Cmt |  |  | PHPA |  |  |
| Condition | T-2 B-2 In gauge |  |  | Repair rig | 3.5 |  | KCL | % |  |
| Impact Force | 461 |  |  | Wait On Cement |  |  | Daily Cost $ | 1,031 |
| Jet Velocity | 176 |  |  | Test BOPs |  |  | Cum Cost $ | 5,924 |
| B.H.A.: | 400mm Bit-Bit Sub-2 x 8” Drill Collars- Stabilizer-Crossover sub- 8 x 6-1/4” Drill Collars- 4 x HWDP |
| HOURLY OPERATIONS SUMMARY (0000 – 2400) |  | SURVEYS |  | CHEMICALS USED |
| From | To | Operation |  | 8deg plus | ° at | 258 | m |  | Type | Amount |
| 0000 | 06:00 | Drilled 400mm hole from 483m to 522m |  | 12 deg | ° at | 319 | m |  | Aus-Gel | 42 |
| 06:00 | 06:30 | Serviced the rig |  | 11 deg | ° at | 357 | m |  | Dextrid |  |
| 06:30 | 11:00 | Replaced broken rotary chain ( circulated worked pipe ) |  | 9 deg | ° at | 414 | m |  | Pac - R |  |
| 11:00 | 19:00 | Drilled 400mm hole from 522m to 556m casing depth |  | 3 deg | ° at | 471 | m |  | Barite | 50 |
| 19:00 | 20:00 | Ran survey on wireline at 546m |  | 2 deg | ° at | 546 | m |  | Bulk Barite |  |
| 20:00 | 22:30 | Wiper tripped hole to 270m with no problems |  |  | ° at |  | m |  | PHPA/ KCL |  |
| 22:30 | 23:00 | No fill on bottom pumped pill |  |  | ° at |  | m |  | Caustic Soda |  |
| 23:00 | 24:00 | Tripped out for Casing |  |  |  |  |
|  |  |  |  | PUMP 1 |  | PUMP 2 |
|  |  |  |  | Liner | 108 | mm |  | Liner | 108 | mm |
|  |  | Drilled into Strezlecki formation for Casing seat |  | Pressure | 4900 | kPa |  | Pressure | 4900 | KPa |
|  |  | 13-5/8” BOP arrived on site |  | A.V. DP | 18 | m/min |  | A.V. DP | 18 | m/min |
|  |  |  |  | A.V. DC | 20 | m/min |  | A.V. DC | 20 | m/min |
|  |  |  |  | SPM | 130 |  | SPM | 130 |
|  |  |  |  | LPM | 1,200 |  | LPM | 1,200 |
|  |  |  |  | CEMENT DATA |  | LAST CASING |
|  |  |  |  | Sacks Halliburton |  |  | Size | 450 | mm |
|  |  |  |  | Class Bulk |  |  | Weight |  | Kg/m |
|  |  |  |  | % |  |  |  | Grade | Line pipe |  |
|  |  |  |  | % |  |  |  | Connection | Welded |  |
|  |  |  |  | % |  |  |  | Joints |  |  |
|  |  |  |  | % |  |  |  | Length | 281.00 | m |
| Days since | LTA |  |  | Av. Wt |  |  | Shoe | 286.00 m from RKB | m |

,66