LAKES OIL N.L

DAILY DRILLING REPORT

| WELL : | Hazelwood-1 | REPORT No. : | 4 | DFS: | 3 | DATE : | 27-03-07 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 2400 DEPTH : | 556m | LAST DEPTH : | 556 | 24 HR PROGRESS: | 0 | PTD : | 2,700m |
| TOTAL FUEL : | 7,300 | FUEL USAGE : | 1,300 | DAYCOST : $ |  | CUM. COST : $ |  |
| 0600 OPS : | Wait on Cement- Cut off conductor pipe – Cut off landing joint to accommodate the weld- on Casing Bowl |
| Next 24 Hrs Op | Weld Casing bowl- Install the 13-5/8” BOP-Test same |
|  | Lou DeVattimo - Supervisor |

| BIT INFORMATION |  | OPS BREAKDOWN |  | MUD PROPERTIES |
| --- | --- | --- | --- | --- |
| Bit Number | 1 |  |  | Drilling |  |  | Density | 1.104 | S.G. |
| Size (mm) | 400 |  |  | Tripping | 3.00 |  | Viscosity | 38 | Sec |
| Make | Smith |  |  | Surveys |  |  | Water Loss | 15.00 | Cc |
| Type | GX-1VC |  |  | Rigged up |  |  | pH | 10.0 | Strip |
| IADC Code | 2-1-7 |  |  | Testing/tools |  |  | Filter Cake | 1 | 32 nd |
| Serial Number | MM4714 |  |  | Circulate Sample |  |  | PV / YP | 10 / 12 | Cp/lb/100’ |
| Nozzles (32) | 18-22-22 |  |  | Casing | 15.00 |  | Gels | 2 / 5 | S/m |
| Depth in (m) | 293.00 |  |  | Cementing | 4.00 |  | Sand | tr | % Vol |
| Depth out (m) | 556 |  |  | Surveys |  |  | Solids | 6.1 | % Vol |
| Total Metres | 263 |  |  | Circulate & Condition |  |  | Oil |  | % Vol |
| Hours | 30.00 |  |  | Rig Service |  |  | K+ |  | Mg/l |
| WOB (kg) | 5min-12max |  |  | Pick up BHA |  |  | Chlorides | 1,000 | Mg/l |
| RPM | 100 |  |  | Drill out Cmt |  |  | PHPA |  |  |
| Condition | T-2 B-2 In gauge |  |  | Repair rig |  |  | KCL | % |  |
| Impact Force | 461 |  |  | Wait On Cement | 2.00 |  | Daily Cost $ | Nil |
| Jet Velocity | 176 |  |  | Test BOPs |  |  | Cum Cost $ | 5,924 |
| B.H.A.: | 400mm Bit-Bit Sub-2 x 8” Drill Collars- Stabilizer-Crossover sub- 8 x 6-1/4” Drill Collars- 4 x HWDP |
| HOURLY OPERATIONS SUMMARY (0000 – 2400) |  | SURVEYS |  | CHEMICALS USED |
| From | To | Operation |  | 8deg plus | ° at | 258 | m |  | Type | Amount |
| 0000 | 03:00 | Continued trip out for running Casing |  | 12 deg | ° at | 319 | m |  | Aus-Gel |  |
| 03:00 | 05:00 | Rigged up to run 340mm Casing |  | 11 deg | ° at | 357 | m |  | Dextrid |  |
| 05:00 | 15:00 | Ran 38 jnts of Casing to 420m |  | 9 deg | ° at | 414 | m |  | Pac - R |  |
| 15:00 | 16:00 | Worked stuck casing string due to deviation of well |  | 3 deg | ° at | 471 | m |  | Barite |  |
| 16:00 | 18:30 | Circulated and worked Casing string with no success |  | 2 deg | ° at | 546 | m |  | Bulk Barite |  |
| 18:30 | 19:30 | Rigged up Halliburton , held safety meeting |  |  | ° at |  | m |  | PHPA/ KCL |  |
| 19:30 |  | Cemented Casing, displaced and bumped plug |  |  | ° at |  | m |  | Caustic Soda |  |
|  | 22:00 | cement returns to surface |  |  |  |  |
| 22:00 | 24:00 | Wait on cement |  | PUMP 1 |  | PUMP 2 |
|  |  |  |  | Liner | 108 | mm |  | Liner | 108 | mm |
|  |  | Ran 38 jnts of 340mm Casing |  | Pressure |  | kPa |  | Pressure |  | KPa |
|  |  | 15 jnts left on site |  | A.V. DP |  | m/min |  | A.V. DP |  | m/min |
|  |  |  |  | A.V. DC |  | m/min |  | A.V. DC |  | m/min |
|  |  |  |  | SPM |  |  | SPM |  |
|  |  |  |  | LPM |  |  | LPM |  |
|  |  |  |  | CEMENT DATA |  | LAST CASING |
|  |  |  |  | Sacks Halliburton |  |  | Size | 340 | mm |
|  |  |  |  | Class Bulk |  |  | Weight | 81 | Kg/m |
|  |  |  |  | % |  |  |  | Grade | K-55 |  |
|  |  |  |  | % |  |  |  | Connection | Buttress |  |
|  |  |  |  | % |  |  |  | Joints | 38 |  |
|  |  |  |  | % |  |  |  | Length | 420.00 m RKB |  |
| Days since | LTA |  |  | Av. Wt |  |  | Shoe | 286.00 m from RKB | m |

,66