LAKES OIL N.L

DAILY DRILLING REPORT

| WELL : | Hazelwood-1 | REPORT No. : | 5 | DFS: | 4 | DATE : | 28-03-07 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 2400 DEPTH : | 556m | LAST DEPTH : | 556 | 24 HR PROGRESS: | 0 | PTD : | 2,700m |
| TOTAL FUEL : | 26,600 | FUEL USAGE : | 860 | DAYCOST : $ |  | CUM. COST : $ |  |
| 0600 OPS : | Completed the installation of BOP |
| Next 24 Hrs Op | Install the Koomey lines –Function test all lines-Test BOP and Choke Manifold-Make up and run 311mm Drilling assembly |
|  | Lou DeVattimo - Supervisor |

| BIT INFORMATION |  | OPS BREAKDOWN |  | MUD PROPERTIES |
| --- | --- | --- | --- | --- |
| Bit Number | 1 |  |  | Drilling |  |  | Density | 1.104 | S.G. |
| Size (mm) | 400 |  |  | Tripping |  |  | Viscosity | 38 | Sec |
| Make | Smith |  |  | Surveys |  |  | Water Loss | 15.00 | Cc |
| Type | GX-1VC |  |  | Rigged up |  |  | pH | 10.0 | Strip |
| IADC Code | 2-1-7 |  |  | Testing/tools |  |  | Filter Cake | 1 | 32 nd |
| Serial Number | MM4714 |  |  | Circulate Sample |  |  | PV / YP | 10 / 12 | Cp/lb/100’ |
| Nozzles (32) | 18-22-22 |  |  | Casing |  |  | Gels | 2 / 5 | S/m |
| Depth in (m) | 293.00 |  |  | Cementing |  |  | Sand | tr | % Vol |
| Depth out (m) | 556 |  |  | Surveys |  |  | Solids | 6.1 | % Vol |
| Total Metres | 263 |  |  | Circulate & Condition |  |  | Oil |  | % Vol |
| Hours | 30.00 |  |  | Rig Service |  |  | K+ |  | Mg/l |
| WOB (kg) | 5min-12max |  |  | Pick up BHA |  |  | Chlorides | 1,000 | Mg/l |
| RPM | 100 |  |  | Drill out Cmt |  |  | PHPA |  |  |
| Condition | T-2 B-2 In gauge |  |  | Repair rig |  |  | KCL | % |  |
| Impact Force | 461 |  |  | Wait On Cement | 4.0 |  | Daily Cost $ | Nil |
| Jet Velocity | 176 |  |  | Rig up BOPs | 20.0 |  | Cum Cost $ | 5,924 |
| B.H.A.: |  |
| HOURLY OPERATIONS SUMMARY (0000 – 2400) |  | SURVEYS |  | CHEMICALS USED |
| From | To | Operation |  | 8deg plus | ° at | 258 | m |  | Type | Amount |
| 0000 |  | W.O.C- Rigged down Casing tools – Halliburton tools |  | 12 deg | ° at | 319 | m |  | Aus-Gel |  |
|  |  | Installed Kill and Choke line valves onto mud cross- |  | 11 deg | ° at | 357 | m |  | Dextrid |  |
|  | 13:00 | Cut off conductor pipe and 13-3/8” landing joint |  | 9 deg | ° at | 414 | m |  | Pac - R |  |
| 13;00 | 18:00 | Installed the weld on 13-5/8” casing bowl welded same |  | 3 deg | ° at | 471 | m |  | Barite |  |
| 18:00 |  | Rigged up the BOP trolley guide the installed the DSA- |  | 2 deg | ° at | 546 | m |  | Bulk Barite |  |
|  | 24:00 | Mud cross-with kill and choke valves and BOP |  |  | ° at |  | m |  | PHPA/ KCL |  |
|  |  |  |  |  | ° at |  | m |  | Caustic Soda |  |
|  |  |  |  | PUMP 1 |  | PUMP 2 |
|  |  |  |  | Liner | 108 | mm |  | Liner | 108 | mm |
|  |  |  |  | Pressure |  | kPa |  | Pressure |  | KPa |
|  |  |  |  | A.V. DP |  | m/min |  | A.V. DP |  | m/min |
|  |  |  |  | A.V. DC |  | m/min |  | A.V. DC |  | m/min |
|  |  |  |  | SPM |  |  | SPM |  |
|  |  |  |  | LPM |  |  | LPM |  |
|  |  |  |  | CEMENT DATA |  | LAST CASING |
|  |  |  |  | Sacks Halliburton |  |  | Size | 340 | mm |
|  |  |  |  | Class Bulk |  |  | Weight | 81 | Kg/m |
|  |  |  |  | % |  |  |  | Grade | K-55 |  |
|  |  |  |  | % |  |  |  | Connection | Buttress |  |
|  |  |  |  | % |  |  |  | Joints | 38 |  |
|  |  |  |  | % |  |  |  | Length | 420.00 m RKB |  |
| Days since | LTA |  |  | Av. Wt |  |  | Shoe | 286.00 m from RKB | m |

,66