| PETRO TECH PTY LTD A.B.N. 009 116 429 | Registered Office: Level 11, 500 Collins Street, Melbourne, Vic. 3000 Phone: (03) 9629 1566 | Postal Address PO Box 300, Collins Street West Melbourne Vic. 8007 Fax: (03) 9629 1624 |
| --- | --- | --- |

# Hazelwood-1 (Stage 2) Wellsite

# via Morwell

April 11th 2007

# Hazelwood-1 (stage two) Drilling Report #18 – April 11th 2007

Well History

Site works commenced on the 22nd January with the levelling of the pad, the placing of the gravel and the excavating of the sumps and flare pit. The first stage of drilling at Hazelwood-1 commenced on Friday 23rd February with the Drilltec Cardwell HL rig drilling the surface hole to a depth of 288m before running the 450mm (18”) surface casing to 281m. The Drilltec rig was moved off site and the Century#11 rig commenced mobilising to the site and rigging up on Monday 19th March with the drilling of stage 2 commencing at 6pm on Saturday 24th March.

24 Hour Progress

At 6am this morning the contractor was drilling out the cement in the casing at a depth of 1030m. After completing the pressure testing of the BOP the 8-1/2” drilling assembly was made up and run into the hole to the top of the cement. The top of the cement was encountered at 815m indicating that there was approximately 480m of cement remaining in the casing due to the packing off during the pumping process. Enough cement was pumped out of the casing for the top of the cement to reach above the top of the Strzelecki Formation and into the 16” hole. The excess drillpipe was laid out and the bit was run back to the bottom to commence drilling out the cement. A number of surveys were run on the way down and during the drilling of the cement, to give an accurate profile of the holes deviation and direction, confirming the previous results.

Next 24 Hours

Continue to drill out the cement down to the casing shoe at 1298m, taking surveys at approximately 1140m and 1240m, before drilling 3m of new hole and conducting the Formation Integrity Test (FIT) then drilling ahead in 8-1/2” hole towards TD.

Safety and Environment

No safety or environmental incidents have occurred in the past 24hrs.

Tim O’Brien

Operations Manager

Lakes Oil N.L. as operator for Petro Tech Pty Ltd