| PETRO TECH PTY LTD A.B.N. 009 116 429 | Registered Office: Level 11, 500 Collins Street, Melbourne, Vic. 3000 Phone: (03) 9629 1566 | Postal Address PO Box 300, Collins Street West Melbourne Vic. 8007 Fax: (03) 9629 1624 |
| --- | --- | --- |

# Hazelwood-1 (Stage 2) Wellsite

# via Morwell

April 14th 2007

# Hazelwood-1 (stage two) Drilling Report #21 – April 14th 2007

Well History

Site works commenced on the 22nd January with the levelling of the pad, the placing of the gravel and the excavating of the sumps and flare pit. The first stage of drilling at Hazelwood-1 commenced on Friday 23rd February with the Drilltec Cardwell HL rig drilling the surface hole to a depth of 288m before running the 450mm (18”) surface casing to 281m. The Drilltec rig was moved off site and the Century#11 rig commenced mobilising to the site and rigging up on Monday 19th March with the drilling of stage 2 commencing at 6pm on Saturday 24th March.

24 Hour Progress

At 6am this morning the contractor was circulating the hole prior to pulling out of the hole to change the drill bit due to slow drill rate. The hole was drilled to a depth of 1487m having progressed 56m in the past 24hrs. A survey taken at 1460m (28.5º) indicated that the hole had continued to deviate despite the attempts to correct it suggesting the rocks are dipping at a relatively high angle. Over 6hrs was lost due to the rotary drive chain on the V drive breaking and the bit was pulled back into the shoe while it was repaired. Once the rotary drive was repaired and the bit run back to bottom the drilling rate was very slow (1-2m/hr) suggesting the rock had become too hard for the PDC bit to penetrate despite varying the drilling parameters. It was then decided to pull out of the hole and to remove the PDC bit and to run in with the tri-cone insert bit to attempt to achieve a greater penetration rate. The geology remained very similar to previous days being predominantly green grey claystone with minor laminated sandstones with background gas levels up to 0.2 units (C1 100%).

Next 24 Hours

Continue to pull out of the hole to change the drill bit before running back in and drilling ahead in 8-1/2” hole towards TD.

Safety and Environment

No safety or environmental incidents have occurred in the past 24hrs.

Tim O’Brien

Operations Manager

Lakes Oil N.L. as operator for Petro Tech Pty Ltd