DRILLING / WELLWORK REPORT 24HRS TO 0500 HRS December 21, 2006

SAFETY:

DAYS SINCE LAST TRI:	PREVIOUS BEST TRI PERIOD

| RIG 453 | 216 | 363 |
| --- | --- | --- |
| CAMERON | 1683 | 1683 |
| HALLIBURTON | 3470 | 3470 |
| SCHLUMBERGER | 2412 | 2412 |
| ISDL | 216 | 647 |
| ISS | 204 | 2357 |

Well: HLA_A2A

Rig/Contractor: 	Rig 453	Report Date: December 21, 2006

Supervisor:	Bennett, James M

Steel, George A

| AFE Number: AFE Number: | 40000466 | Ave Angle: |  |
| --- | --- | --- | --- |
| Days to Complete: | 2.33 | AFE Cost/Days: | $1,967,822 |
| Daily Cost: | $177,224 |  |  |
| Total Cost: | $423,126 | Planned MD/TVD: |  |
| Casing Size: |  | Actual MD/TVD: |  |
| Mud Weight: |  | Tubing Size: |  |

| Objective: | HLA_A2A |
| --- | --- |
| Management Summary: | PTSM's. Conduct Hazard hunt. Continue with rig up of HES w/line equipment. N/up w/line Totco BOP/riser/lubricator & run hi-pressure lines. Howco p/test lines & BOP/riser/lubricator to 300/3000psi, solid. Bullhead well with s/water at 8 bbls/min, pump total of 167 bbls. HES RIH with 3.688" RN plug, set @ 2216m (w/line depth) and P/test to 1000psi/15 mins, solid. RIH to latch GLV @ 756m, pull free & POOH. Line up to effluent line. Displace PA to effluent line with 105 bbls s/water, check returns, hydrocarbon clear. RIH & set DGLV in SPM @ 756m. P/test tbg to 1000psi/15mins (0.8bbls) with PA open to atmosphere, solid test. P/test PA to 1000psi /15mins(1.0bbls), solid.. Stand back HES w/line lub & l/out riser jnt. Cameron install BPV in the tubing hanger w/ dry rod. Nipple down the xmas tree and THAF whilst install choke line to BOP's. P/test BOP's off critical path. Crane down due to high winds. |
| Current: | Nipple down Xmas tree. |
| Planned: | Nipple up riser/BOP. |