Longtom- 3 ST1

| Date: | 05-08-2006 | Last Casing: | 406 mm (16”) @ 995.32 mMDRT |
| --- | --- | --- | --- |
| Report Number: | 6 | Leak Off Test: | 1.62 sg EMW @ 1008.0 mMDRT |
| Report Period: | 24hrs to 24:00 | Current hole size: | 343 mm (13½ ”) |
| Depth @ 2400 Hrs: | 2098m | Mud Weight: | 1.44 sg |
| Last Depth: | 1727m | ECD: | 1.47 sg |
| Progress: | 371m | Mud Type: | SBM Petrofree |
| TD Lithology: | Siltstone and Claystone | V: 6 / 3 | 14 / 13 |
| Water Depth: | 56.0 m | Mud Fluid Loss: | 3.4 cc |
| RT Elevation: | 21.5 m | Bit Type: | Smith PDC MRG75 TFA 1.74 |

OPERATIONS SUMMARY

| 24 HOUR SUMMARY 00:00 - 24:00: | Ran in the hole to the shoe. Serviced the drilling equipment. Ran in the hole to 1697mrt. Reamed f/ 1697 to 1727mrt (TD). Drilled ahead 13 1/2" directional hole f/ 1727 to 1981mMDRT. Circulated out drilled gas (36%). Drilled ahead f/ 1981 to 2098mMDRT. |
| --- | --- |
| 06:00 Update | Drilling ahead 13 1/2" hole at 2181m in the Admiral Formation 400 sands. |
| NEXT 24 HOURS: | Drill ahead 13 1/2” hole through the Admiral Formation 400, 300 and 100 sands and into the Emperor Volcanics. |

GEOLOGICAL SUMMARY

LITHOLOGIC DESCRIPTION:

| Interval mMDRT | Description |
| --- | --- |
| 1727-1780 ROP: 3.0 – 70.2 m/hr Av: 23.0 m/hr | Massive Claystone with minor Sandstone CLAYSTONE (50-90%): medium – dark grey, brownish grey, rare medium to light grey, soft – firm, sub blocky, carbonaceous in part, silty in part. SANDSTONE (10-50%): clear – translucent to off white, fine to medium, rare coarse to very coarse grains, dominantly loose to occasionally soft aggregates, sub angular to rounded, moderately sorted, aggregates have up to 20% argillaceous matrix, trace pyrite cement, good inferred porosity |
| 1780-1830 ROP: 12.2 – 89.7 m/hr Av: 51.0 m/hr | Massive Claystone interbedded with Silty Claystone and minor Sandstone SILTY CLAYSTONE (10-80%): light grey to dark medium grey, rare moderate yellowish brown, soft, amorphous to sub blocky, occasionally very arenaceous with disseminated fine sand, minor carbonaceous specks, non calcareous. CLAYSTONE (15-88%): dark grey, occasional light grey, moderately hard, blocky, massive, carbonaceous specks, non calcareous. SANDSTONE (Trace-10%): light grey to white, translucent, soft aggregates to loose, very fine to fine grading to arenaceous SILTSTONE in parts, occasionally medium, sub rounded, moderately sorted, trace light grey argillaceous matrix, weak siliceous cement, poor visual porosity, no show. |
| 1830-1895 ROP: 21.5 – 89.1 m/hr Av: 41.3 m/hr | Admiral Formation (1830.0 mMDRT 1788.2 mTVDRT 1766.7 mSS) Sandstone interbedded with Siltstone SANDSTONE (15-55%): translucent, light yellowish grey to white, dominantly soft aggregates to occasionally loose, fine to medium, sub rounded - sub angular, moderately well sorted, 50% light grey argillaceous matrix supported, weak siliceous cement, poor visual porosity in aggregates, fair to good inferred porosity in loose fraction. Gas shows 4.3% see table below. SILTSTONE (45-85%): light grey to dark medium grey, soft to firm, sub blocky to occasionally sub fissile, trace disseminated fine sand, minor carbonaceous specks and laminae, non calcareous. |
| 1895 - 1930 ROP: 46.2 – 117.2 m/hr Av: 52.2 m/hr | Massive Claystone interbedded with minor Silty Claystone CLAYSTONE (60-95%): dark brownish grey, brownish black, soft to firm, sub blocky, occasionally splintery, very rare carbonaceous specks, uniform. SILTSTONE (5-40%): dark brownish grey, brownish grey, soft, sub blocky to blocky, trace carbonaceous specks, occasional carbonaceous laminae, massive, uniform, gradational to SILTY CLAYSTONE. |
| 1930 - 2040 ROP: 13– 101 m/hr Av: 53.0 m/hr | 500 Sand (1930.0 mMDRT 1877.2 m TVDRT 1855.7 mSS) Sandstone interbedded with SILTSTONE minor Claystone, trace Coal. SANDSTONE (10-50%): yellowish brown, off white, dominantly soft aggregates, very fine to fine, sub rounded, well sorted, 20% argillaceous matrix, gradational in part to silt, trace carbonaceous specks. Occasionally loose, clear to translucent, white to light grey, fine to rare coarse, dominantly medium, moderately well sorted, sub angular to dominantly sub rounded, trace glauconite, fair to good inferred porosity, Gas shows 36% see table below. SILTSTONE (50-80%): medium dark grey to brownish grey, soft to firm, sub blocky to sub fissile, common disseminated fine sand grading to very fine Sandstone, minor carbonaceous specks and laminae, non calcareous. CLAYSTONE (Nil-25%): dark brownish grey, brownish black, brownish grey, soft to firm, sub blocky, very rare carbonaceous specks, uniform. COAL (Nil-2%): brownish black to black, sub vitreous to dull, brittle, hackly fracture, silty and argillaceous in part with quartz inclusions. |
| 2040 – 2098 ROP: 21 – 96 m/hr Av 50 m/hr | Massive Siltstone grading to Claystone with depth trace Sandstone SILTSTONE: (70-100%) brownish grey, dark brownish grey, very soft – rare firm, sub blocky, argillaceous to occasionally arenaceous, carbonaceous specks, occasional very fine sand. CLAYSTONE: (0-30%) medium grey, very soft – soft, occasionally firm, sub blocky, uniform and massive, none calcareous, rarely silty. SANDSTONE: (0-5%) light brownish grey, soft aggregate, very fine grained, sub rounded to rounded, well sorted, abundant argillaceous matrix to 60%, silty in part, carbonaceous grains, poor visible porosity, no shows. |

HYDROCARBON FLUORESCENCE:

| INTERVAL (mMDRT) | FLUORESCENCE |
| --- | --- |
|  | No fluorescence observed |

GAS SUMMARY:

| INTERVAL (mMDKB) | Total GAS (%) | C1 (ppm) | C2 (ppm) | C3 (ppm) | IC4 (ppm) | NC4 (ppm) | IC5 (ppm) | NC5 (ppm) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Trip Gas at 1727m | 1.1 | 9146 | 217 | 38 | 8 | 8 | 15 | 2 |
| 1727 - 1780 | 0.50 | 4561 | 60 | 9 | 5 | 2 | 13 | 0 |
| 1771 peak sandstone | 1.46 | 12152 | 180 | 16 | 5 | 2 | 15 | 0 |
| 1780 - 1830 | 0.70 | 6230 | 98 | 11 | 6 | 2 | 12 | 1 |
| 1829 peak sandstone | 4.32 | 32941 | 565 | 39 | 7 | 1 | 9 | 1 |
| 1830 -1895 | 1.60 | 12844 | 202 | 17 | 7 | 3 | 11 | 0 |
| 1831 peak sandstone | 4.26 | 32903 | 548 | 39 | 7 | 3 | 9 | 1 |
| 1895 -1930 | 1.80 | 14518 | 292 | 30 | 7 | 3 | 9 | 0 |
| 1924 peak sandstone | 3.87 | 29183 | 652 | 111 | 16 | 15 | 10 | 1 |
| 1930 -2040 | 4.5 | 33705 | 750 | 176 | 26 | 21 | 10 | 2 |
| 1953 peak sandstone | 32.8 | 163738 | 3777 | 695 | 80 | 76 | 13 | 5 |
| 1967.5 peak sandstone | 36 | 189389 | 4454 | 817 | 93 | 93 | 14 | 6 |
| 2040 - 2098 | 2 | 15015 | 442 | 108 | 20 | 17 | 9 | 1 |
| 2088 peak | 6.4 | 46867 | 1050 | 222 | 30 | 26 | 10 | 4 |

SURVEYS

Tie in point to Longtom -3 ST1 is 1005.00m

| MD | ANGLE | Azi | TVD | MD | ANGLE | Azi | TVD |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 1703.59 | 29.2 | 185.09 | 1676.2 | 2048.00 | 40.87 | 188.24 | 1973.8 |
| 1733.25 | 29.06 | 183.62 | 1702.1 | 2076.57 | 43.25 | 188.28 | 1995.0 |
| 1761.83 | 27.21 | 181.89 | 1727.3 | 2105.26 | 45.26 | 188.86 | 2015.6 |
| 1790.12 | 26.78 | 181.20 | 1752.5 |  |  |  |  |
| 1818.86 | 26.52 | 181.62 | 1778.2 |  |  |  |  |
| 1847.19 | 27.12 | 182.86 | 1803.5 |  |  |  |  |
| 1875.62 | 26.65 | 186.04 | 1828.9 |  |  |  |  |
| 1904.30 | 26.86 | 187.48 | 1854.5 |  |  |  |  |
| 1932.56 | 29.13 | 187.47 | 1879.4 |  |  |  |  |
| 1962.25 | 32.15 | 187.62 | 1905.0 |  |  |  |  |
| 1990.65 | 34.98 | 188.01 | 1928.6 |  |  |  |  |
| 2019.25 | 37.97 | 187.90 | 1951.6 |  |  |  |  |

FORMATION TOPS

| WD = 56.7 m RTE = 21.5 m |
| --- |
| FORMATION | PROGNOSED DEPTHS (m) | ACTUAL DEPTHS (m) |
|  | MDKB | TVDSS | THICK | MDKB | TVDSS | HI/LO | THICK | DIFF |
| Sea Floor/ Gippsland Limestone | 77.5 | 56 | 1096 | 77.5 | 56 |  | 1104 | +8 |
| Lakes Entrance | 1172.0 | 1150.0 | 64 | 1182 | 1160.0 | 10.0 LO | 33.5 | -30.5 |
| Latrobe | 1236 | 1214.0 | 234 | 1216 | 1193.5 | 20.5 HI | 261.8 | +27.8 |
| K/T Boundary | 1476 | 1448 | 37 | 1484 | 1455.3 | 7.3 LO | 61.3 | +24.3 |
| Un-named Volcanics | 1515 | 1485 | 37 | 1546 | 1513.8 | 28.8 LO | 15.0 | n/a |
| Kipper Shale | 1555 | 1522 | 201 | 1603 | 1565.9 | 43.9 LO | 200.8 | -0.2 |
| Admiral Formation (Nexus) | 1777 | 1723 | 163 | 1830.0 | 1766.7 | 43.7 LO | 89.0 | -74.0 |
| Admiral Formation (SRD) | 1963 | 1889 | N/A | 1930.0 | 1855.7 | 33.3 HI |  |  |
| 500 sand | 1963 | 1889 | 154 | 1930.0 | 1855.7 | 33.3 HI |  |  |
| 400 sand | 2166 | 2043 | 117 |  |  |  |  |  |
| 300 sand | 2366 | 2160 | 77 |  |  |  |  |  |
| 200 sand | 2502 | 2237 | 47 |  |  |  |  |  |
| 100 sand | 2584 | 2284 | 44 |  |  |  |  |  |
| Emperor Volcanics | 2661 | 2328 | N/A |  |  |  |  |  |
| TD | 2733 | 2370 |  |  |  |  |  |  |

COMMENTS:

Gas peaks in the 500 sand (36%) circulated out prior to drilling ahead.

Anadrill Schlumberger LWD sensor to bit distances: Resistivity: 11.87m Gamma 11.92m, Ultrasonic Caliper 26.6m, Density: 26.99, Neutron Porosity 28.04m.

WELLSITE GEOLOGISTS:

| Mike Woodmansee | Trevor Lobo |
| --- | --- |