DRILLING / WELLWORK REPORT 24HRS TO 0500 HRS December 15, 2006

| RIG 453 | 210 | 363 |
| --- | --- | --- |
| CAMERON | 1679 | 1679 |
| HALLIBURTON | 3466 | 3466 |
| SCHLUMBERGER | 2408 | 2408 |
| ISDL | 210 | 647 |
| ISS | 198 | 2357 |

Well: HLA_A23

Rig/Contractor: 	Rig 453	Report Date: December 15, 2006

Supervisor:	Bennett, James M

Steel, George A

| AFE Number: AFE Number: | L0501G205 | Ave Angle: |  |
| --- | --- | --- | --- |
| Days to Complete: | 2.0 | AFE Cost/Days: | $1,500,000 |
| Daily Cost: | $188,247 |  |  |
| Total Cost: | $353,702 | Planned MD/TVD: |  |
| Casing Size: |  | Actual MD/TVD: |  |
| Mud Weight: |  | Tubing Size: |  |

| Objective: | HLA_A23 |
| --- | --- |
| Management Summary: | PTSM's. RIH w/ 16" casing from 80m to 178.5m. RIH w/ cement stinger and spaceout to 171m. P/up baker cement assy. RIH and sting into float @ 179m. Commence 16" cement job. Pump 80 bbl 15.9 ppg slurry. Bump plug with 900 psi. 0 bbl of flow back volume. WOC. Circulate hole clean. Cut casing above cellar deck. Lay out cut casing. Conduct rig service. |
| Current: | Lay out cement head. Prepare to skid. |
| Planned: | Dress casing. Move to slot 24. |