DRILLING / WELLWORK REPORT 24HRS TO 0500 HRS August 16, 2006

SAFETY

DAYS SINCE LAST TRI:	PREVIOUS BEST TRI PERIOD

| RIG 453 | 290 | 363 |
| --- | --- | --- |
| CAMERON | 5543 | 5542 |
| HALLIBURTON | 3365 | 3364 |
| SCHLUMBERGER | 2145 | 22 |
| ISDL | 290 | 647 |
| ISS | 78 | 2365 |

Well: WKF_W21A

Rig/Contractor: 	Rig 453	Report Date: August 16, 2006

Supervisor:	Campbell, Glen R

Davis, Brian

| AFE Number: | L0501G658 | Ave Angle: |  |
| --- | --- | --- | --- |
| Days to Complete: | 1.0 | AFE Cost/Days: | $5,120,000 |
| Daily Cost: | $207,291 |  |  |
| Total Cost: | $207,291 | Planned MD/TVD: |  |
| Casing Size: |  | Actual MD/TVD: | 684.00/622.38 |
| Mud Weight: |  | Tubing Size: |  |

| Objective: | WKF_W21A |
| --- | --- |
| Management Summary: | Change & P/tst rams. Run W/bushing. C/out Anadrill standpipe sensor. Orient BHA, set bend to 1.5° & shallow test. RIH t/ 497m. R/serv. Power Choke & Trip Drills. TIH & tag cmt @ 625m. Drill cement. Kickoff cement plug. POH. |
| Current: | Circulating Hole Clean Prior to PIT. Service Boat. |
| Planned: | Circ Hole Clean, PIT. Drill & Survey 8½" Production Hole. |