DRILLING / WELLWORK REPORT 24HRS TO 0500 HRS FEBRUARY 27, 2007

SAFETY:

DAYS SINCE LAST TRI:	PREVIOUS BEST TRI PERIOD

| ISDL RIG 453 | 284 | 363 |
| --- | --- | --- |
| ISDL RIG 175 | 206 | 206 |
| CAMERON | 1759 | 1759 |
| HALLIBURTON | 3563 | 3563 |
| SCHLUMBERGER | 2468 | 2468 |
| ISS | 276 | 2357 |

Well: FTA _A12a

Rig/Contractor: 	Rig 175	Report Date: February 27, 2007

Supervisor:	Davis, Brian

Stead, Cory

| AFE Number: AFE Number: | L0501H000 | Ave Angle: |  |
| --- | --- | --- | --- |
| Days on AFE | 46.71 | AFE Cost/Days: | $10,210,000 |
| Daily Cost: | $181,983 |  |  |
| Total Cost: | $8,019,711 | Planned MD/TVD: |  |
| Casing Size: |  | Actual MD/TVD: |  |
| Mud Weight: |  | Tubing Size: |  |

| Objective: | FTA_A12a |
| --- | --- |
| Management Summary: | Prepare to skid rig. Skid rig over A12 well bay. Secure rig & re-connect services. Service MV Far Scandia. Offload V-door, catwalk, bit store & Cameron equipment. Install V-door & catwalk. Continue w/ rig up operations. DNV checks ongoing. Rig up 86% complete. |
| Current: | General rig up operations. |
| Planned: | Continue w/ rig up operations. |

DRILLING / WELLWORK REPORT 24HRS TO 0500 HRS FEBRUARY 27, 2007

SAFETY:

DAYS SINCE LAST TRI:	PREVIOUS BEST TRI PERIOD

| ISDL RIG 453 | 284 | 363 |
| --- | --- | --- |
| ISDL RIG 175 | 206 | 206 |
| CAMERON | 1759 | 1759 |
| HALLIBURTON | 3563 | 3563 |
| SCHLUMBERGER | 2468 | 2468 |
| ISS | 276 | 2357 |

Well: HLA_A16

Rig/Contractor: 	Rig 453	Report Date: February 27, 2007

Supervisor:	Bareswill, J R (Dicky)

Smith, Gary G

| AFE Number: AFE Number: | 40000448 | Ave Angle: |  |
| --- | --- | --- | --- |
| Days on AFE | 4.65 | AFE Cost/Days: | $2,177,350 |
| Daily Cost: | $202,981 |  |  |
| Total Cost: | $2,036,514 | Planned MD/TVD: | 2,581.00 / |
| Casing Size: |  | Actual MD/TVD: |  |
| Mud Weight: |  | Tubing Size: |  |

| Objective: | HLA_A16 |
| --- | --- |
| Management Summary: | Finish N/u Bops. Failed to achieve pressure test between Bop Riser/DSA and wellhead due to casing slips not sealing. Received MOC: Bops were tested to 3000 psi 17 Feb., casing test was previously conducted. M/U Baker csg cutting tools, Cut 7 5/8" casing at 625m, CBU, Pooh, L/D Baker BHA, M/u Casing Spear, pulled and retrieve casing to rotary, removed casing slips, L/d Baker spear. CBU 3 times, Pooh L/D 7 5/8" csg. |
| Current: | Pooh L/D 7 5/8" csg. |
| Planned: | Set P&A Plug |