DRILLING / WELLWORK REPORT 24HRS TO 0500 HRS FEBRUARY 7, 2007

SAFETY:

DAYS SINCE LAST TRI:	PREVIOUS BEST TRI PERIOD

| ISDL RIG 453 | 264 | 363 |
| --- | --- | --- |
| ISDL RIG 175 | 186 | 186 |
| CAMERON | 1739 | 1739 |
| HALLIBURTON | 3543 | 3543 |
| SCHLUMBERGER | 2448 | 2448 |
| ISS | 256 | 2357 |

Well: HLA_A24

Rig/Contractor: 	Rig 453	Report Date: February 7, 2007

Supervisor:	Bareswill, JR (Dicky)

Campbell, Glenn R

| AFE Number: AFE Number: | L0501G208 | Ave Angle: |  |
| --- | --- | --- | --- |
| Days on AFE | 14.5 | AFE Cost/Days: | $6,507,763 |
| Daily Cost: | $243,939 |  |  |
| Total Cost: | $3,164,984 | Planned MD/TVD: | 2,984.99/2,616.57 |
| Casing Size: |  | Actual MD/TVD: | 1,875.00/ |
| Mud Weight: |  | Tubing Size: |  |

| Objective: | HLA_A24 |
| --- | --- |
| Management Summary: | PTSM's. Held pit drills. Drill, steer & survey 8-1/2" production hole from 1528m to 1875m. Rig service. |
| Current: | Rig service. |
| Planned: | Continue to drill, steer & survey 8-1/2" production hole. |

DRILLING / WELLWORK REPORT 24HRS TO 0500 HRS FEBRUARY 7, 2007

SAFETY:

DAYS SINCE LAST TRI:	PREVIOUS BEST TRI PERIOD

| ISDL RIG 453 | 264 | 363 |
| --- | --- | --- |
| ISDL RIG 175 | 186 | 186 |
| CAMERON | 1739 | 1739 |
| HALLIBURTON | 3543 | 3543 |
| SCHLUMBERGER | 2448 | 2448 |
| ISS | 256 | 2357 |

Well: FTA _A12a

Rig/Contractor: 	Rig 175	Report Date: February 7, 2007

Supervisor:	Davis, Brian

Bennett, James

| AFE Number: AFE Number: | L0501H000 | Ave Angle: |  |
| --- | --- | --- | --- |
| Days on AFE | 26.71 | AFE Cost/Days: | $10,210,000 |
| Daily Cost: | $179,958 |  |  |
| Total Cost: | $4,435,716 | Planned MD/TVD: |  |
| Casing Size: |  | Actual MD/TVD: |  |
| Mud Weight: |  | Tubing Size: |  |

| Objective: | FTA_A12a |
| --- | --- |
| Management Summary: | PTMS's. Continue rig up operations. Install BOP stump and lower rams in sub base. Service boat: unload remaining baskets/containers. Back load as needed. Complete installation of exhaust lagging. Set up engine shut down. Stand BOP's in transport frame. Continue with electric cables for lower part of drilling module. Install lifting eyes on BOP stack. Bolt on annular lift frame, position and remove lift frame, bolt up to BOP ram / test stump. Continue with tank spooling. Position lift and roll jacks in sub base. Complete mud pump suction spooling. Empty containers and baskets. 43% rig up completed. Held weekly safety meeting with day crew @ 18:30-20:00 hrs. |
| Current: | General rig up operations. Spooling. Empty baskets |
| Planned: | Continue rig up operations. |