| WELL | WKF-W6A |
| --- | --- |
| DATE | 17-09-2006 |
| DAY # | 12 |
| MIDNIGHT ACTIVITY | Pulling out of the hole at 2282.0 mMDRT. |  | ROP DATA (LAST 24 hours) | M/hr | DEPTH (m) |
| MIDNIGHT DEPTH | 3477.0 m |  | MINIMUM | 4.7 | 3475.0 |
| TVDRT | 2271.1 m |  | MAXIMUM | 85.5 | 3290.0 |
| PROGRESS LAST 24 hrs | 189.0 m |  | AVERAGE | 27.4 | 3288.0-3477.0 |

PRELIMINARY FIELD PICKS ONLY. SUBJECT TO CHANGE.

|  | TOP (mMDRT) | TOP (mTVDRT) | TOP (mTVDSS) RTtoMSL (33.4m) | HIGH/ LOW (mTVD) | PROGNOSED TOP (mMDRT) | PROGNOSED TOP (mTVDRT) |
| --- | --- | --- | --- | --- | --- | --- |
| Base of High Velocity Channel | 1845.0 | 1392.9 | -1359.5 | 0.5 HIGH | 1844.6 | 1393.4 |
| Top of Lakes Entrance | 2952.0 | 2052.1 | -2018.7 | 1.3 HIGH | 2949.7 | 2053.4 |
| Top of Latrobe | 3279.0 | 2248.9 | -2215.5 | 5.5 LOW | 3267.8 | 2243.4 |
| Top of P1.1 (FSP1) | 3323.5 | 2276.9 | -2243.5 | 8.5 LOW | 3309.6 | 2268.4 |
| Base of P1.1 (SBP1) | 3338.5 | 2286.3 | -2252.9 | 9.9 LOW | 3339.7 | 2276.4 |
| Top of P1.2 | 3345.0 | 2290.4 | -2257.0 | 4.0 LOW | 3341.6 | 2286.4 |
| Top of M1.2L | 3352.0 | 2294.8 | -2261.4 | 6.4 LOW | 3354.2 | 2288.4 |
| Base of M1.2 | 3358.0 | 2298.5 | -2265.1 | 1.1 LOW | 3358.2 | 2297.4 |
| Top of M1.3U (PS6 ) | 3368.0 | 2304.8 | -2271.4 | 2.6 HIGH | 3374.8 | 2307.4 |
| Top of M1.3U (PS5) | 3374.5 | 2308.8 | -2275.4 | 2.6 HIGH | 3378.5 | 2311.4 |
| Top of M1.3U (PS4) | 3377.0 | 2310.4 | -2277.0 | 3.0 HIGH | 3381.6 | 2313.4 |
| Top of M1.3L (PS3) | 3398.0 | 2323.3 | -2289.9 | 4.1 HIGH | 3406.5 | 2327.4 |
| Top of M1.3L (PS2) | 3408.0 | 2329.5 | -2296.1 | 5.9 HIGH | 3407.2 | 2335.4 |
| Base M1.3L/Top M1.4 | 3441.5 | 2349.8 | -2316.4 | 6.4 LOW | 3435.2 | 2343.4 |
| Top of M1.5 |  |  |  |  | 3477.0 | 2368.4 |
| Total Depth | 3477.0 | 2371.1 | -2337.7 | 2.7 LOW | 3477.0 | 2368.4 |

| Current Formation | Latrobe: Sandstone / Siltstone / Claystone. |
| --- | --- |

| GAS DATA | DEPTH (m) | TOTAL GAS (U) | C1 % | C2 % | C3 % | iC4 % | nC4 % | C5 % |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| MAX (FCP/FGP) | 3374.0 | 93.0 | 0.341 | 0.105 | 0.116 | 0.048 | 0.90 | 0.073 |
| MAX (Reserval) | 3330.0 | 823.0 | 2.351 | 0.825 | 1.338 | 0.493 | 0.781 | 0.665 |
| BG (FCP/FGP) | 3288.0-3477.0 | 45.0 | 0.165 | 0.045 | 0.059 | 0.022 | 0.045 | 0.040 |
| BG (Reserval) | 3288.0-3477.0 | 350.0 | 0.756 | 0.324 | 0.573 | 0.229 | 0.358 | 0303 |
| TRIP GAS (FCP) | 3477.0 | 19.0 | 0.126 | 0.007 | 0.014 | 0.008 | 0.016 | 0.019 |
| TRIP GAS Reserval) | 3477.0 | 115.0 | 0.444 | 0.032 | 0.106 | 0.070 | 0.119 | 0.141 |

| BIT DATA | PRESENT BIT | LAST BIT |
| --- | --- | --- |
| BIT No. | 1RR | 1 |
| SIZE (in) | 8½ | 8½ |
| MANUFACTURER/TYPE | Smith S73PX | Smith S73PX |
| JETS (/32 inch) | 6 x 20 | 6 x 20 |
| DEPTH IN (m) | 2768.0 | 695.0 |
| DEPTH OUT (m) |  | 2768.0 |
| METRES ON RUN (m) | 709.0 | 2073.0 |
| HRS ON BTM 24hrs/total | 6.9 / 29.8 | 70.7 |
| BIT CONDITION |  | 1-1-NO-A-X-IN-NO-PP |
| RPM RANGE LAST 24 hrs | Mud Motor: 169-175 Top Drive: 100-115 |  |
| Pump Hrs 24 hrs / total | 17.5 / 78.3 | 119.8 |
| Krevs 24 hrs / total | 121 / 485 | 1068 |
| 24 HOUR SUMMARY | Rotary drill and survey 8½" hole from 3288.0 mMDRT to 3431.0 mMDRT. Rotate, work string and circulate at reduced pump rate while replacing swab on mud pump #1. Rotary drill and survey 8½" hole from 3431.0 mMDRT to 3477.0 mMDRT. Rotate, work string, pump 30 bbl sweep and circulate hole clean while racking back 1 stand per ½ hour to 3431.0 mMDRT. Flow check and pull from 3431.0 mMDRT to 3000.0 mMDRT. Rotate, work string, pump 30 bbl sweep and circulate hole clean. Run in hole from 3000.0 mMDRT to 3477.0 mMDRT, precautionary wash and ream last stand. Rotate, work string, pump 30 bbl sweep and circulate hole clean while racking back 1 stand per ½ hour to 3373.0 mMDRT. Flow check, slug pipe and pull out of hole to 2282.0 mMDRT. |
| 05:00 AM UPDATE 18-09-2006. DEPTH AT 05:00 hours | Pull out of hole from 2282.0 mMDRT to 1302.0 mMDRT. Rotate, work string, pump 30 bbl sweep and circulate hole clean. Pull out of hole from 1302.0 mMDRT to tight hole at 835.0 mMDRT. Run in 2 stands and make up TDS. Rotate, work string and circulate hole clean at 902.0 mMDRT. 3477.0 mMDRT (2371.1 mTVDRT) |