Report for : Dan Daniels / Mark Calicutt / Sam Falkner

Compiled by  : Mark Smith

| WELL | CBA A14B |
| --- | --- |
| DATE | 08-04-2009 |
| REPORT # | 8 |
| MIDNIGHT ACTIVITY | Drilling 97/8" hole. |  | ROP DATA (LAST 24 hours) | m/hr | DEPTH (m) |
| MIDNIGHT DEPTH | 2971.0 mMDRT |  | MINIMUM | 9.8 | 2900.0 |
| TVD | 2436.0 mTVDRT |  | MAXIMUM | 131.1 | 2155.0 |
| PROGRESS LAST 24 hrs | 875.0 m |  | AVERAGE | 67.3 | 2096.0-2971.0 |

| PRELIMINARY FIELD PICKS | ACTUAL TOP (mMDRT) | ACTUAL TOP (mTVDRT) | ACTUAL TOP (mTVDSS) RT to MSL (41.0m) | HIGH/ LOW (mTVD) | PROGNOSED TOP (mMDRT) | PROGNOSED TOP (mTVDRT) |
| --- | --- | --- | --- | --- | --- | --- |
| Lakes Entrance Fm. | 2660.0 | 2195.5 | -2154.5 | 10.5m H | 2674.3 | 2206.0 |
| Top of Latrobe Grp | 2928.0 | 2403.1 | -2362.1 | 0.1m L | 2928.2 | 2403.0 |
| Top Coarse Clastics | 2929.5 | 2404.3 | -2363.3 | 0.3m L | 2929.5 | 2404.0 |
| 4 FS / M141 | 2939.0 | 2411.6 | -2370.6 | 2.6m L | 2936.0 | 2409.0 |
| 4.5 FS / M145 | 2969.0 | 2434.8 | -2393.8 | 1.2m H | 2970.8 | 2436.0 |
| OOWC | 2973.2 | 2438.0 | -2397.0 | 0.0m | 2973.3 | 2438.0 |
| Total Depth |  |  |  |  | 3013.3 | 2469.0 |

| Current Formation | Latrobe Group |
| --- | --- |

| GAS DATA | DEPTH (m) | TOTAL GAS (U) | C1 % | C2 % | C3 % | C4 % | C5 % | H2S ppm |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| MAX (Reserval) | 2155.0 2949.0 2968.0 | 48.1 46.1 48.3 | 0.919 0.361 0.338 | 0.006 0.093 0.084 | 0.002 0.066 0.074 | - 0.052 0.062 | - 0.019 0.023 | - - - |
| MAX (GFF) | 2968.0 | 24 | 0.219 | 0.061 | 0.062 | 0.063 | 0.031 | - |
| BG (Reserval) | 2096.0-2971.0 | 25 | 0.428 | 0.009 | 0.006 | - | - | - |
| BG (GFF) | 2096.0-2971.0 | 11 | 0.201 | 0.005 | 0.002 | - | - | - |
| TRIP GAS (Reserval) | - | - | - | - | - | - | - | - |
| TRIP GAS (GFF) | - | - | - | - | - | - | - | - |
| CONNECTION GAS | - | - | - | - | - | - | - | - |

| BIT DATA | PRESENT BIT | PREVIOUS BIT |
| --- | --- | --- |
| BIT No. | 3 | 2 |
| SIZE (in) | 9⅞" | 9.894" |
| MANUFACTURER/TYPE | Reed Hycalog RSX616M-A12 | Water Melon Mill |
| JETS (/32 inch) | 6 x 18 | 9 x 10 mm |
| DEPTH IN (m) | 565.0 | 543.5 |
| DEPTH OUT (m) |  | 565.0 |
| METRES ON RUN (m) | 2406.0 | 21.5 |
| HRS ON BTM 24hrs/total | 13.0 / 50.3 | 11.4 |
| BIT CONDITION |  |  |
| RPM RANGE 24hrs | 100-180 |  |
| Pump Hrs 24 hrs / total | 21.4 / 75.3 | 25.4 |
| Krevs 24 hrs / total | 111 / 434 | 57.7 |

| 24 HOUR SUMMARY | Drill and steer 9⅞" hole from 2096.0 mMDRT to 2575.0 mMDRT. Circulate and rotate pipe at 2575.0 mMDRT until shakers clean. Drill and steer 9⅞" hole from 2575.0 mMDRT to 2897.0 mMDRT, commence control drilling at 50 m/hr from 2826.0 mMDRT. Circulate and rotate pipe at 2897.0 mMDRT until shakers clean. Drill and steer 9⅞" hole at controlled rate from 2897.0 mMDRT to 2971.0 mMDRT. |
| --- | --- |
| 09-04-2009 5AM UPDATE | Drill and steer 9⅞" hole at controlled rate from 2971.0 mMDRT to 3043.0 mMDRT. Anadrill downlink to tools to set RSS to zero degrees and take survey. Circulate and rotate pipe until hole clean, racking back 1 stand every bottoms up, from 3043.0 mMDRT to 2975.0 mMDRT. 3043.0 mMDRT (2491.8 mTVDRT) |