Report for : Dan Daniels / Mark Calicutt / Andy Choy

Compiled by  : Mark Smith

| WELL | CBA A14B |
| --- | --- |
| DATE | 09-04-2009 |
| REPORT # | 9 |
| MIDNIGHT ACTIVITY | Back reaming out of hole at 794.0 mMDRT. |  | ROP DATA (LAST 24 hours) | m/hr | DEPTH (m) |
| MIDNIGHT DEPTH | 3043.0 mMDRT |  | MINIMUM | 21.3 | 2974.0 |
| TVD | 2491.7 mTVDRT |  | MAXIMUM | 57.3 | 3038.0 |
| PROGRESS LAST 24 hrs | 72.0 |  | AVERAGE | 37.9 | 2971.0-3043.0 |

| PRELIMINARY FIELD PICKS | ACTUAL TOP (mMDRT) | ACTUAL TOP (mTVDRT) | ACTUAL TOP (mTVDSS) RT to MSL (41.0m) | HIGH/ LOW (mTVD) | PROGNOSED TOP (mMDRT) | PROGNOSED TOP (mTVDRT) |
| --- | --- | --- | --- | --- | --- | --- |
| Lakes Entrance Fm. | 2660.0 | 2195.5 | -2154.5 | 10.5m H | 2674.3 | 2206.0 |
| Top of Latrobe Grp | 2928.0 | 2403.1 | -2362.1 | 0.1m L | 2928.2 | 2403.0 |
| Top Coarse Clastics | 2929.5 | 2404.3 | -2363.3 | 0.3m L | 2929.5 | 2404.0 |
| 4 FS / M141 | 2939.0 | 2411.6 | -2370.6 | 2.6m L | 2936.0 | 2409.0 |
| 4.5 FS / M145 | 2969.0 | 2434.8 | -2393.8 | 1.2m H | 2970.8 | 2436.0 |
| OOWC | 2973.2 | 2438.0 | -2397.0 | 0.0m | 2973.3 | 2438.0 |
| Total Depth | 3043.00 | 2491.76 | -2450.76 | 22.76 L | 3013.3 | 2469.0 |

| Current Formation | Latrobe Group |
| --- | --- |

| GAS DATA | DEPTH (m) | TOTAL GAS (U) | C1 % | C2 % | C3 % | C4 % | C5 % | H2S ppm |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| MAX (Reserval) | 2979.0 3004.0 3022.0 3040.0 | 54.2 44.8 39.6 41.4 | 0.363 0.335 0.328 0.326 | 0.093 0.105 0.100 0.103 | 0.077 0.054 0.039 0.043 | 0.069 0.045 0.034 0.037 | 0.029 0.016 0.011 0.014 | - - - - |
| MAX (GFF) | 2979.0 | 21.0 | 0.217 | 0.073 | 0.043 | 0.042 | 0.021 | - |
| BG (Reserval) | 2971.0-3043.0 | 38 | 0.277 | 0.079 | 0.045 | 0.041 | 0.015 | - |
| BG (GFF) | 2971.0-3043.0 | 17 | 0.146 | 0.046 | 0.034 | 0.036 | 0.011 | - |
| TRIP GAS (Reserval) | - | - | - | - | - | - | - | - |
| TRIP GAS (GFF) | - | - | - | - | - | - | - | - |
| CONNECTION GAS | - | - | - | - | - | - | - | - |

| BIT DATA | PRESENT BIT | PREVIOUS BIT |
| --- | --- | --- |
| BIT No. | 3 | 2 |
| SIZE (in) | 9⅞" | 9.894" |
| MANUFACTURER/TYPE | Reed Hycalog RSX616M-A12 | Water Melon Mill |
| JETS (/32 inch) | 6 x 18 | 9 x 10 mm |
| DEPTH IN (m) | 565.0 | 543.5 |
| DEPTH OUT (m) |  | 565.0 |
| METRES ON RUN (m) | 2478.0 | 21.5 |
| HRS ON BTM 24hrs/total | 1.9 / 52.2 | 11.4 |
| BIT CONDITION |  |  |
| RPM RANGE 24hrs | 100 |  |
| Pump Hrs 24 hrs / total | 15.9 / 91.2 | 25.4 |
| Krevs 24 hrs / total | 11 / 445 | 57.7 |

| 24 HOUR SUMMARY | Drill and steer 9⅞" hole at controlled rate from 2971.0 mMDRT to 3043.0 mMDRT. Anadrill downlink to tools to set RSS to zero degrees and take survey. Circulate and rotate pipe until hole clean, racking back 1 stand every bottoms up, from 3043.0 mMDRT to 2956.0 mMDRT. Back ream out of hole from 2956.0 mMDRT to 915.0 mMDRT, at 5 minutes a stand while logging. Whilst back reaming experience 10 to 20 klbs overpull at 915 mMDRT. Worked string, circulated bottoms up and pulled through tight spot. Back ream out of hole from 954.0 mMDRT to 794.0 mMDRT, at 5 minutes a stand while logging. |
| --- | --- |
| 10-04-2009 5AM UPDATE | Whilst back reaming experience 10 to 20 klbs overpull at 794 mMDRT. Worked string and pulled through tight spot. Back ream out of hole from 794.0 mMDRT to 766.0 mMDRT, at 5 minutes a stand while logging. Circulate and work string due to auger shut down. Divert cuttings over board due auger motor failure. Back ream out of hole from 766.0 mMDRT to 545.0 mMDRT, at 5 minutes a stand while logging. 3043.0 mMDRT (2491.81 mTVDRT) |