Report for : Greg Doty / Richard Moore

Compiled by : Mark Smith

| WELL | CBA A15B |
| --- | --- |
| DATE | 21-08-2009 |
| REPORT # | 8 |
| MIDNIGHT ACTIVITY | Drill ahead 9-7/8” production hole. |  | ROP DATA (LAST 24 hours) | m/hr | DEPTH (m) |
| MIDNIGHT DEPTH | 2980.0 mMDRT |  | MINIMUM | 17.7 | 2642.0 |
| TVD | 2381.0 mTVDRT |  | MAXIMUM | 112.2 | 2258.0 |
| PROGRESS LAST 24 hrs | 817.0 m |  | AVERAGE | 71.7 | 2163.0 – 2980.0 |

| PRELIMINARY FIELD PICKS | ACTUAL TOP (mMDRT) | ACTUAL TOP (mTVDRT) | ACTUAL TOP (mTVDSS) RT to MSL (41.0m) | HIGH/ LOW (mTVD) | PROGNOSED TOP (mMDRT) | PROGNOSED TOP (mTVDRT) |
| --- | --- | --- | --- | --- | --- | --- |
| Top of Lakes Entrance Formation | 2715.0 | 2174.6 | -2133.6 | 3.6m L | 2712.0 | 2171.0 |
| Top of Latrobe Group | 3022.5 | 2411.9 | -2370.9 | 3.9m L | 3018.0 | 2408.0 |
| TCC / M112 | 3024.0 | 2413.0 | -2372.0 | 3.0m L | 3020.0 | 2410.0 |
| M131A | 3028.0 | 2416.1 | -2375.1 | 4.1m L | 3023.0 | 2412.0 |
| M131B | 3031.0 | 2418.4 | -2377.4 | 3.4m L | 3027.0 | 2415.0 |
| M132 Upper | 3034.0 | 2420.8 | -2379.8 | 0.8m L | 3033.0 | 2420.0 |
| M132 Lower | 3038.0 | 2423.8 | -2382.8 | 0.2m H | 3038.0 | 2424.0 |
| M141 | 3048.0 | 2431.6 | -2390.6 | 2.6m L | 3044.0 | 2429.0 |
| OOWC | 3056.4 | 2438.0 | -2397.0 | 0.4m L | 3056.0 | 2438.0 |
| Total Depth |  |  |  |  | 3116.0 | 2484.0 |

| Current Formation | Lakes Entrance |
| --- | --- |

| GAS DATA | DEPTH (m) | TOTAL GAS (U) | C1 % | C2 % | C3 % | C4 % | C5 % | H2S ppm |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| MAX (Reserval) | 2488.0 | 24.8 | 0.398 | 0.003 | 0.001 | 0.001 | - | - |
| MAX (GFF) | 2326.0 | 15.3 | 0.331 | 0.001 | - | - | - | - |
| BG (Reserval) | 2163.0-2980.0 | 13.1 | 0.224 | 0.002 | - | - | - | 0 |
| BG (GFF) | 2163.0-2980.0 | 9.0 | 0.177 | - | - | - | - | 0 |
| TRIP GAS (Reserval) | - | - | - | - | - | - | - | - |
| TRIP GAS (GFF) | - | - | - | - | - | - | - | - |
| CONNECTION GAS | - | - | - | - | - | - | - | - |

| BIT DATA | PRESENT BIT | PREVIOUS BIT |
| --- | --- | --- |
| BIT No. | 5 | 4RR |
| SIZE (in) | 9.875 | 9.875 |
| MANUFACTURER/TYPE | REED / RSX616M-11 | REED / RSX616M-A14 |
| JETS (/32 inch) | 6 x 18 | 6 x 20 |
| DEPTH IN (m) | 1217.0 | 1215.0 |
| DEPTH OUT (m) | - | 1217.0 |
| METRES ON RUN (m) | 1763.0 | 2.0 |
| HRS ON BTM 24hrs/total | 11.4 / 26.9 | 0.0 / 0.4 |
| BIT CONDITION | - | 7-7-BT-A-X-E-WT-BHA |
| RPM RANGE 24hrs | 122-163 | - |
| Pump Hrs 24 hrs / total | 21.8 / 42.4 | 0.0 / 8.0 |
| Krevs 24 hrs / total | 104 / 239 | 0 / 1 |

| 24 HOUR SUMMARY | Drill and survey 9-7/8” production hole from 2163.0 mMDRT to 2455.0 mMDRT as per Anadrill’s instructions. Circulate at reduced rate while unblocking cuttings dryer, as well as clean and clear auger and overboard chute. Drill and survey 9-7/8” production hole from 2455.0 mMDRT to 2921.0 mMDRT as per Anadrill’s instructions. Circulate bottoms up. Drill and survey 9-7/8” production hole from 2921.0 mMDRT to 2980.0 mMDRT as per Anadrill’s instructions. |
| --- | --- |
| 22-08-2009 5 AM UPDATE | Drill and survey 9-7/8” production hole from 2980.0 mMDRT to 3099.0 mMDRT as per Anadrill’s instructions. 5AM DEPTH: 3099.0 mMDRT 2472.9 mTVDRT |