Report for : Greg Doty / Richard Moore

Compiled by : Mark Smith

| WELL | CBA A15B |
| --- | --- |
| DATE | 23-08-2009 |
| REPORT # | 10 |
| MIDNIGHT ACTIVITY | Running 7” casing at 1376.0 mMDRT. |  | ROP DATA (LAST 24 hours) | m/hr | DEPTH (m) |
| MIDNIGHT DEPTH | 3120.0 mMDRT |  | MINIMUM | - | - |
| TVD | 2486.3 mTVDRT |  | MAXIMUM | - | - |
| PROGRESS LAST 24 hrs | 0.0 m |  | AVERAGE | - | - |

| PRELIMINARY FIELD PICKS | ACTUAL TOP (mMDRT) | ACTUAL TOP (mTVDRT) | ACTUAL TOP (mTVDSS) RT to MSL (41.0m) | HIGH/ LOW (mTVD) | PROGNOSED TOP (mMDRT) | PROGNOSED TOP (mTVDRT) |
| --- | --- | --- | --- | --- | --- | --- |
| Top of Lakes Entrance Formation | 2715.0 | 2174.6 | -2133.6 | 3.6m L | 2712.0 | 2171.0 |
| Top of Latrobe Group | 3022.5 | 2411.9 | -2370.9 | 3.9m L | 3018.0 | 2408.0 |
| TCC / M112 | 3024.0 | 2413.0 | -2372.0 | 3.0m L | 3020.0 | 2410.0 |
| M131A | 3028.0 | 2416.1 | -2375.1 | 4.1m L | 3023.0 | 2412.0 |
| M131B | 3031.0 | 2418.4 | -2377.4 | 3.4m L | 3027.0 | 2415.0 |
| M132 Upper | 3034.0 | 2420.8 | -2379.8 | 0.8m L | 3033.0 | 2420.0 |
| M132 Lower | 3038.0 | 2423.8 | -2382.8 | 0.2m H | 3038.0 | 2424.0 |
| M141 | 3048.0 | 2431.6 | -2390.6 | 2.6m L | 3044.0 | 2429.0 |
| OOWC | 3056.4 | 2438.0 | -2397.0 | 0.4m L | 3056.0 | 2438.0 |
| Total Depth | 3120.0 | 2486.3 | -2445.3 | 2.3m L | 3116.0 | 2484.0 |

| Current Formation | Latrobe Group |
| --- | --- |

| GAS DATA | DEPTH (m) | TOTAL GAS (U) | C1 % | C2 % | C3 % | C4 % | C5 % | H2S ppm |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| MAX (Reserval) | - | - | - | - | - | - | - | - |
| MAX (GFF) | - | - | - | - | - | - | - | - |
| BG (Reserval) | - | - | - | - | - | - | - | - |
| BG (GFF) | - | - | - | - | - | - | - | - |
| TRIP GAS (Reserval) | - | - | - | - | - | - | - | - |
| TRIP GAS (GFF) | - | - | - | - | - | - | - | - |
| CONNECTION GAS | - | - | - | - | - | - | - | - |

| BIT DATA | PRESENT BIT | PREVIOUS BIT |
| --- | --- | --- |
| BIT No. |  | 5 |
| SIZE (in) |  | 9.875 |
| MANUFACTURER/TYPE |  | REED / RSX616M-11 |
| JETS (/32 inch) |  | 6 x 18 |
| DEPTH IN (m) |  | 1217.0 |
| DEPTH OUT (m) |  | 3120.0 |
| METRES ON RUN (m) |  | 1903.0 |
| HRS ON BTM 24hrs/total |  | 30.7 |
| BIT CONDITION |  | 1-2-CT-N-X-IN-WT-TD |
| RPM RANGE 24hrs |  | - |
| Pump Hrs 24 hrs / total |  | 2.5 / 60.7 |
| Krevs 24 hrs / total |  | 272 |

| 24 HOUR SUMMARY | Back ream out of hole from 907.0 mMDRT to 695.0 mMDRT. Pump out of hole from 695.0 mMDRT to inside shoe at 655.0 mMDRT. Circulate and work string until shakers clean. Flow check and pump 15 bbl slug. Pull out of hole from 655.0 mMDRT to 39.0 mMDRT. Down load radioactive source and lay out RSS drilling assembly. Run in hole and remove wear bushing. Make up jetting assembly and jet BOP / well head. Clear and clean rig floor. Rig up Weatherford 7" casing gear. Make up 5.0 m pup o casing hanger and lay out. Make up shoe track to 39.0 mMDRT and run in hole with 7" casing from 39.0 mMDRT to 650.0 mMDRT. Make up pump in assembly and stage up pumps to 6 bbl/min for 1 full circulation. Continue to run in hole with 7" casing from 650.0 mMDRT to 1376.0 mMDRT. (Remove and arrange main deck plates over F35. Install Cameron 26" adaptor riser). |
| --- | --- |
| 24-08-2009 5 AM UPDATE | Continue to run in hole with 7" casing from 1376.0 mMDRT to 2480.0 mMDRT. 5AM DEPTH: 3120.0 mMDRT 2486.3 mTVDRT |