Report for : Richard Moore / Greg Doty / Sam Falkner

Compiled by : Mark Smith

| WELL | CBA A19A |
| --- | --- |
| DATE | 27-04-2009 |
| REPORT # | 14 |
| MIDNIGHT ACTIVITY | Drilling 8½" hole at 2958.0 mMDRT. |  | ROP DATA (LAST 24 hours) | m/hr | DEPTH (m) |
| MIDNIGHT DEPTH | 2958.0 mMDRT |  | MINIMUM | 22.2 | 2904.0 |
| TVD | 2305.2 mTVDRT |  | MAXIMUM | 94.7 | 2860.0 |
| PROGRESS LAST 24 hrs | 790.0 |  | AVERAGE | 61.2 | 21680 - 2958.0 |

| PRELIMINARY FIELD PICKS | ACTUAL TOP (mMDRT) | ACTUAL TOP (mTVDRT) | ACTUAL TOP (mTVDSS) RT to MSL (41.0m) | HIGH/ LOW (mTVD) | PROGNOSED TOP (mMDRT) | PROGNOSED TOP (mTVDRT) |
| --- | --- | --- | --- | --- | --- | --- |
| Top Lakes Entrance |  |  |  |  | 2829.0 | 2206.0 |
| Top of Latrobe Group |  |  |  |  | 3049.0 | 2365.6 |
| Top Coarse Clastics / M111 reservoir |  |  |  |  | 3053.7 | 2370.1 |
| Top M112 reservoir |  |  |  |  | 3063.1 | 2375.4 |
| Top M131 Upper reservoir |  |  |  |  | 3071.4 | 2381.1 |
| Top M132 Upper reservoir |  |  |  |  | 3094.4 | 2396.9 |
| Top M132 Lower reservoir |  |  |  |  | 3105.2 | 2404.2 |
| 3.5FS |  |  |  |  | 3105.2 | 2405.2 |
| M141 reservoir |  |  |  |  | 3111.3 | 2408.5 |
| Halibut Original Oil Water Contact |  |  |  |  | 3154.2 | 2438.0 |
| Total Depth |  |  |  |  | 3194.2 | 2465.2 |

| Current Formation | Lakes Entrance Formation |
| --- | --- |

| GAS DATA | DEPTH (m) | TOTAL GAS (U) | C1 % | C2 % | C3 % | C4 % | C5 % | H2S ppm |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| MAX (Reserval) | 2537.0 | 28.0 | 0.484 | 0.004 | 0.002 | 0.001 | - | - |
| MAX (GFF) | 2484.0 | 21.0 | 0.418 | 0.002 | - | - | - | - |
| BG (Reserval) | 2168.0-2958.0 | 17.3 | 0.305 | 0.003 | 0.001 | - | - | - |
| BG (GFF) | 2168.0-2958.0 | 14.0 | 0.272 | 0.001 | - | - | - | - |
| TRIP GAS (Reserval) | - | - | - | - | - | - | - | - |
| TRIP GAS (GFF) | - | - | - | - | - | - | - | - |
| CONNECTION GAS | - | - | - | - | - | - | - | - |

| BIT DATA | PRESENT BIT | PREVIOUS BIT |
| --- | --- | --- |
| BIT No. | 4RR | 3 |
| SIZE (in) | 8½ | 8½ |
| MANUFACTURER/TYPE | REED HYCALOG RSX616M | REED HP21G |
| JETS (/32 inch) | 6 x 18 | 3 x 18 |
| DEPTH IN (m) | 732.0 | 615.0 |
| DEPTH OUT (m) |  | 732.0 |
| METRES ON RUN (m) |  | 117.0 |
| HRS ON BTM 24hrs/total | 12.9 / 47.5 | 11.1 |
| BIT CONDITION |  | 1-1-WT-A-E-E-E-In-No-BHA |
| RPM RANGE 24hrs | 160 |  |
| Pump Hrs 24 hrs / total | 21.5 / 73.2 | 22.0 |
| Krevs 24 hrs / total | 252 / 848 | 208 |

| 24 HOUR SUMMARY | Continue to circulate and condition mud from 2168.0 mMDRT to 2139.0 mMDRT due to high winds over 60 knots. Unable to safely make connection. Conduct rig service and secure loom rings where possible. Drill 8½” hole from 2168.0 mMDRT to 2900.0 mMDRT. Circulate hole clean to reduce ECD prior to drilling into Latrobe Group. Drill 8½” hole from 2900.0 mMDRT to 2958.0 mMDRT. |
| --- | --- |
| 28-04-2009 5AM UPDATE | Drill 8½” hole from 2958.0 mMDRT to 3050.0 mMDRT. 5AM DEPTH: 3050.0 mMDRT (2369.5 mTVDRT) |