Report for : Richard Moore / Mark Calicutt / Andy Choy

Compiled by  : Col Chadwick

| WELL | CBA-A21A |
| --- | --- |
| DATE | 22-03-2009 |
| REPORT # | 08 |
| MIDNIGHT ACTIVITY | POOH for Bit Change @ 2283.0 mMDRT |  | ROP DATA (LAST 24 hours) | m/hr | DEPTH (m) |
| MIDNIGHT DEPTH | 3700.0 mMDRT |  | MINIMUM | 2.28 | 3669.0 |
| TVD | 2356.30 mTVDRT |  | MAXIMUM | 108.01 | 3588.5 |
| PROGRESS LAST 24 hrs | 200.0 m |  | AVERAGE | 31.75 | 3500-3700m |

| PRELIMINARY FIELD PICKS | ACTUAL TOP (mMDRT) | ACTUAL TOP (mTVDRT) | ACTUAL TOP (mTVDSS) RT to MSL (41.0m) | HIGH/ LOW (mTVD) | PROGNOSED TOP (mMDRT) | PROGNOSED TOP (mTVDRT) |
| --- | --- | --- | --- | --- | --- | --- |
| Lakes Entrance Fm. | 3390.0 | 2185.9 | -2144.9 | 12.1 H | 3406.0 | 2198.0 |
| Top of Latrobe Grp | 3665.5 | 2337.7 | -2296.7 | 7.7 L | 3648.0 | 2330.0 |
| Top Coarse Clastics / M111 Reservoir |  |  |  |  | 3656.0 | 2334.0 |
| Top M112 Reservoir |  |  |  |  | 3689.9 | 2351.0 |
| Top M131 Reservoir |  |  |  |  | 3699.9 | 2356.0 |
| Top M132 Upper Reservoir |  |  |  |  | 3733.8 | 2373.0 |
| Top M132 Lower Reservoir |  |  |  |  | 3741.8 | 2377.0 |
| 4AFS Marker |  |  |  |  | 3763.8 | 2388.0 |
| M145 Reservoir |  |  |  |  | 3791.7 | 2402.0 |
| Halibut Org OWC |  |  |  |  | 3863.5 | 2438.0 |
| Total Depth |  |  |  |  | 3903.5 | 2458.0 |

| Current Formation | 60% CLAYSTONE ; 5% SILTSTONE; 35% SANDSTONE |
| --- | --- |

| GAS DATA | DEPTH (m) | TOTAL GAS (U) | C1 % | C2 % | C3 % | C4 % | C5 % | H2S ppm |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| MAX (Reserval) | 3678.5 | 125.00 | 0.827 | 0.316 | 0.249 | 0.162 | 0.050 | - |
| MAX (GFF) | 3679.5 | 76.00 | 0.712 | 0.253 | 0.204 | 0.147 | 0.062 | - |
| BG (Reserval) | 3500.0-3700.5 | 19.92 | 0.195 | 0.037 | 0.028 | 0.019 | 0.006 | - |
| BG (GFF) | 3500.0-3700.5 | 11.32 | 0.097 | 0.025 | 0.027 | 0.027 | 0.007 | - |
| TRIP GAS (Reserval) | - | - | - | - | - | - | - | - |
| TRIP GAS (GFF) | - | - | - | - | - | - | - | - |
| CONNECTION GAS | - | - | - | - | - | - | - | - |

| BIT DATA | PRESENT BIT | PREVIOUS BIT |
| --- | --- | --- |
| BIT No. | 1 | - |
| SIZE (in) | 97/8" | - |
| MANUFACTURER/TYPE | Reed Hycalog RSX616M-A11 | - |
| JETS (/32 inch) | 6 x 18 | - |
| DEPTH IN (m) | 638.0 | - |
| DEPTH OUT (m) | - | - |
| METRES ON RUN (m) | 3062.0 | - |
| HRS ON BTM 24hrs/total | 6.3 / 87.1 | - |
| BIT CONDITION | - | - |
| RPM RANGE 24hrs | 82 -162 | - |
| Pump Hrs 24 hrs / total | 16.8 / 113.8 | - |
| Krevs 24 hrs / total | 55 / 583 | - |

| 24 HOUR SUMMARY | Drill, steer and survey 97/8" hole from 3500.0 mMDRT to 3617.0 mMDRT. Circulate and condition hole clean from 3589.0 mMDRT to 3617.0 mMDRT. Drill, steer and survey 97/8" hole from 3617.0 mMDRT to 3700.5 mMDRT. High Stand Pipe Pressure observed. Picked up off bottom and pressure remained. Flow check. Back ream out of hole from 3700.0 to 3300.0 mMDRT. Pulled out of hole 15 stands wet on elevators from 3300.0 mMDRT to 2833.0 mMDRT. Pump Slug. Continued to pull out of hole on elevators to 2283.0 mMDRT. |
| --- | --- |
| 23-03-2009 5AM UPDATE | Continued to pull out of hole on elevators to 2241.0 mMDRT. Encountered tight spot at 2241.0 mMDRT and 2213.0 mMDRT. Work through. Pull out of hole on elevators from 2113.0 mMDRT to 1952.0 mMDRT. Run in hole from 1952.0 mMDRT to 2008.0 mMDRT. Pull out of hole from 1952.0 mMDRT to 1942.0 mMDRT. Hole packing off at 1942.0 mMDRT. No rotation. Worked pipe through and rotated at 30 rpm. Pumped out of hole from 1942.0 mMDRT to 1919.0 mMDRT. Pulled out of hole on elevators from 1919.0 mMDRT to 1820.0 mMDRT. 3700.0 mMDRT (2356.30 mTVDRT) 1820.0 mMDRT (1282.3 mMDRT) Bit Depth |