Report for : Andy Choy / Mark Calicut / Dan Daniels

Compiled by : Gareth Munro

| WELL | CBA A28 |
| --- | --- |
| DATE | 15-07-2009 |
| REPORT # | 15 |
| MIDNIGHT ACTIVITY | Pump out of hole. |  | ROP DATA (LAST 24 hours) | m/hr | DEPTH (m) |
| MIDNIGHT DEPTH | 3995.0 mMDRT |  | MINIMUM | 3.11 | 3978.5 |
| TVD | 2495.50mTVDRT |  | MAXIMUM | 53.92 | 3964.5 |
| PROGRESS LAST 24 hrs | 135.0 m |  | AVERAGE | 11.16 |  |

| PRELIMINARY FIELD PICKS | ACTUAL TOP (mMDRT) | ACTUAL TOP (mTVDRT) | ACTUAL TOP (mTVDSS) RT to MSL (41.0m) | HIGH/ LOW (mTVD) | PROGNOSED TOP (mMDRT) | PROGNOSED TOP (mTVDRT) |
| --- | --- | --- | --- | --- | --- | --- |
| Top Lakes Entrance | 3435.0 | 2175.7 | -2134.7 | -27.3 | 3490.0 | -2203 |
| Top of Latrobe Group | 3770.5 | 2346.2 | -2305.2 | -0.8 | 3774.0 | -2347 |
| Top Coarse Clastics | 3772.5 | 2347.2 | -2306.2 | -0.8 | 3776.0 | -2348 |
| Top M112 Reservoir | 3824.0 | 2373.3 | -2332.3 | -6.7 | 3839.0 | -2380 |
| Top M131 Reservoir | 3828.0 | 2375.3 | -2334.3 | -6.7 | 3843.0 | -2382 |
| Top M132 Upper Reservoir | 3857.5 | 2390.2 | -2349.2 | -7.8 | 3875.0 | -2398 |
| Top M132 Lower Reservoir | 3869.0 | 2396.1 | -2355.1 | -6.9 | 3885.0 | -2403 |
| Top M141 Reservoir | 3890.0 | 2406.7 | -2365.7 | -6.3 | 3904.0 | -2413 |
| Top M145 Reservoir | 3922.5 | 2423.2 | -2382.2 | -6.8 | 3938.0 | -2430 |
| Original Oil Water Contact | 3951.9 | 2438.0 | -2397.0 | - | 3954.0 | -2438 |
| Total Depth | 3995.0 | 2459.6 | -2418.6 | -8.4 | 4014.0 | -2468 |

| Current Formation | Latrobe Group |
| --- | --- |

| GAS DATA | DEPTH (m) | TOTAL GAS (U) | C1 % | C2 % | C3 % | C4 % | C5 % | H2S ppm |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| MAX (Reserval) | 3988.0 | 50.0 | 0.427 | 0.096 | 0.028 | 0.011 | 0.004 | 0 |
| MAX (GFF) | 3926.5 | 37.0 | 0.319 | 0.086 | 0.041 | 0.029 | 0.012 | 0 |
| BG (Reserval) | 3900.0-3995.0 | 31.8 | 0.192 | 0.070 | 0.032 | 0.019 | 0.007 | - |
| BG (GFF) | 3900.0-3995.0 | 23.0 | 0.170 | 0.056 | 0.026 | 0.017 | 0.009 | - |
| TRIP GAS (Reserval) | - | - | - | - | - | - | - | - |
| TRIP GAS (GFF) | - | - | - | - | - | - | - | - |
| CONNECTION GAS | - | - | - | - | - | - | - | - |

| BIT DATA | PRESENT BIT | PREVIOUS BIT |
| --- | --- | --- |
| BIT No. | 4 | 3 |
| SIZE (in) | 9.875 | 14.75 |
| MANUFACTURER/TYPE | REED / RSX61M-A14 | REED / Mill Tooth |
| JETS (/32 inch) | 6 x 15 | 3 x 20, 1 x 18 |
| DEPTH IN (m) | 587.0 | 229.0 |
| DEPTH OUT (m) | 3995.0 | 587.0 |
| METRES ON RUN (m) | 3408.0 | 358.0 |
| HRS ON BTM 24hrs/total | 12.1 / 97.7 | - /3.1 |
| BIT CONDITION | - | I-I-WT-A-E-In-No-TD |
| RPM RANGE 24hrs | 88-158 | - |
| Pump Hrs 24 hrs / total | 19.8 / 140.3 | - /10.7 |
| Krevs 24 hrs / total | 65 / 717 | - / 4 |

| 24 HOUR SUMMARY | Drill ahead 9-7/8” hole as per Schlumberger instructions from 3860.0 mMDRT to 3995.0 mMDRT Total depth. Take survey and downlink X-ceed tool to neutral. Back ream out of hole at 15 minutes a stand to 2821.0 mMDRT. Increase rate of back reaming out of hole to 12 minutes a stand until 3792.0 mMDRT. Continue to back ream out of hole at 10 minutes a stand staging back to 5 minutes at 3220.0 MDRT. |
| --- | --- |
| 16-07-2009 5 AM UPDATE | Back ream out of hole at 5 minutes a stand from 3220.0 mMDRT to 2650.0 mMDRT. 5AM DEPTH: 3995.0 mMDRT: 2459.32 mTVDRT |