Report for : Sam Falkner / Mark Calicut / Dan Daniels

Compiled by : Gareth Munro

| WELL | CBA A28 |
| --- | --- |
| DATE | 16-07-2009 |
| REPORT # | 16 |
| MIDNIGHT ACTIVITY | Pump out of hole. |  | ROP DATA (LAST 24 hours) | m/hr | DEPTH (m) |
| MIDNIGHT DEPTH | 3995.0 mMDRT |  | MINIMUM | - | - |
| TVD | 2495.50mTVDRT |  | MAXIMUM | - | - |
| PROGRESS LAST 24 hrs | 135.0 m |  | AVERAGE | - |  |

| PRELIMINARY FIELD PICKS | ACTUAL TOP (mMDRT) | ACTUAL TOP (mTVDRT) | ACTUAL TOP (mTVDSS) RT to MSL (41.0m) | HIGH/ LOW (mTVD) | PROGNOSED TOP (mMDRT) | PROGNOSED TOP (mTVDRT) |
| --- | --- | --- | --- | --- | --- | --- |
| Top Lakes Entrance | 3435.0 | 2175.7 | -2134.7 | -27.3 | 3490.0 | -2203 |
| Top of Latrobe Group | 3770.5 | 2346.2 | -2305.2 | -0.8 | 3774.0 | -2347 |
| Top Coarse Clastics | 3772.5 | 2347.2 | -2306.2 | -0.8 | 3776.0 | -2348 |
| Top M112 Reservoir | 3824.0 | 2373.3 | -2332.3 | -6.7 | 3839.0 | -2380 |
| Top M131 Reservoir | 3828.0 | 2375.3 | -2334.3 | -6.7 | 3843.0 | -2382 |
| Top M132 Upper Reservoir | 3857.5 | 2390.2 | -2349.2 | -7.8 | 3875.0 | -2398 |
| Top M132 Lower Reservoir | 3869.0 | 2396.1 | -2355.1 | -6.9 | 3885.0 | -2403 |
| Top M141 Reservoir | 3890.0 | 2406.7 | -2365.7 | -6.3 | 3904.0 | -2413 |
| Top M145 Reservoir | 3922.5 | 2423.2 | -2382.2 | -6.8 | 3938.0 | -2430 |
| Original Oil Water Contact | 3951.9 | 2438.0 | -2397.0 | - | 3954.0 | -2438 |
| Total Depth | 3995.0 | 2459.6 | -2418.6 | -8.4 | 4014.0 | -2468 |

| Current Formation | Latrobe Group |
| --- | --- |

| GAS DATA | DEPTH (m) | TOTAL GAS (U) | C1 % | C2 % | C3 % | C4 % | C5 % | H2S ppm |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| MAX (Reserval) | - | - | - | - | - | - | - | - |
| MAX (GFF) | - | - | - | - | - | - | - | - |
| BG (Reserval) | - | - | - | - | - | - | - | - |
| BG (GFF) | - | - | - | - | - | - | - | - |
| TRIP GAS (Reserval) | - | - | - | - | - | - | - | - |
| TRIP GAS (GFF) | - | - | - | - | - | - | - | - |
| CONNECTION GAS | - | - | - | - | - | - | - | - |

| BIT DATA | PRESENT BIT | PREVIOUS BIT |
| --- | --- | --- |
| BIT No. | 4 | 3 |
| SIZE (in) | 9.875 | 14.75 |
| MANUFACTURER/TYPE | REED / RSX61M-A14 | REED / Mill Tooth |
| JETS (/32 inch) | 6 x 15 | 3 x 20, 1 x 18 |
| DEPTH IN (m) | 587.0 | 229.0 |
| DEPTH OUT (m) | 3995.0 | 587.0 |
| METRES ON RUN (m) | 3408.0 | 358.0 |
| HRS ON BTM 24hrs/total | 0 / 97.7 | - /3.1 |
| BIT CONDITION | - | I-I-WT-A-E-In-No-TD |
| RPM RANGE 24hrs | - | - |
| Pump Hrs 24 hrs / total | 13.5 / 153.8 | - /10.7 |
| Krevs 24 hrs / total | 65 / 782 | - / 4 |

| 24 HOUR SUMMARY | Back ream out of hole at 5 minutes a stand from 3220.0 mMDRT to 2120.0 mMDRT. Excessive torque seen at 2120.0 mMDRT, work string as required to clean up hole. Back ream out of hole at 5 minutes a stand from 2120.0 mMDRT to 1574.0 mMDRT. Tight connections encountered, rig up and use HT-100’s as needed. Back ream out of hole at 5 minutes a stand from 1574.0 mMDRT to 1020.0 mMDRT. |
| --- | --- |
| 17-07-2009 5 AM UPDATE | Ream out of hole at 30 minutes a stand whilst Anadrill reacquire continuous inclinations from 1030.0 mMDRT to 960.0 mMDRT. High torque whilst back reaming, ream out at suitable speed due to the torque. Some tight connections encountered, use HT-100’s as required. 5 am bit depth 735.0 mMDRT. 5AM DEPTH: 3995.0 mMDRT: 2449.56 mTVDRT |